## Slide 1
State of the Art and Efficiency for
Hadron Colliders
plus some Advanced Ideas
Frank Zimmermann
EuCARD-2 XBEAM Strategy Workshop,
Valencia, 13 February 2017
Work supported by the European Commission under Capacities 7th Framework Programme project EuCARD-2, grant agreement 312453, and the HORIZON 2020 project EuroCirCol, grant agreement 654305, as well as by the German BMBF

## Slide 2
colliders and discoveries
Standard Model
Particles and forces
powerful instruments for discovery and precision measurement
A. Ballarino
Notes: New slide from Davide.
Showing that conductor development is launched at international level, Russia, Japan, (Korea and Europe in preparation)
Underline importance of that development as main cost driver for the hadron collider machine.

## Slide 3
peak luminosity > 1.4 x 1034 cm-2s-1
OVER 25 fb-1 in both ATLAS and CMS
2016 LHC : production year
≈153 days physics ≈3738.7 hours
 | Duration [h]
Stable Beams | 1839.5
Fault / Downtime | 980.0
Operations | 857.9
Pre-Cycle | 61.3
TS1 - TS2 : stable beams 58 %
TS2 - TS3 : stable beams 54 %
F. Bordry

## Slide 4
very large circular hadron collider - only feasible approach to reach 100 TeV c.m. collision energy in coming decades
access to new particles (direct production) in few-TeV to 30 TeV mass range, far beyond LHC reach
much-increased rates for phenomena in sub-TeV mass range → much increased precision w.r.t. LHC
energy frontier in the 21st century
hadron collider energy reach
Cf. LHC: factor ~4 in radius, factor ~2 in field  O(10) in Ecms
M. Mangano

## Slide 5
International FCC collaboration (CERN as host lab) to study:
pp-collider (FCC-hh)  main emphasis, defining infrastructure requirements
80-100 km tunnel infrastructure in Geneva area, site specific
e+e- collider (FCC-ee), as a possible first step
p-e (FCC-he) option, integration one IP, FCC-hh & ERL
HE-LHC with FCC-hh technology
~16 T  100 TeV pp in 100 km
Future Circular Collider Study
Goal: CDR for European Strategy Update 2018/19
suggested
in 2010
HE-LHC

## Slide 6
CepC/SppC study (CAS-IHEP) 100 km (new baseline!) , e+e- collisions ~2028; pp collisions ~2042
Qinhuangdao (秦皇岛）
easy access
300 km east
from Beijing
3 h by car
1 h by train
Yifang Wang
CepC, SppC
“Chinese Toscana”
100 km
50 km

## Slide 7
Qinhuangdao site visit July 2016

## Slide 8
near proposed construction site and vinyards – bilingual beach resort (Chinese-Russian)

## Slide 9
… Geneva beach for comparison

## Slide 10
M. Koratzinos, HongKong
alternative CEPC sites

## Slide 11
Constr.
Physics
LEP
Construction
Physics
Proto
Design
LHC – in operation
Construction
Physics
Design
HL-LHC - ongoing project
Physics
Construction
Proto
1980
1985
1990
1995
2000
2005
2010
2015
2020
2025
2030
2035
~20 years
Design
FCC – design study
must advance fast now to be ready for the period 2035 – 2040
milestone: CDR by end 2018 for next update of European Strategy
CERN Circular Colliders & FCC
2040

## Slide 12
hadron collider history
hadron collider peak luminosity as a function of year – for past, operating, and proposed facilities [courtesy W. Fischer]

## Slide 13: FCC-hh peak luminosity with constraints
synchrotron radiation power / beam:
total beam-beam
tune shift
luminosity
limited
with
maximum
acceptable
luminosity formula for SR-power and
tune-shift limited hadron collider
r: bending radius
C: circumference
nb: #bunches/beam
Nb: #p/bunch
E: beam energy
rp: class. proton radius

## Slide 14: FCC-hh peak luminosity with other constraint
event
pile up / Xing
luminosity
maximum
acceptable
luminosity formula for
pile-up limited hadron collider
σtot [mbarn] ≈ 42.1s -0.467-32.19 s-0.540 +35.83 +0.315 ln2(s/34); s in units of GeV2
~112 mbarn at 14 TeV, ~156 mbarn at 100 TeV
σinel [mbarn] ≈ σtot-11.7 +1.59 ln s - 0.134 ln2s
~83 mbarn at 14 TeV, ~110 mbarn at 100 TeV
shorter bunch spacing could help?!
(e.g. 25→ 5 ns would increase nb 5x!)

## Slide 15
parameter | FCC-hh |  |  | HE-LHC | (HL) LHC
collision energy cms [TeV] | 100 |  |  | 25 | 14
dipole field [T] | 16 |  |  | 16 | 8.3
circumference [km] | 100 |  |  | 27 | 27
beam current [A] | 0.5 |  |  | 1.27 | (1.12) 0.58
bunch intensity [1011] | 1 (0.2) | 1 (0.2) |  | 2.5 | (2.2) 1.15
bunch spacing [ns] | 25 (5) | 25 (5) |  | 25 (5) | 25
IP b*x,y [m] | 1.1 | 0.3 |  | 0.25 | (0.15) 0.55
luminosity/IP [1034 cm-2s-1] | 5 | 30 |  | 34 | (5) 1
peak #events/bunch crossing | 170 | 1020 (204) |  | 1070 (214) | (135) 27
stored energy/beam [GJ] | 8.4 |  |  | 1.4 | (0.7) 0.36
synchrotron rad. [W/m/beam] | 30 |  |  | 4.1 | (0.35) 0.18
transv. emit. damping time [h] | 1.1 |  |  | 4.5 | 25.8
initial proton burn off time [h] | 17.0 |  | 3.4 | 2.3 | (15) 40
hadron collider parameters (pp)

## Slide 16
phase 1: b*=1.1 m, xtot=0.01, tta=5 h, 250 fb-1 / year
phase 2: b*=0.3 m, xtot=0.03, tta=4 h, 1000 fb-1 / year
  for both phases:
  beam current 0.5 A, unchanged!
  total synchrotron radiation power ~5 MW.
radiation damping: t~1 h
luminosity evolution over 24 h
PRST-AB 18, 101002 (2015)

## Slide 17
FCC-hh - 100 TeV c.m., 25 ns
burn off slower than emittance
damping → emittance control

## Slide 18
FCC-hh - 100 TeV c.m., 25 ns
in phase 2, b* 1.1→0.3 m,
without (or with less)
emittance control:
tune shift increases during fill
until reaching maximum of 0.03

## Slide 19
Parameter | Unit | SPPC |  |  | FCC |  | 
 |  | PreCDR | “CDR” | “Ultimate” |  |  | 
Circumference | km | 54.4 | 100 | 100 | 100 |  | 
c.m. energy | TeV | 70.6 | 75 | 125-150 | 100 |  | 
dipole field | T | 20 | 12 | 20-24 | 16 |  | 
injection energy | TeV | 2.1 | 2.1 | 4.2 | 3.3 |  | 
#IPs |  | 2 | 2 | 2 | 2 |  | 
luminosity per IP | 1035 cm-2s-1 | 1.2 | 1.0 | - | 0.5 |  | 3.0
IP beta function | m | 0.75 | 0.75 | - | 1.1 |  | 0.3
beam current | A | 1.0 | 0.7 | - | 0.5 |  | 
bunch separation | ns | 25 | 25 | - | 25 (5) | 25 (5) | 
bunch population | 1011 | 2.0 | 1.5 | - | 1.0 (0.2) | 1.0 (0.2 | 
SR power /beam | MW | 2.1 | 1.1 | - | 2.5 |  | 
SR heat load/ap | W/m | 45 | 13 | - | 30 |  | 
SPPC main parameters
J. Tang

## Slide 20
integrated luminosity per year vs maximum pile-up, assuming 160 days of physics run, a machine availability A of 71%, two primary collision points (nIP=2), nb=10600 bunches per beam, and a maximum beam intensity of Nb,0=1015 protons; curves for different av. turnaround times tta
limits on integrated luminosity
F.Z. et al,
IPAC’16
turnaround challenge
asymptotic limit:
Ttot: total time
allocated for physics
/ year
case for
availability

## Slide 21
2 main IPs in A, G for both machines
asymmetric IR optic/geometry for ee to limit synchrotron radiation to detector
common layouts for hh & ee
11.9 m
30 mrad
9.4 m
FCC-hh/
ee Booster
Common
RF (tt)
Common
RF (tt)
IP
IP
0.6 m
Max. separation of 3(4) rings is about 12 m:
wider tunnel or two tunnels are necessary around the IPs, for ±1.2 km.
Lepton beams must cross over through the common RF to enter the IP from inside.
Only a half of each ring is filled with bunches.
FCC-ee 1, FCC-ee 2,
FCC-ee booster (FCC-hh footprint)
FCC-hh
layout
K. Oide
Notes: Check with Katsunobu to have latest layout.
Check with detector people if 9 m offset is acceptable for ee detector

## Slide 22
FCC and CEPC convergence
FCC-ee design, K. Oide, 2015
CEPC design, J. Gao, 2017
Notes: Check with Katsunobu to have latest layout.
Check with detector people if 9 m offset is acceptable for ee detector

## Slide 23
intercepting synchrotron radiation:
- beam screen
photon distribution
FCC-hh beam screen prototypes
ready for Testing 2017 in ANKA within EuroCirCol study
high synchrotron radiation load of proton beams @ 50 TeV:
~30 W/m/beam (@16 T) (LHC <0.2W/m)
5 MW total in arcs (@1.9 K!)
new beam screen with ante-chamber
absorption of synchrotron radiation at 50 K to reduce cryogenic power
factor 50! reduction of cryo power
simulation of
quench behaviour

## Slide 24
50 K chosen for efficiency and beam stability;
but for 4.5 K magnets can also consider 110 K
100 MW
200 MW
300 MW
Ph. Lebrun
L. Tavian
V. Baglin
based on LHC screen
synchrotron radiation – cryopower & beam-screen temperature
D. Schulte
total
cryo
power

## Slide 25
main SC magnet system
FCC (16 T) vs LHC (8.3 T)
FCC
bore diameter: 50 mm
dipoles:
quads:
LHC
bore diameter: 56 mm
dipoles:
quads:

## Slide 26
Nb3Sn conductor program
Nb3Sn is one of the major cost & performance factors for FCC-hh and is given highest attention
main development goals until 2020:
Jc increase (16T, 4.2K) > 1500 A/mm2 i.e. 50% increase wrt HL-LHC wire
reference wire diameter 1 mm
potentials for large scale production and cost reduction
3150 mm2
~1.7 times less SC
~10% margin
HL-LHC
~10% margin
FCC ultimate
5400 mm2
D. Tommasini et al.
Notes: New slide from Davide.
Showing that conductor development is launched at international level, Russia, Japan, (Korea and Europe in preparation)
Underline importance of that development as main cost driver for the hadron collider machine.

## Slide 27
16 T dipole options and plans
Cos-theta
Blocks
Common coils
down-selection of options end 2017 for detailed design work
model production 2018 – 2022
prototype production 2023 - 2025
Swiss contribution
via PSI
Canted
Cos-theta
Notes: New slide from Davide.
Showing that conductor development is launched at international level, Russia, Japan, (Korea and Europe in preparation)
Underline importance of that development as main cost driver for the hadron collider machine.

## Slide 28
US Magnet Development Program
Under Goal 1:
16 T cos theta dipole design
16 T canted cos theta (CCT) design
S. Gourlay

## Slide 29
1250 min.
115
Φ 1180
Φ 1300
Φ 1180
Φ 1300
115
HE-LHC integration & transport
FCC-hh tunnel diameter: 6.0 m
LHC tunnel diameter: 3.8 m
cryostat outer diameter: 1.18-1.3 m
options:
remove QRL
reduce margin
  for transport
  - automatic
  guiding system?
shrink cryostat
enlarge tunnel?
…
V. Mertens., V.. Parma, D. Schoerling, L. Tavian,
Y. Muttoni, et al.
very preliminary

## Slide 30
S. Prestemon, HongKong

## Slide 31
S. Prestemon, HongKong

## Slide 32
pp/p-pbar in the L-E plane

## Slide 33
Collider | c.m. energy [TeV] | Pel: tot. el. power [MW] | Pb: IP beam power [GW] | luminosity L [nb-1s-1] | Pb/Pel | L/Pel (/IP) [nb-1s-1 / MW]
LHC | 13.0 | ~150 | 8000 | 10 | 50000 | 0.07
HE-LHC | 25.0 | ~250 (guess) | 32000 | 340 | 128000 | 1.4
FCC-hh | 100.0 | 500 (target) | 50000 | 300 (phase 2) | 100000 | 0.6
SPPC | 75 | 600 (guess) | 53000 | 100 | 90000 | 0.2
hadron-collider beam power

## Slide 34
20
Companies
30
Countries
98
Institutes
collaboration & industry relations

## Slide 36
beyond FCC
muon colliders?
gg colliders? (low energy or high energy – CLICHÉ/SAPPHiRE)
crystal accelerators?
gravitational waves
detection and/or generation
others (piggyback, single particles, black holes)
beyond FCC

## Slide 37
 | LCLS-2 | XFEL weak focusing | XFEL strong focusing
# photons per pulse | 2.1012 | 2.1012 | 2.1012
FEL pulse energy (mJ) | 3.2 | 3.2 | 3.2
repetition rate | 1 MHz | 30 kHz | 30 kHz
spot size at collision (mm) | 1. | 1. | 0.2
Luminosity (cm-2s-1) | 3.2.1037 | 9.6.1035 | 2.4.1037
photon-photon scattering events per second | 3.2.10-4 | 9.6.10-6 | 2.4.10-4
photon-photon scattering events per hour | 1.2 | 0.034 (0.83 per day) | 0.86
Measurements of photon-photon scattering at LCLS-2 and at XFEL:
Energy hn =10 keV or c.m. energy 20 keV. Total Cross Section 1.0 ab.
2 FEL beam pulses colliding head-on against each other
(at 20 keV g’s, cross section goes to 64 ab , scaling like hn6)
L. Serafini, F3iA 2016
Photon-photon scattering probes the structure of the QFT vacuum.
low-energy gg colliders

## Slide 38
W. Krasny, PBC
“Gamma factory” initiative

## Slide 39
W. Krasny, PBC

## Slide 40
W. Krasny, PBC

## Slide 41
W. Krasny, PBC

## Slide 42
W. Krasny, PBC

## Slide 43
single particle accelerators
- wave function propagating through lattice
  use emerging ultra-cold and precision alignment technology (e.g. LIGO)
  cleaner, more customised physics output in detector, better luminosity (per particle) – perhaps get rid of beamstrahlung?
creating a big black hole (106xEplanck in 106xLplanck)?
cheating with entanglement?
“beams may be holding us back”
S. Brooks, F3iA 2016

## Slide 44
2 * 2.5e14 * 6500 GeV
= 521 MJ
= 0.266 EPlanck
total energy is OK but it’s in too many particles
@JoshMcFayden (UCL/ATLAS) via Twitter
“the case for optimism”
S. Brooks, F3iA 2016

## Slide 45
Tokyo/Ueno – similar to Fallas
… but where/who is the European guy?