## Slide 1: Space charge and electron cloud in the CERN accelerators
G. Rumolo
With the input of H. Bartosik, G. Iadarola, K. Li, L. Mether, A. Romano, M. Schenk
EuCARD-2 XBEAM Strategy Workshop, Valencia, Spain, 13/02/2017

## Slide 2: Beam brightness limitation due to direct space charge
Tune spread is proportional to beam brightness
z
y
x
Particles oscillating close to the bunch peak density

## Slide 3: Beam brightness limitation due to direct space charge
Tune spread is proportional to beam brightness
We need to stay clear of resonances, else
  Blow-up (e.g. from integer)
  Beam losses
  Emittance increases with intensity
LHC injectors
  Suffer space charge mainly at low energy
  Long injection plateau for multiple injections  very challenging for beam degradation
  Tune areas to be carefully determined to allow reaching the required performance
  Future beam requirements pose a big challenge!
  Space charge can remain a limitation even at higher energy due to increasing circumference and short bunch length (high peak currents)

## Slide 4: Space charge activities at CERN
Space charge important subject at CERN in view of the upgrade of the accelerators of the LHC injectors chain (LIU project)
Experimental observations and studies
  Space charge effects in the injector chain (PSB, LEIR, PS, SPS)
    Study of beam loss and emittance growth on long injection plateaus (working point dependence, resonance characterisation)
    Dedicated experiments with purposely excited nonlinearities
    Assessment of brightness limitations in the different machines
  Mitigation techniques, e.g. hollow bunches, second harmonic, resonance compensation, enhanced dispersion
Numerical simulations
  Several codes presently used (PTC-ORBIT/PyORBIT, MAD-X space charge, PyHEADTAIL) or collaborations (e.g. with G. Franchetti – MICROMAP)
  Interest in assessing both incoherent effects over long times and effect of space charge on coherent effects

## Slide 6: The PSB
From Linac2
Ekin =50 MeV
To PS
Ekin =1.4 GeV
C = 157 m

## Slide 7: The PSB
Injection@275
Extraction@805
b
Space charge eased at low energy thanks to the double harmonic and flattened bunch profile
No plateau at injection energy alleviates space charge effects due to rapid acceleration
PSB acceleration cycle

## Slide 8: The PSB
Injection@275
Extraction@805
b
Tune spreads about 3-5x lower (from bg2, bunch length and longitudinal distribution)
Six of these bunches are then sent to the PS over two successive injections (4 + 2)
PSB acceleration cycle

## Slide 9: The PSB
Dynamic working point
Multipoles are used to compensate for resonances and limit losses along the cycle
Injection at 160 MeV from Linac4 will preserve the tune spreads for double intensity (bg2 will be half)
Injection
Extraction

## Slide 10: The PS
From PSB
Ekin =1.4 GeV
To SPS
p0 =26 GeV/c
C = 628 m

## Slide 11: The PS
PS acceleration cycle (LHC beams)
First train of four bunches from the PSB sits for 1.2 s waiting for the second train
After second injection, there is the triple splitting and acceleration (mitigated space charge)

## Slide 12: The PS
PS acceleration cycle (LHC beams)
Acceleration, diluted longitudinal emittances strongly reduce space charge along the cycle
Before extraction there is a fast bunch rotation to fit the bunches into the 5 ns buckets of the SPS

## Slide 13: The PS
Nominal tune in “resonance free” region
Tune spread necktie from space charge extends by ~0.30 in the vertical plane for LHC beams
Spread fits tightly between integer resonance and 6.25 structure resonance

## Slide 14: The PS
Measurements of losses and emittance growth for different tune spreads reveal the effects of resonance crossing
To guarantee 5% loss and emittance growth we are limited to 0.31 tune spread with a ‘high’ working point
Assuming 0.31 as a brightness limit for the PS, the increase of the injection energy to 2 GeV and the transfer of larger longitudinal emittance bunches will provide the margin to double the intensity injected into the PS

## Slide 15: The SPS
From PS
Ekin =25 GeV
C = 6911 m

## Slide 16: The SPS
Different types of beams produced by the PS (50 and 25 ns, trad, BCMS)
Quoted values are for the ‘worst’ beams now, i.e. 50 ns or future (LIU) 25 ns beams
First trains of 36 (24) or 72 (48) bunches from the PS sit for several seconds at injection energy

## Slide 17: The SPS

## Slide 18: The LEIR
From Linac3
Ekin =4.2 MeV/u
To PS
Ekin =72 MeV/u
C = 78 m

## Slide 19: The LEIR cycle
Multi-turn injections:
6D painting with typical efficiency of 50-70%
Electron cooling:
Coasting beam
Regime of beam loss
Einj = 4.2 MeV/n
Eext = 72 MeV/n
RF capture: h=2 and double harmonic
Longitudinal Schottky spectrum: cooling, dragging and stacking

## Slide 20: The LEIR

## Slide 21: The LEIR
Iso-adiabatic capture in single/double RF with and without longitudinal blow-up
  Clear dependence of losses on line charge density

## Slide 22: Space charge mitigation techniques
Increase of injection energy
Reduction of peak line density (flat profile)
  Maximize bunch length
  Flat bunches with longitudinal hollow distribution generated by parametric resonance in single harmonic
  Off-energy RF capture of coasting beam in double RF
Overcome low energy brightness limitation by longitudinal bunch merging at intermediate energy plateau
Optimization of working point and compensation of betatron resonance to reduce losses and blow-up
Compensation of space charge forces
  Studies of using e-lenses (e.g. proof-of-principle experimental studies at GSI)
  Use of RFQ?
Optics optimization (e.g. large horizontal and/or vertical dispersion)

## Slide 23: Electron cloud in one slide
    Secondary Electron Emission can drive an avalanche multiplication effect filling the beam chamber with an electron cloud
    Proton bunch
    e- is emitted (photoelectric effect)
    Secondary Electron Emission
Trailing bunches of the train interact with a dense e-cloud
Transverse instabilities, energy loss
Transverse emittance blow-up
Particle losses
e-cloud induces other unwanted effects like:
Heat load on the beam chambers
Vacuum degradation
Something like this…

## Slide 24: Electron cloud activities at CERN
Electron cloud is a key subject for both the upgrade of the LHC injectors chain (PS and SPS) within LIU, and for the HL-LHC era, due to the limitations observed in LHC
Experimental observations and studies
  Direct electron cloud measurements with dedicated detectors (shielded pick ups, strip monitors)
  Monitoring of other electron cloud observables: vacuum rise, heat load in LHC cold regions, stable phase shift along a bunch train
  Electron cloud effects on the beam  fast beam instabilities, emittance growth, poor lifetime
  Scrubbing runs in SPS and LHC: strategies, beam parameters, machine settings
  Laboratory measurements of scrubbing curves (different surfaces, conditions, etc)
  Mitigation techniques and their assessment in the machines, e.g. coating, LESS, clearing electrodes

## Slide 25: Electron cloud activities at CERN
Numerical simulations
  Development, optimization and massive application of build up code PyECLOUD
    It has required steady development over the years to include all required features (e.g. import measured beam structures, load arbitrary magnetic field configurations, use arbitrary chamber shapes with holes and non-uniform SEY, simulate chambers with two beams, handle limiting cases of tiny beams in large chambers, etc.)
  Development, optimization and massive application of beam dynamics code PyHEADTAIL (interaction between beam and electron cloud)
    To study both coherent and incoherent effects, establish instability thresholds, produce tune footprints
  Integration of build up and beam dynamics simulations into a single tool
    Use PyECLOUD module in PyHEADTAIL for electron tracking
    Use snapshot distributions from PyECLOUD to initialise electrons in PyHEADTAIL
    Eventually run build up and beam dynamics simulations self-consistently to study multi-bunch effects  parallelisation, being tested

## Slide 26: Electron cloud activities at CERN
Experimental studies (BE/ABP, BE/RF, BE/OP, TE/VSC, TE/CRG)
Direct electron cloud measurements
Monitoring of electron cloud observables
Electron cloud effects on the beam
Scrubbing runs in SPS and LHC and strategies
Laboratory measurements of SEY and scrubbing
Coating and mitigation techniques (LESS, clearing electrodes)
Numerical simulations (BE/ABP)
PyECLOUD
PyHEADTAIL
Integration of build up and beam dynamics simulations into a single tool
Interpretation, planning, steering
Modeling, benchmarking, steering

## Slide 27: Electron cloud in the PS
Most of the direct electron cloud measurements in the PS were made in a straight section equipped with shielded pick ups
However, the electron cloud is expected in the main magnet units (combined functions) for 25 ns beams and SEY of the surface above 1.5

## Slide 28: Electron cloud in the PS
Most of the direct electron cloud measurements in the PS were made in a straight section equipped with shielded pick ups
However, the electron cloud is expected in the main magnet units (combined functions) for 25 ns beams

## Slide 29: Electron cloud in the PS
Most of the direct electron cloud measurements in the PS were made in a straight section equipped with shielded pick ups
However, the electron cloud is expected in the main magnet units (combined functions) for 25 ns beams
50
150
250
300
200
100
40 MHz RF Voltage [kV]
Time [ms]
b.l.≈14 ns
11 ns
0
10
20
30
40
50
60
4 ns

## Slide 30: Electron cloud in the SPS
Strong limitation due to e-cloud with 25 ns beams until ~2011
  Instabilities at injection + incoherent effects: high chromaticity needed
  Severe pressure rise around the machine
  Strong emittance growth along bunch trains
  Scrubbing runs since 2002 with long cycles at 26 GeV/c
  Typically limited by heating/outgassing of specific elements
43.2 s
400%
2000 (48 b. - 0.8x1011 p/b @inj.)
3.5 μm

## Slide 31: Electron cloud in the SPS
Strong limitation due to e-cloud with 25 ns beams until ~2011
  Instabilities at injection + incoherent effects: high chromaticity needed
  Severe pressure rise around the machine
  Strong emittance growth along bunch trains
  Scrubbing runs since 2002 with long cycles at 26 GeV/c
  Typically limited by heating/outgassing of specific elements
Several years with systematic scrubbing runs led to a point in which SPS could successfully accelerate four batches of 72 bunches of nominal 25 ns beam (1.2e11 p/b) to 450 GeV/c without significant beam degradation
~1 month before 2005 long shutdown
16 days in 2006 – 2009
2002
(14d)
2003
(8d)
2004
(10d)
2006
(5d)
2007
(7d)
2008
(2.5d)
2012
(5d)
2009
(1.5d)
Shutdown
2010-11
(-)

## Slide 32: The SPS main magnets
Four types of main magnets and their chambers (following beam envelope)
MBA
QF
MBA
MBB
MBB
QD
MBA
MBA
MBB
MBB
QF
MBA
MBA
QF
QD
MBA
MBB
Machine element | Field/Gradient | Length | N. installed | Fraction of the SPS
MBA dipole magnet | 0.12 T at 26 GeV/c 2.1 T at 450 GeV/c | 6.3 m | 360 | 32.8 %
MBB dipole magnet | 0.12 T at 26 GeV/c 2.1 T at 450 GeV/c | 6.3 m | 384 | 35.0 %
QF quadrupole magnet | 14.2 T/m at 450 GeV/c 0.82 T/m at 26 GeV/c | 3.1 m | 108 | 4.8 %
QD quadrupole magnet | 14.2 T/m at 450 GeV/c 0.82 T/m at 26 GeV/c | 3.1 m | 108 | 4.8 %

## Slide 33: SPS MBA-type chambers
1.0 x 1011 ppb
1.5 x 1011 ppb
2.0 x 1011 ppb
2.5 x 1011 ppb
Transverse distribution with two vertical stripes (typical of e-cloud in dipoles)
Multipacting threshold at SEYthr=1.55
Dependence on bunch intensity is quite weak, but in reality increasing the intensity moves stripes to unscrubbed regions and may re-awaken e-cloud

## Slide 34: SPS MBB-type chambers
Transverse distribution with two vertical stripes (typical of e-cloud in dipoles)
Multipacting threshold at SEYthr=1.3
Dependence on bunch intensity is quite weak, but in reality increasing the intensity moves stripes to unscrubbed regions and may re-awaken e-cloud
1.0 x 1011 ppb
1.5 x 1011 ppb
2.0 x 1011 ppb
2.5 x 1011 ppb

## Slide 35: SPS MBB-type chambers
Transverse distribution with two vertical stripes (typical of e-cloud in dipoles)
Multipacting threshold at SEYthr=1.3
Dependence on bunch intensity is quite weak, but in reality increasing the intensity moves stripes to unscrubbed regions and may re-awaken e-cloud
1.0 x 1011 ppb
1.5 x 1011 ppb
2.0 x 1011 ppb
2.5 x 1011 ppb
SPS measurements from e-cloud strip monitors

## Slide 36: SPS QD-type chambers
Trapping of electrons along the field lines
Very low multipacting threshold at SEYthr=1.0-1.1
Dependence on bunch intensity is quite weak
1.0 x 1011 ppb
1.5 x 1011 ppb
2.0 x 1011 ppb
2.5 x 1011 ppb

## Slide 37: SPS QF-type chambers
Trapping of electrons along the field lines
Multipacting threshold at SEYthr=1.2-1.3
“Inverse” dependence on bunch intensity (higher thresholds for higher currents)
1.0 x 1011 ppb
1.5 x 1011 ppb
2.0 x 1011 ppb
2.5 x 1011 ppb

## Slide 38: SPS large drift chambers
Typical build up in field-free region
Multipacting threshold decreasing for larger bunch intensities SEYthr=1.15-1.45

## Slide 39: High intensity LHC beams in the SPS
LHC beams with 2e11 p/b exhibited transverse instability, emittance blow up and poor lifetime when it was first injected into the SPS
Beam quality improved with ~10 days scrubbing and tuning, but losses could not be decreased below 11% over 10 s (length of SPS injection plateau)

## Slide 40: Electron cloud in the LHC: 25 ns beams in 2011-12
2011
2012
6-8/12

## Slide 41: Electron cloud in the LHC: 25 ns beams in 2011-12
6-8/12
Calculation of beam screen SEY (dmax) from heat load measurements

## Slide 42: Electron cloud in the LHC: 25 ns beams in 2011-12
2011
2012
42

## Slide 43: Electron cloud in the LHC during Run II: 2015 scrubbing
50 ns
Scrubbing Run 1: 24/6 – 2/7
Scrubbing Run 2: 25/7 – 8/8
After Long Shutdown 1
  SEY of beam screens reset to pre 25 ns values
  Lots of limitations from instabilities, vacuum on sensitive equipment, cryogenic transients  defined machine settings also for physics ramp (tunes, chromaticities, octupoles, transverse feedback)
  By end of scrubbing run, return to SEY values around 1.4 (beam quality improvement in last part)
  Deconditioning evident, took time to recondition

## Slide 44: Electron cloud in the LHC during Run II: 2015 scrubbing
50 ns
Scrubbing Run 1: 24/6 – 2/7
Scrubbing Run 2: 25/7 – 8/8
After Long Shutdown 1
  SEY of beam screens reset to pre 25 ns values
  Lots of limitations from instabilities (machine settings, speed of progress), vacuum on sensitive equipment, cryogenic transients
  By the end of scrubbing run, return to SEY values around 1.4
  Deconditioning evident, took time to recondition

## Slide 45: Electron cloud in the LHC during Run II: 2015
In 2015, first operation at 6.5 TeV with 25 ns beam
  In spite of long scrubbing campaign with 25 ns beams (~ 2 weeks), heat load induced by electron cloud limited the intensity that could be stored in physics
Slow intensity ramp-up (defined by heat loads on the beam screens)
Reached 2040 bunches in trains of 72b and 2244b in trains of 36b
Conditioning was observed throughout the year, but full e-cloud suppression did not occur

## Slide 46: Electron cloud in the LHC during Run II: 2016
Clear signs of deconditioning w.r.t. end-2015
  Transverse instabilities and emitt. blow-up, larger heat load and stable phase shift
Reconditioning very fast  1 day at 450 GeV sufficient to recondition machine up to ~1800 bunches/beam with injections 216b at injection energy
Generally less problems than in 2015 thanks to:
  Scrubbing accumulated in 2015
  Improved cryogenics feed-forward (heat load transients)
  Settings optimized for e-cloud (Q, Q’, octupoles, feedback)  better beam quality
25 April 2016

## Slide 47: Electron cloud in the LHC during Run II: 2016
Conditioning experienced in 2015 continued over the first two months of 2016
Very little change in the following months
No correlation of this evolution with changes of settings and beam configuration
2015
2016
2x48b
2x72b
72b
Train
type
4x36b
72b

## Slide 48: Electron cloud in the LHC during Run II: 2016
Conditioning experienced in 2015 continued over the first two months of 2016
Very little change in the following months
No correlation of this evolution with changes of settings and beam configuration
2015
2016
2x48b
2x72b
72b
Train
type
4x36b
72b
2015
2016

## Slide 49: Electron cloud in the LHC: General
At the LHC beam induced surface conditioning (scrubbing) was sufficient to mitigate e-cloud but full suppression was not achieved
  Need high feedback gain, chromaticity and octupole settings to keep the beam stable
The tunes at injection had to be modified to accommodate large footprint
A feedforward system had to be implemented to adapt the cryogenics setting to the heat load generated by the e-cloud (large fraction of the available capacity)
2244b.
Average
Imp.+syn.rad
Octupole knob at -1.5
Q’=15/20, 5 x 1011 e/m3
(.28, .31)
(.27, .295)
Avg. half-cell

## Slide 50: Electron cloud in the LHC: Some open questions
Difference between sectors
  Important info from thermal cycle in Sector 12 for dipole replacement
  Magnets around the exchanged dipole are being instrumented for detailed heat load measurements
Detailed arc half-cell heat load breakdown (dipoles, quadrupoles, drifts)
  Important information from new instrumented cell in S12
  Improvement of the simulation model (including synchrotron radiation tracking and photoelectron generation - synergy with FCC studies)
  Improvement of heat load data calibration
  Tests with 50 ns or 8b4e for heat load measurement calibration
Understanding on surface behavior
  Laboratory surface characterization: vital input to improve simulations
    Effect of electron energy on secondary emission and scrubbing
    Effect of surface temperature - further tests also in the machine?
  Beam configurations to improve scrubbing
    Longer 25 ns trains
    Slightly higher bunch intensity
    5 ns spaced doublet beams

## Slide 51: Electron cloud mitigation
Scrubbing (but up to which point??...)
Coating of the beam pipes with amorphous carbon (a-C) has been developed at CERN to suppress e-cloud formation (a-C has very low Secondary Electron Yield)
  Validated for full scale deployment in a large accelerator (room temperature)
  In 2019-20 a large fraction of SPS will be coated with a-C
  Studies at an advanced stage to use a-C coating also in cold magnets:
    e-cloud suppression validated at the COLDEX experiment
    Developing methods to deploy the coating “in situ”, i.e. directly in the magnets installed in the LHC tunnel (inner triplets in IP2 and IP8)
Low Secondary Electron Yield can be obtained also using Laser Engineered Surface Structures (LESS)
  Developed by in universities and laboratories in the UK
  Being tested inside a particle accelerator at CERN SPS (strip monitor at room temperature, COLDEX cryogenic experiment)
Clearing electrodes, solenoids …
High bandwidth feedback system

## Slide 52: Summary
Space charge and electron cloud are two key subjects for the future upgrades of all CERN machines
Space charge
  Limits brightness in injectors mainly due to long injection plateaus
  Effect on coherent instability thresholds not yet clear
Electron cloud
  Affects PS, but only in the last phase of LHC beam production
  Affects SPS, which is scrubbed for present LHC beams and will be partly coated with a-C for future beams
  Affects LHC potentially limiting its performance mainly due to the heat load on the cryogenic system
Notes:   Injection speed, downtime

## Slide 53: LHC beams in the PS
1st injection
2nd injection
Flat top
Bunch shortening
25ns bunch spacing
Bunch splittings
x 3
x 4
0
10
20
30
40
50
60
50
150
250
300
200
100
40 MHz RF Voltage [kV]
Time [ms]
Double splitting
Adiabatic shortening
Bunch rotation
b.l.≈14 ns
11 ns
4 ns
E-cloud expected and observed

## Slide 54: LHC beams in the PS
1st injection
2nd injection
Flat top
Bunch shortening
330ns
25ns bunch spacing
Bunch splittings
x 3
x 4
Before last bunch splitting
e-cloud neither expected nor observed

## Slide 55: Electron cloud in the PS
Most of the direct electron cloud measurements in the PS were made in a straight section equipped with shielded pick ups
However, the electron cloud is expected in the main magnet units (combined functions) for 25 ns beams
This electron cloud can be source of instabilities  Studied by storing for about 100 ms a 25 ns beam with b.len.≈10 ns
H pickup signal – 357 kHz component
50
150
250
300
200
100
40 MHz RF Voltage [kV]
Time [ms]
b.l.≈14 ns
b.l.≈ 10 ns
0
10
20
30
40
50
60
70
80
90
100

## Slide 56: Electron cloud in the PS
Most of the direct electron cloud measurements in the PS were made in a straight section equipped with shielded pick ups
However, the electron cloud is expected in the main magnet units (combined functions) for 25 ns beams
This electron cloud can be source of instabilities  Studied by storing for about 100 ms a 25 ns beam with b.len.≈10 ns
Instability onset can be efficiently delayed by means of transverse feedback system, which provides margin for future operation
10 ms

## Slide 57: Electron cloud in the PS
Most of the direct electron cloud measurements in the PS were made in a straight section equipped with shielded pick ups
However, the electron cloud is expected in the main magnet units (combined functions) for 25 ns beams
This electron cloud can be source of instabilities  Studied by storing for about 100 ms a 25 ns beam with b.len.≈10 ns

## Slide 58: Electron cloud in the PS
Most of the direct electron cloud measurements in the PS were made in a straight section equipped with shielded pick ups
However, the electron cloud is expected in the main magnet units (combined functions) for 25 ns beams
This electron cloud can be source of instabilities  Studied by storing for about 100 ms a 25 ns beam with b.len.≈10 ns

## Slide 59: Electron cloud in the PS
Most of the direct electron cloud measurements in the PS were made in a straight section equipped with shielded pick ups
However, the electron cloud is expected in the main magnet units (combined functions) for 25 ns beams
This electron cloud can be source of instabilities  Studied by storing for about 100 ms a 25 ns beam with b.len.≈10 ns

## Slide 60: Electron cloud in the PS
Most of the direct electron cloud measurements in the PS were made in a straight section equipped with shielded pick ups
However, the electron cloud is expected in the main magnet units (combined functions) for 25 ns beams
This electron cloud can be source of instabilities  Studied by storing for about 100 ms a 25 ns beam with b.len.≈10 ns

## Slide 61: Electron cloud in the PS
Most of the direct electron cloud measurements in the PS were made in a straight section equipped with shielded pick ups
However, the electron cloud is expected in the main magnet units (combined functions) for 25 ns beams
This electron cloud can be source of instabilities  Studied by storing for about 100 ms a 25 ns beam with b.len.≈10 ns

## Slide 62: Electron cloud in the PS
Most of the direct electron cloud measurements in the PS were made in a straight section equipped with shielded pick ups
However, the electron cloud is expected in the main magnet units (combined functions) for 25 ns beams
This electron cloud can be source of instabilities  Studied by storing for about 100 ms a 25 ns beam with b.len.≈10 ns

## Slide 63: Electron cloud in the PS
Most of the direct electron cloud measurements in the PS were made in a straight section equipped with shielded pick ups
However, the electron cloud is expected in the main magnet units (combined functions) for 25 ns beams
This electron cloud can be source of instabilities  Studied by storing for about 100 ms a 25 ns beam with b.len.≈10 ns

## Slide 64: Electron cloud in the PS
Most of the direct electron cloud measurements in the PS were made in a straight section equipped with shielded pick ups
However, the electron cloud is expected in the main magnet units (combined functions) for 25 ns beams
This electron cloud can be source of instabilities  Studied by storing for about 100 ms a 25 ns beam with b.len.≈10 ns

## Slide 65: Electron cloud in the PS
Most of the direct electron cloud measurements in the PS were made in a straight section equipped with shielded pick ups
However, the electron cloud is expected in the main magnet units (combined functions) for 25 ns beams
This electron cloud can be source of instabilities  Studied by storing for about 100 ms a 25 ns beam with b.len.≈10 ns

## Slide 66: LHC beams in the SPS
1st injection
2nd injection
25ns bunch spacing
3rd injection
4th injection
Flat top
Extraction
2ms
8ms (out of 23ms SPS circumference)

## Slide 67: The SPS main magnets
Four types of main magnets and their chambers (following beam envelope)
MBA
QF
MBA
MBB
MBB
QD
MBA
MBA
MBB
MBB
QF
MBA
MBA
QF
QD
MBA
MBB

## Slide 68: Electron cloud in the LHC during Run II: scrub with physics
2015
High b*
72 bpi
144 bpi
72g72
72g72
(4x36) bpi
1.25 ns
1.3 ns
1.35 ns
1.35 ns
Filling pattern
Target b. length
100 ns

## Slide 69: Electron cloud in the LHC during Run II: scrub with physics
2015
Average
14 September – Average arc half cells
4 November – Average arc half cells
Impedance+synch. rad

## Slide 70: Electron cloud in the LHC during Run II: deconditioning and reconditioning cycles
2015
Scrub.
MD2
TS2
High b*
TS3
MD3

## Slide 71: Electron cloud in the LHC during Run II: deconditioning and reconditioning cycles
2015
Scrub.
MD2
TS2
High b*
TS3
MD3

## Slide 72: Electron cloud in the LHC during Run II: deconditioning and reconditioning cycles
2015
Scrub.
MD2
TS2
High b*
TS3
MD3
Scrubbing checks at 450 GeV
deconditioning
decondit.
3h scrub.
3h scrub.
3h scrub.

## Slide 73: Electron cloud in the LHC during Run II: deconditioning and reconditioning cycles
2015
Scrub.
MD2
TS2
High b*
TS3
MD3
Scrubbing checks at 450 GeV
deconditioning
decondit.
3h scrub.
3h scrub.
3h scrub.
From vacuum gauges
Thanks to G. Bregliozzi, P. Chiggiato, C. Yin Vallgren

## Slide 74: Electron cloud in the LHC during Run II: deconditioning and reconditioning cycles
2015
Scrub.
MD2
TS2
High b*
TS3
MD3
Scrubbing checks at 450 GeV
deconditioning
decondit.
3h scrub.
3h scrub.
3h scrub.
From vacuum gauges
Thanks to G. Bregliozzi, P. Chiggiato, C. Yin Vallgren
Scrubbing reasonably well preserved during Technical Stops and Machine Development with low intensity/low energy beams
Deconditioning mainly driven when running with low e-cloud/high synchrotron radiation schemes, however recovery can be achieved rather quickly
  Maybe it is the effect of synchrotron radiation cleaning other parts of the beam chamber, but ‘polluting’ the previously cleaned ones?