## Slide 1: A scalable online monitoring system based on Elasticsearch for distributed data acquisition in CMS
Presenter: Dainius Šimelevičius on behalf of CMS DAQ group
Primary authors: Luciano Orsini - CERN, Dainius Šimelevičius - CERN/Vilnius University
CHEP 2018
23rd International Conference on Computing in High Energy and Nuclear Physics
9-13 July 2018, Sofia, Bulgaria

## Slide 2: Outlook
CMS Data Acquisition System
Motivation
About Elasticsearch technology
Elasticsearch-based monitoring system
Conclusion

## Slide 3: CMS Data Acquisition System

## Slide 4: CMS DAQ
CMS DAQ
Detector Front-End
L1 Trigger
High-Level
Trigger
*
Andre, J-M et al. “A Scalable Monitoring for the CMS Filter Farm Based on Elasticsearch.”
Journal of Physics: Conference Series 664, no. 8 (December 2015): 082036.
*

## Slide 5: Monitoring of CMS DAQ
Monitoring of DAQ is a data acquisition on its own which runs in parallel with event data flow and shares hardware and software resources with the DAQ system
It is used to collect, present and store monitoring data in order to detect deviation from a normal DAQ behavior
Users of the monitoring are shifters, DAQ experts on-call, expert system, etc.
Data space is f(sources, variables) ≈ 200,000 updated every 1-5 seconds
Data items are time-stamped collections of fields, namely, flashlists

## Slide 6: Motivation

## Slide 7: Motivation
Current monitoring system is custom made
  Uses custom protocols and formats
Two different approaches are used for keeping data
  In-memory for instant data
  Oracle DB for persistent data
Usage of off-the-shelf components
Usage of standard protocols and formats
Inherent scalability and reliability (fault tolerance/redundancy)

## Slide 8: About Elasticsearch technology

## Slide 9: About Elasticsearch
NoSQL database
RESTful API with JSON over HTTP
Horizontally scalable architecture
Seamless data indexing and searching throughout the cluster
Based on Apache Lucene

## Slide 10: Elasticsearch terminology
Elasticsearch cluster
Node 1
Index n
Index 1
Shard 1 (primary)
Shard 2 (primary)
Shard 1 (primary)
Shard 2 (primary)
Node 2
Index n
Index 1
Shard 1 (replica)
Shard 2 (replica)
Shard 1 (replica)
Shard 2 (replica)
Fields
…
…
{
“name“: „ferol2“,
“slotNumber“: 2,
“rate“: 1.2,
“busy“: true,
“values“: [4.5, 2.3, 12.1]
}
Index
Document 1
Document 2
Document n
…

## Slide 11: Elasticsearch-based monitoring system

## Slide 12: Data life cycle
Index
n
Index n+2
Index n+3
Index n+4
Index n+5
timetolive
timeinterval
expired data
Full data available
Index
n+1
Index
Document 1
Document 2
Document n
…
Most of the monitoring data has a defined lifetime (timetolive) and has to be removed when expires
Time based indices are created automatically according to a timeinterval
Efficient data removal is achieved by index deletion

## Slide 13: Indices, documents and aliases
Document
in
in+1
in+2
in+3
in+4
Full history
Last updates
Access to full data set
Access to the latest data for instant monitoring
Expired
Searchable
Flashing
in+5
Alias
Index

## Slide 14: Managing the load
…
Scalability is achieved by distributing the load among several Elasticsearch nodes using round-robin DNS for reading and writing

## Slide 15: Cloud oriented architecture
…
Expert Systems
Monitoring Systems
External Users
Data Sources

## Slide 16: Coping with backpressure
Data Source
Index creation is an expensive operation. Red and yellow
states indicate that shards are not fully allocated.

## Slide 17: Rotation of aliases and indices
Delete expired indices
Update aliases of indices
Indices with expired data are removed by scripts started periodically by cronjob
“Last updates” aliases are moved to the most recent indices

## Slide 18: System diagnostics

## Slide 19: Monitoring data age

## Slide 20: Conclusion

## Slide 21: Conclusion
Used in parallel with existing monitoring system with comparable performance and functionality
Valuable solution for a future monitoring system
Pros
  Scalability
  Fault tolerance/redundancy
  Uniform access for reading and writing
  Free, well documented software
Cons
  Frequent Elasticsearch releases with deprecated features
  Tedious porting of client software after major Elasticsearch releases
  Limited number of data types (e.g., lacks unsigned integer 64)
  Burden on client software to manage time-to-live

## Slide 22: Thank you for your attention