## Slide 1: The Open High Throughput Computing Content Delivery Network
Dave Dykstra
CHEP 2018
10 July 2018

## Slide 2: Background - WLCG Content Delivery Network
The WLCG Content Delivery Network is based on general purpose squids, primarily for CVMFS and the Frontier Distributed Database Caching system
Last CHEP I presented a new way to find squids: Web Proxy Auto Discovery
  At http://wlcg-wpad.cern.ch/wpad.dat and http://wlcg-wpad.fnal.gov/wpad.dat
  Since then the service has been updated:
    Based on CMS & ATLAS squid registrations, cross-checked against registrations in GOCDB & OIM, plus a few additional squids manually added
    Different answers can be given for different address ranges in same GeoIP Organizations -- used to distinguish CERN Meyrin & Wigner, for example
  Now used in production by U.S. CMS opportunistic computing
  WLCG standard extended to look first for http://grid-wpad/wpad.dat to provide local override & offload
    implemented at CERN, including IPv6 support
Having squids on-site is important for low-latency and performance with many queries and clients, but what about very small sites or extremely distributed resources such as LHC@Home?

## Slide 3: Cloudflare CDN
Cloudflare is a large commercial Content Delivery Network vendor
  Has easy-to-use web interface
  Works with any domain when Cloudflare hosts the DNS
  Caches Http content from any hosted DNS alias in their huge network of distributed caching servers
    Administrator can choose whether aliases are cached or not cached
  Works with CVMFS & Frontier
  Has a free tier that allows unlimited bandwidth
  Includes DDoS protections, IPv6 support, DNSSEC, and more

## Slide 4: AnyCast
Cloudflare uses a small number of IP addresses automatically routed to their nearest data center with AnyCast
  No need to abuse DNS caching (as I suggested at the last CHEP) with different responses based on GeoIP
  Requires a lot of effort on their part to set up, to arrange with many ISPs
    Not something that could be used to direct traffic to squids at many grid sites; needs one entity controlling the distributed network
Addresses are shared, but queries are directed to the correct origin server based on the ‘Host’ header from clients

## Slide 5: openhtc.io
Domain hosted in Cloudflare free tier
For use when no local squids are available
“Page Rules” set to Cache Everything, Respect server expiration headers
Domain is set up for long term sustainability, with multiple people having access
Initial aliases are made for CVMFS stratum 1s and CMS frontier servers. For example:
  s1fnal-cvmfs.openhtc.io, s1cern-cvmfs.openhtc.io
  cms-frontier.openhtc.io
Extendable to other High Throughput Computing applications if they don’t want to use their own domain

## Slide 6: Use cases
In production use for LHC@Home
Configured for any Open Science Grid cvmfs installation that sets CVMFS_HTTP_PROXY=DIRECT
Configured for Frontier for U.S. CMS opportunistic use, when no WLCG squid available to WPAD
  Hasn’t actually run at such sites, but was successfully used to serve a large grid site for a weekend when the local squid was failing
Planned for LHC OpenData
Planned for CernVM cvmfs default when nothing found in WLCG WPAD

## Slide 7: Performance
Measurements of CMS@Home have shown an average start time improvement of 295 seconds, almost 5 minutes
  Average start speedup: 2.2 times [measurements thanks to Laurence Field]

## Slide 8: Disadvantages
Much less detailed monitoring
Uses more WAN bandwidth, has higher latency than on-site squids
See more hits on origin servers than using squid alone, but much fewer than the number of clients
Only caches ports 80 & 8080 (and https on 443)
Need to disable If-Modified-Since on Frontier, because it is not possible to purge errors
Cloudflare Terms of Service says they may disable this type of service if they detect it causing problems with their servers
  I asked, and they said that this is unlikely to happen under the expected usage patterns I described
We can live with these disadvantages

## Slide 9: Info
http://openhtc.io
How does Cloudflare work?
How does Anycast work?