## Slide 1: Ion source operation and interventions during the Reliability Run
Linac4 H- sources:
  IS03a (6.5 mm, Einzel 30 kV): 50 mA but poor transfer through LEBT and too large emittance. RFQ trans ~80% peak.
  IS03b (5.5 mm, Einzel 43 kV): 35 mA, LEBT transfer Ok, emittance up to 27 mA Ok but Hollow beam.
  IS03c (AlN, 6.5 mm, 43 kV, reduced filter field strength) being assembled, in its Al2O3 version faced challenging Helicoflex leaks. Not tested yet but should be ready by end of HST.
L4IS Expectations form R2 :
  Test of the Autopilot regulations (must be tuned to each IS-prototype)
  Test of Autopilot-restart procedures (HV and RF)
  Measure Availability via Autopilot logs
  Starting with IS03c: 3 prototypes at 2-3 month intervals including 2 weeks start up + 2 days dedicated RFQ transmission measurements

## Slide 2: Monitoring of the Linac4 H- source availability / reliability
Autopilot test cases

## Slide 4: Status, Conclusion, Outlook
The source beam intensity is close to what was announced as nominal for the cesiated surface prototype.
The emittance suffers form the LEBT and from a hollow beam, there is no evidence that the RMS value of 0.25 p·mm·mrad can be achieved.
  The test stand today delivers an emittance, the positive signals is dominated by SEY, its linearity is questionable. The grids cannot be used besides beam centring.
Precision measurement is mandatory to measure the impact of hardware “improvement” on beam emittance
  Impaired by inhomogeneity of wire response, unknown SEY. Major temperature variation in the hall that cannot be compensated lead to instability even at the 1 hour meas.-duration scale.
The tool for monitoring the availability and reliability of components (HV, RF) will be ready for the Reliability-run.
Organisation of Interventions:
  The list of possible interventions exists, reaction time to failure and down time measurement shall provide feed back

## Slide 5
What will be the beam intensity and pulse length during the run?
  30-40 mA, 200 ms SCC followed by 600 ms beam
What will be the schedule (technical stops, shutdown, etc.)?
  3 periods separated by 2-3 weeks IS exchange
  3-6 cesiations per running period
Who will check the beam parameters, which ones need to be controlled, and what will be the threshold to declare a fault?
  Autopilot + Timber, warning for beam below 90% nominal, fault below 80%
What will happen when a fault is declared?
  Reduced intensity triggers decision meeting, no beam triggers intervention.
Who will come to Linac4 and when if the machine is «on fault»?
  There is no IS piquet. All actions by Autopilot or operators. IS-team during working hours.
Who will do the «post-mortem» of the faults, how the information will be structured and communicated, and who will decide/implement actions?
  IS team will present the result of each period to the Commissioning team. Actions will be proposed by the IS-team, decision by the com-team.