## Slide 2: Beam Instrumentation Availability
L4 Reliability Run – Mini workshop
30 November 2016
F.Roncarolo/U.Raich on behalf of BE-BI

## Slide 3: Diagnostics Park (including L4T)
25 | BPM
15 | BSG
11 | BCT
12 | WS
19 | BLM
2 | BSM
1 | FC
1 | BTV
2 | LEM (2017)

## Slide 4: Systems linked to interlock
BCT watch dogs
  Protect against bad transmission
BLM thresholds
  Protect against losses
SEM grids and WS
  Protect wires
  SIS, to limit the pulse length
Laser emittance meter
  diamond detectors can’t be IN when upstream bend is OFF
  When L4T dump removed: not possible to operate diamond detectors, monitor will measure beam profile and not emittance, no interlock

## Slide 5: Systems operation
SEM and WS
  OP Expert GUI as in PS complex
  Setting up (gains) straight forward
BCT
  BI expert GUI
    used as fixed display by ABP
    used by BI for setting up
    watch dog OP setting (and reset) via OP GUI
      Thresholds (SW) decided by ABP

## Slide 6: Systems operation
BPMs – trajectory
  Setting up by BI via expert GUI. Need to change settings for very short pulses (<100ns)
  OP trajectory display (OP) as in PS complex
BPMs – ToF
  Setting up by BI
  OP display being developed

## Slide 7: Systems operation
BLMs
  BI expert GUI used by BI for setting up and display
  OP display developed for HST (BCTs and BLM) very nice and useful!
  Thresholds: to be studied!
    Need ABP and OP support
  BLMs not in INCA yet. Once done (EYETS?) OP-ABP can manage thresholds, BI support for threshold determination will be always needed

## Slide 8: How instrumentation is operated today (~= foreseen for RR)
BI experts commission the systems
ABP crew try to use them
BI expert intervene to fix the problem
Wire scanner not moving
SEM grid with wrong signals
BPM measuring wrong ToF
All working OK
Ready for users!
Best effort
Diagnostics of the problem and solution when possible within the 24h
BI expert called or JIRA issue sent

## Slide 9: Operation and support during RR
At the beginning of the RR and anytime the beam parameters will change, BI may ask for dedicated time to properly setup the various systems
CERN wide BI support is granted on the best effort basis (apart from LHC BLMs piquet service)
LHC BLM piquet likely not applicable to L4 RR since experts are not trained yet on LINAC4 systems
What proposed by Maurizio (no nights, yes WE days) is ok for BI, remembering that : ‘WE experts availability’ is generally best effort (no piquet) and specifically outside working hours
Operation from the CCC may speed up some intervention (SW and setting up) w.r.t. present operation from the L4 control room

## Slide 10: Main BI system failures (guess)
WS, SEM grids, BSM
  Mechanics
    pneumatic IN-OUT  may stop operation, need access
    Wire breaking  need access and vacuum opening only if want to recover functionality
  Electronics
    Components failure. Easy to change, need access if pre-amps in tunnel fail
  SW
    Wrong configuration or FESA server crashes  fix remotely

## Slide 11: Main BI system failures (guess)
BCT, BPM, BLMs
  Electronics
    Components failure. Easy to change, need access if pre-amps in tunnel fail
  SW
    Wrong configuration or FESA server crashes  fix remotely

## Slide 12: Post Mortem (BLMs)
There is NO post mortem (LHC like) for the L4 BLMs
When the interlock is triggered, the timestamp is recorded
The BLM expert GUI will give the information on if it was losses or electronics failure  call expert

## Slide 13: Technical Stops Schedule during the L4 RR
Overlapping with Injectors and LHC TS is very risky, may end-up in resources problems
Would be wise to have L4 TS the week after normal TSs ? Will be all L4 services available to run L4 during the injectors TSs?

## Slide 14: Conclusions/Outlook
L4 instrumentation is in general ready for 24/7 operation
Still need to install few SEM grid /WS in L4P (vacuum validation)
Certainly need to train ABP and OP teams on L4 (some BI expert interventions are managed by OP elsewhere)
BLM Interlock thresholds still to be studied and defined
Still need few OP GUIs, like for ToF and BSM
BI support during RR will be on best effort basis outside working hours
Could be good to have a review (BI, ABP, OP) before the RR start
  Summary (diagnostics wise) of the160 MeV commissioning
  GUIs status and needs
  Main failures and cures
  ….