## Slide 1: Position resolution of Gd-GEM detectors for the NMX instrument
14.12.2016
RD51 miniweek
This work was funded by the EU Horizon 2020 framework, BrightnESS project 676548
Dorothea Pfeiffer

## Slide 2: NMX detectors

## Slide 3: Reflections of example crystal
NMX: Macromolecular Diffractometer
Science goal: Protein crystallography with neutrons

## Slide 4: TOF separation of reflections

## Slide 5: Requirements and challenges
200 μm position resolution (beyond state of art for time resolved neutron detectors)
High rate requirements with up to MHz/cm2
High gain stability and count rate stability
Mechanical robustness (detectors mounted on freely movable robotic arms)
Reasonable gamma suppression
Idea: Use GEM detector with Gd converter
GEM foil
Electrical field in holes

## Slide 6: Gd-GEM backwards setup
neutron
conversion electron
Start of track

## Slide 7: 10B4C GEM μTPC Results
Pristine position resolution σ <200 μm reached with Single GEM
Detection efficiency < 5 % at normal incidence of neutron
D. Pfeiffer et al., JINST 10 (2015) 04, P04004

## Slide 8: Gd-GEM μTPC Results
Position resolution σ <300 μm reached with Triple GEM, APV-25
Detection efficiency < 12 % at normal incidence of neutron
D. Pfeiffer et al, 2016 JINST 11 P05011

## Slide 9: Better tracking algorithms needed
Used for 10B4C
VMM-like?
Used for APV-25

## Slide 10: Geant4 Gd simulation problems Getting worse in 10.2.p02
Photon Evaporation 10.1
Photon Evaporation 10.2
Without Photon Evaporation
gamma
gamma
gamma
ce
ce
  Problems with gamma spectra:
  https://zzz.physics.umn.edu/lowrad/_media/meeting8/ychen_gdgammas_aarm2015.pdf

## Slide 11: Task division Geant4/Garfield++
gamma
(Standard and low energy EM physics)
“Kill” gamma when entering gas region in Geant4
TransportPhoton()
Garfield++ simulation according to needs
Charged particle
PAI/PAIPhot Model
In gas region
“Kill” secondary e- produced in gas region in Geant4
TransportDeltaElectron()
Charged particle
(Standard and low energy EM physics)
“Kill” primary when entering gas region in Geant4
SetParticle()
NewTrack()
Primary particle entering gas
Physics model in Geant4
Point of transfer of
Control between
Geant4/Garfield++
TrackHeed Method
in Heed/Garfield++
1b
2
1a
Geant4
Garfield++

## Slide 12: Arrival position neutron on converter
10cm x 10 cm detector

## Slide 13: Arrival time neutron on converter
10cm x 10 cm detector

## Slide 14: Arrival position ce in drift
10cm x 10 cm detector

## Slide 15: Arrival position Compton e- in drift
10cm x 10 cm detector

## Slide 16: Arrival position gamma in drift
10cm x 10 cm detector

## Slide 17: Number of conduction electrons in drift
10cm x 10 cm detector

## Slide 18: Position of conduction electron that arrives last in time on first GEM
10% <= 11 um
25% <= 29 um
50% <= 57 um
75% <= 86 um
90 % <= 238 um
92% <= 400 um
Spectrum of ce entering drift
10cm x 10 cm detector

## Slide 19: Degrad Simulations
DEGRAD simulation of 70 keV electron in Ar/CO2 70/30
DEGRAD by Steve Biagi: http://magboltz.web.cern.ch/magboltz/
3D
xz
yz
Only Monte Carlo program that incorporates all relevant physics processes for electrons in gas
Simulations with Geant4/Garfield interface have to be benchmarked against Degrad
Check of primary ionization distribution in Geant4/Garfield++

## Slide 20: Degrad: Obtainable position resolution in um
The (x,y) position of the electron with the smallest z position was taken
2-25% of tracks turn back depending on energy
No drift and diffusion
Infinite volume

## Slide 21: Summary
Scattering of neutron considerably deteriorates position resolution
Two GEM foils instead of three and low material budget readout lead to major improvement
The position where the conversion electron enters the drift can be reconstructed with <= 400 um precision for ca 90% of all conversion (without diffusion from amplification)
Announcements from Stephen: New Magboltz version 11 is out, includes better simulation of molecular light emission by using the null collision technique
New Degrad 3.1 before Xmas will inlcude C2H6 update