## Slide 1: FCC OTHER MAGNETS
E. Todesco
With contributions from L. Bottura, P. Hagen, D. Tommasini,
R. Garcia Tomas, D. Schulte, S. Izquierdo Bermudez (CERN)
B. Dalena (CEA)

## Slide 2: FILLING FACTOR
Filling factor definition
  Ratio between sum of dipole magnetic lengths (over a cell) and cell length
Present status
  LHC: cell length 107 m, 6 dipole of 14.3 m, fill factor 80.3%
  FCC: cell length 214 m, 12 dipoles of 14.3 m, fill factor 80.3%
  Other than dipole, we have
    Quadrupole MQ (2)
    Orbit corrector MCB (2)
    Tuning quadrupoles MQT (2) – sometimes they become skew quadrupole to correct coupling
    Chromatic sextupoles MS (2) – sometimes they become skew sextupoles to correct coupling
    Sextupole spool pieces MCS (12? 6?)
FCC cell [D. Schulte, B. Dalena]

## Slide 3: THE MAIN QUADRUPOLE
Today requirements: 2300 T of integrated field
  Over 50 mm with Nb-Ti you can make 250 T/m … this gives 9 m long magnet so we have to go to Nb3Sn
  This is also why I insisted so much on grading
With Nb3Sn one can reach 400 T/m
[C. Lorin, P. Verdine this conference]
  So we have 6 m magnet

## Slide 4: ORBIT CORRECTORS
LHC orbit correctors are 2.93 T magnets close to each quadrupole
  Nb-Ti ribbon technology
    0.647 m long, ~2 T m requirement
    This magnet is attached to the orbit feedback system so it should be able to act with a ramp rate of 100 s to have full field (for LHC today, 0.03 T/s)
FCC requirement is to have 3.5 T m [B. Dalena talk, this conference]
    With a 4 T field, we can go for a 1 m long magnet
    Nb-Ti magnet, looks at hand
      I would see no reason to push more to save 0.5 m
    So 4 T field, 1 m long magnet, 50 mm aperture

## Slide 5: TUNING QUADRUPOLES
LHC tuning quadrupoles (MQT) are individually powered small quadrupoles close to each main quadrupole
  Nb-Ti ribbon technology
    123 T/m, 0.32 m long, 39 T requirement (5% of the MQ)
    This magnet is attached to the tune feedback system – variations up to 1 T/m/s
FCC requirement is to have 325 T (15% of the MQ) [B. Dalena talk, this conference]
    This because it is assumed that this magnet is also used in the Dispersion Suppressor (DS) to allow optics matching
    But 325 T would imply a 3 m long magnet – too much – or going to Nb3Sn
      With Nb3Sn one could get a 1 m long magnet with 325 T/m
    It would be wiser to have different magnets, one for the arc at 5% of the MQ and one for the DS
    I would propose a 200 T/m over 50 mm (~6 T peak field), with 0.5 m length

## Slide 6: LATTICE SEXTUPOLE
Lattice sextupole in the LHC today (56 mm aperture)
  Nb-Ti ribbon technology, gradient is 4430 T/m2 (0.37 m long)
    This gives integrated gradient of 1635 T/m requirement or equivalently 0.070 m-2 if normalized with the beam rigidity Br
  Lattice sextupole correct chromaticity (not only from the arc)
FCC present requirement is to have 6650 T/m requirement or equivalently 0.040 m-2 [B. Dalena talk, this conference]
  Assuming the same peak field as in the LHC, over 50 mm we can give a gradient of 5560 T/m2, so this is a ~1.2 m long object
    There is a wish to have 15000 T/m requirement or equivalently 0.090 m-2
    This would push the sextupoles towards 3 m length
Lattice sextupoles could be not in the shadow
  Institutes interested in exploring HTS sextupole correctors ?

## Slide 7: SEXTUPOLE SPOOL PIECES
Spool pieces in the LHC today (56 mm aperture)
  Nb-Ti ribbon technology
    Spool piece gradient 1630 T/m2 (0.11 m long)
    One can make much larger gradient as in the lattice sextupole 4430 T/m2
    So, 5560 T/m2, 0.11 m long over 50 mm aperture
  Spool pieces corrects in the LHC a max b3=4.35 units at 7 TeV
  Using the same length (0.11 m) and the lattice sextupole strenght, and rescaling at 50 mm, we can obtain
    Ie we can correct up to ±6 units of b3 at 50 TeV – looks reasonable to me
  We have 10 units swing of b3, we can tentatively place -7 at injection and 3 at high field

## Slide 8: LANDAU OCTUPOLES
Landau octupoles in the LHC today (56 mm aperture)
  Nb-Ti ribbon technology
    Gradient 63×103 T/m3 (0.32 m long)
    Peak field is 1.28 T, one can make at least a factor two stronger
    Plus the scaling with aperture from 56 to 50 mm, one can go to 220×103 T/m3
FCC request: factor 3 to 6 larger than in the LHC [V. Kornilov talk, this conference]
  Factor 3 can be obtained with the 220×103 T/m3 gradient and keeping the same length 0.32 m
    So I would propose 220×103 T/m3 and 0.32 m
    Another factor 2 by either doubling the length or placing in the straight part of the ring

## Slide 9: IR QUADRUPOLES
For the IR, interest in having a large squeeze
  Aperture size ranging from 100 to 150 mm,
  Baselin presented in Rome by Cerutti is a 100 mm aperture, ~200 T/m, 150 m long triplet, with some iteration needed
    Everything was scaled, so gap between magnets is huge
    Magnets are 30 m long, they should be split