## Slide 1
Mechanical Concept, design and prototyping of the STS for the CBM Experiment at FAIR
Oleg Vasylyev, GSI Helmholtz Center, Darmstadt, Germany
for the CBM Collaboration
Forum on Tracking Detector Mechanics, Marseille, 03.07.2017
CBM Engineering

## Slide 2
Agenda
Overview of the Silicon Tracking System
Precision requirements
STS Mechanics
Prototyping activities
Material choice
Cooling concept
Outlook and future plans

## Slide 3
STS inside the thermal enclosure
Self carrying STS Mainframe
STS Units
STS Carbon ladders
1. STS general overview
General facts:
8 Stations
9 Units
106 Carbon ladders
896 Sensor modules
silicon area: ~ 4 m2
X0/station: ≈ 0.3 – 1%
STS inside the magnet
Magnetic field - 1[T]

## Slide 4
1. STS general overview
STS
2.5°
25°
Beam axis
General facts:
large aperture
low material budget
~40 kW dissipated power
-5°C operating temperature
self-triggering read-out electronics
collision rates up to 10 MHz
971
1425
2300
18 STS half- units

## Slide 5
Half-Unit details:
C-Frame
Double-sided silicon
micro-strip sensors
(different sizes)
Carbon fiber “Ladders”
Front-End electronics
Peripheral electronics
Cabling concepts:
ultra-thin r/o cables
On the Ladder
Front-End to peripheral:
r/o cables
power cables
Carbon fiber ladder
Isometric view
Front view
Winding
Silicon sensor carrier
Extremely light
Manufactured by winding
Ladder with silicon sensors
1. STS general overview
ladder concept based on ALICE ITS (S. Igolkin et al.)

## Slide 6
2. Precision requirements
Sensor position on the CF Ladder
≤ 0.1 mm XYZ Positioning tolerance
Tilting precision – not yet defined
Achievable through precise tooling and mounting concept
Prototype assembly tool
Vacuum sensor holder
Positioning via dowel pins
r/o cable support arm
Ladder position on the C-Frame
≤ 0.1 mm XY positioning tolerance
Z positioning – less relevant
Tilting precision – not yet defined
Achievable through mounting concept
Floating bearing on top
Fixed bearing at the bottom
Different concepts considered!
C-Frame position in the Mainframe
+- 0.5mm Positioning
Precise rail system
Precise support structure/baseplate
Mounting concept
STS position in the Magnet
+- 2mm Positioning
Precise rail system
Precise support structure
Position measurement

## Slide 7
Floating bearing pin
Fixed bearing pin
3. STS Mechanics
C-Frame:
Spring plunger
Positioning groove
Floating ladder
bearing
Positioning hole
Fixed ladder
bearing
Spring plunger
CF Ladder DOF
CF Ladder DOF
Compensation of thermal deformations!
C-Frame Mounting
Fixed bearing rails
Floating bearing rails
C-Frame vertical DOF
Advantages:
no thermal stress
thermally incompatible materials possible
Design iterations so far:
Different designs
Different Materials
Still ongoing
Ceramic floating
bearing
Spring plunger
Ceramic fixed
bearing

## Slide 8
4. Prototyping
Starting point -> ¼ Unit 07 detailed CAD:
Features:
Unit 07 is the most critical in terms of height
Different ladder bearings
C-Frame cabling
Full dummy - electronic assembly
Assembled CF ladders
Cooling blocks for electronics
Real mounting sequences
=>
Al Bearing
Al2O3 Bearing
Mechanical parts completed and assembled
Front-End electronics
cooling block
Peripheral electronics
cooling block
Still pending:
Electronic dummy components
Cabling
Validation of the CAD cabling
Small assembled ladder prototype:
Prototype tooling tests
Assembly sequence and method test
Room for improvement

## Slide 9
5. Materials
Thickness: 40mm
CF composite 2mm
Rohacell 36mm
Mainframe:
CF – Rohacell Sandwich considered
High stiffness + thermal insulation
Inserts for threads/fittings
Inner skeleton – Aluminum profiles e.g. ITEM, or CF Profiles
C-Frame:
Glass fiber
Fiber reinforced PEEK
Thickness 15mm
More ideas?
Should be lightweight, electrically insulating and allow threads and fittings
Ladder bearings:
Aluminum pins, anodized?
Aluminum or ceramic bearings
Al Bearing
Ceramic bearing
Al pin
CF Ladders:
Multiple prototypes
Different fibers and manufacturing procedures

## Slide 10
6. Cooling concepts
Combination of two concepts:
Local cooling for the electronics
Global cooling of the detector atmosphere
1. Local cooling:
Front-End electronics
Peripheral electronics
Front-End cooling block
Peripheral cooling block
[Cooling Block prototype; Fa. Cool Tec Electronic GmbH]
Key points:
Removal of the 40 kW electronics power
Local overheating prevention
Industrially manufactured coolers
Good conductive contact required
CO2 cooling system planned
Key points:
Required to achieve cold and dry operation atmosphere: -5°C
Blowing cold Nitrogen
Removal of additional heat dissipated by sensors currents (avoid thermal runaway)
2. Global cooling:

## Slide 11
Further assembly of the ¼ Unit 07
  Dummy-electronics
  Cabling
Material definition based on
  Requirement analysis
  Prototyping activity
Concept testing and development
  Local and global cooling
  Multiple unit assembly
Further prototyping
  Large scale prototypes
  Thermal tests
7. Outlook

## Slide 12
CBM Engineering
Thank you for your attention!

## Slide 13
BACKUP
BACKUP

## Slide 14
3. Tooling
L-Leg gluing concept tool
L-Leg suction cup
3D print, version 2
L-Leg suction cup
3D print, version 1
Sensor holder:
Lapped surface
Vendor data: Flatness
applying glue onto the L-Legs
L-Leg holder in position for gluing
Short Ladder piece with 8 L-Legs

## Slide 15
CBM Engineering
 | Prototype #1 | Prototype #2 | Prototype #3
Support | CFK-pipe / 1,5mm | CFK-pipe / 1,5mm | CFK-pipe / 1,5mm
Matrix | L20/EPH960 | L20/EPH960 | L20/EPH960
Fiber | M55J / 6K | M55J / 6K | M60J / 3K
Roving | 1 | 2 | 3
Weight | 11,2 g | 14,8 g | 11,2 g
prototype 1
prototype 2
prototype 3

## Slide 16
STS module assembly

## Slide 17
Compressed Baryonic Matter (CBM) experiment at FAIR
Physics aim
Exploration of the QCD phase diagram at high net baryon densities and moderate temperatures
Starting with SIS100 projectile energies: 2÷11 GeV/nucleon / = 2.74.9 GeV, protons up to 29 GeV
Observables
Hadrons, electrons, muons, photons
Particle yields and multi-differential cross-sections
Rare diagnostic probes: strange mesons, light vector mesons (ρ, ω, φ), charm production
Challenges in QCD matter physics – The scientific programme of the CBM experiment at FAIR; arXiv:1607.01487v2 [nucl-ex] 24 Nov 2016
Observables
Recent paper