## Slide 1: Status of triplet cryostat and magnet support scheme
D. Ramos, M. Moretti, C. Eymin, V. Parma
HL-LHC TCC, 19 Jan 2017

## Slide 2: The “triplet” cryostat string
Ø 630 mm
~ 10.1 / 9.8 m length
Ø 570 mm
~ 7.4 m length
Ø 630 mm
6.1 m length
~ 2 ton per meter length

## Slide 3: LHC triplet and dipole cross sections
Preference for column support posts but LHC layout cannot fit a larger cold mass plus pumping lines
Alignment principle: The magnet postion w.r.t vacuum vessel is measured (fiducialization); the cryo-magnet is then positioned in space by moving the whole assembly on support jacks. Cold supports are not adjustable.

## Slide 4: Preliminary cryo flowscheme (WP9)
https://edms.cern.ch/document/1710017/0.3
Slope dependent!

## Slide 5: Pipe size estimations (WP9)
https://edms.cern.ch/document/1710017/0.3
Heat loads: https://edms.cern.ch/document/1610730/1.1
Static heat loads: https://edms.cern.ch/document/1690235/0.1
Integration inside the cryostat is driven by the Ø100 mm pumping lines
And…
Free longitudinal cross section for HeII: 150 cm2 (100 cm2 btw. CP and D1)
Size of phase separators: 12.5 L for Q1 to Q3; 5.5 L for CP and D1

## Slide 6: HL-LHC triplet cryostat
Cryo pipe diameters take into account cryo parameters and industrial availability
More details on drawing: LHCQQX__0001
Offset creates space for piping inside the cryostat
GFRE column type supports (3x) with intermediate heat intercept
Sledge on rail cryostating method
Radial gap at the top required for cryostating sledge
Carbon steel vacuum vessel
Aluminium thermal shield 40-60K

## Slide 7: Cold mass interfaces
More details on drawing: LHCQQX__0001
Heat exchangers (2x)
HeII cross section 2x75 cm2 located the at same radius as the heat exchanger
Alternative: HeII cross section 150 cm2. Less work in the tunnel but too close to beam line and large (rigid) bellows!
18 kA busbars
Trim+Correctors / CLIQ
or
Trim / Correctors
HeII inlet
Distance between lines compatible with existing cutting machines
Beam line
Beam screen bellows

## Slide 8: Phase separators and pumping lines
Q1
Q2a
Q2b
Q3
CP
D1
Lower than heat exchanger
2x 6.5 L of liquid volume
Reservation for level gauge (if needed)
Pumping manifold requires locally enlarged diameter: service module

## Slide 9: Jumper between Q3 and CP
Q1
Q2a
Q2b
Q3
CP
D1
Larger diameter and height than today in the LHC
Standardised position of phase sepatators and pumping manifold

## Slide 10: Interconnect and service module Q3-CP
Q1
Q2a
Q2b
Q3
CP
D1
Phase separator is always in same position but connected to IP or non-IP magnet depending on slope
Pumping line if reverse slope
BPM cable feedthroughs
Beam line pumping port (only on CP)
Would not be possible if the heat exchangers of MQXF and CP and D1 were not aligned!

## Slide 11: Distance between cold mass supports
  length 9.785 m
  weight 22.5 ton
a = 3500 mm
Minimum deflection at
a = 0.715xL/2 ≈ 3500 mm

## Slide 12: Cold mass support posts
Two-part GFRE column
Aluminium heat intercept plate (perfect heat intercept)
Fixed support in the centre of cold mass rigidly connects the cold mass to vacuum vessel
Sliding support bolted to the cold mass and sliding on vacuum vessel
Bolted assembly using invar washers and lock tab washers to ensure preload maintained at cold
Thermal shield is supported by the heat intercept plates, thus without additional heat load
Thermalization straps on sliding support for independent movement between cold mass and thermal shield
Fixed support
Sliding support (2x)

## Slide 13: Cryostating tooling: sledge on rails
Cold mass supported on at least 3 points at all times
Minimum gaps for cold mass insertion and removal of sledges must be accounted for
The principle currently used in dipoles and long SSS

## Slide 14: Cryostating tooling
Cold mass+shield lifted wrt nominal
Sledge on rails
Tooling removal
Lifting jack
Lifting jack
Support assembly

## Slide 15: LHC Cryo-magnet stability specifications
Position reproducibility after repeated thermal cycling
Position stability with respect to parasitic loads (interconnects, jumper, friction, tunnel slope)
“Quasi-static” movements

## Slide 16: LHC Geometrical Stability: survey measurements
Survey measurements
with laser tracker
SSS positional stability and reproducibility at cold
Mean: +0.1mm; St.dev.: 0.17mm
Mean: +0.08mm; St.dev.: 0.11mm
Cryo-dipole positional stability after transport to tunnel
Transversal movements
Cryo-dipole
Vertical movements
Cryo-dipole
Courtesy of CERN Survey Team
100 m descent to the tunnel
ROCLA vehicle
Tunnel transportation
Cold mass stability w.r.t. fiducials measurements on 20 cryo-dipoles

## Slide 17: Cold mass position monitoring with Frequency Scanning Interferometry
Helene Mainaud Durand and Mateusz Sozin
Test on LHC cryo-dipole being prepared

## Slide 18: Vacuum vessel
3 cold support posts
Fixed support post in the middle for better cold mass stability when handling + lower sliding stroke on other supports
Isostatic vacuum vessel supports (3 points) postioned for minimum cold mass bending
Reinforcing rings to prevent ovalisation
Optimum distance ~3500 mm
Low carbon steel certified resilience down to -50 ºC for pressure applications
Flanges from 304L forged rings
Minimum length for opening of interconnect sleeve

## Slide 19: Dealing with vacuum and pressure end loads
(0,free,0)
(free,free,0)
Tie rod for longitudinal loads
(free,0,free)
(0,free,0)
“Vacuum force” (~80 kN, @ Q1 and D1)
Pressure end effect from cold mass interconnect
(20 bar in case of quench; actual force depends on interconnect design)
Q1
Q2a
Q2b
Q3
CP
D1

## Slide 20: Vibrations (> few Hz)
Possible sources
  Background noise: measurements available; the response can be simulated (exitation ~nm)
  Helium flow:
    No data available, cannot be simulated
    Consider testing in SMI2 with first prototype?
How to address it, if an issue
  Active beam feedback
  Increase natural frequencies: can’t decrease mass, hence increase stiffness by adding supports (cost, more heat loads, hyperstatic, compromised alignment, higher risk of unknowns)
See also Paolo Fessia’s talk at Chamonix 2017

## Slide 21: A concept of cryostat and cold mass that…
Fits in the tunnel (same width as other LHC cryostats) and encloses all the cryogenic piping running along the string, including phase separators.
Interconnects based on all welded seals (LHC solution), including space required for cutting and welding machines.
Minimises work in the tunnel, by design.
Corrector busbars, trims and CLIQ circuit cables may be routed on auxiliary lines along the cryostat.
Cold mass supports based on LHC dipole and SSS concept. Sledge on rails cryostating principle.
Isostatic support of the cryo-assembly, designed to accomodate pressure end loads (vacuum and quench) and allow remote alignment.
Aims at alignment stability requirements comparable to those of the LHC SSS and cryo-dipole.
Minimises the number of component and assembly variants.

## Slide 22: Thank you for your attention!

## Slide 23: Static heat loads in the cryostat
https://edms.cern.ch/document/1690235/0.1

## Slide 24: The simplest magnet interconnect config. (Q1/Q2a or Q2b/Q3 or CP/D1)
Q1
Q2a
Q2b
Q3
CP
D1
Splice box
Universal expansion joints for lower interc forces

## Slide 25: Full scale mockup being built
Busbar splices and routing
Welding clearances
Envelope for cutting tools

## Slide 26: Complete interconnect
Q1
Q2a
Q2b
Q3
CP
D1
Vacuum vessel sleeve opens towards the IP
Service module

## Slide 27: Before interconnecting
Q1
Q2a
Q2b
Q3
CP
D1
2 orbital welds per line to be done in the tunnel: up to 20 welds in total
Sliding sleeves

## Slide 28
Q1
Q2a
Q2b
Q3
CP
D1
2 feedthroughs per cold mass:
Instrumentation
CLIQ (to be decided)
Feedthroughs are preferably on the connection side of the main magnet
Opening direction of vacuum vessel sleeve

## Slide 29: Q2a/Q2b: both are connection side
Q1
Q2a
Q2b
Q3
CP
D1

## Slide 30: The most compact interconnect
Q1
Q2a
Q2b
Q3
CP
D1
Service module at the IP extremity of every cryoassembly

## Slide 31: CP to D1
D1 cold mass diameter is 570 mm. The heat exchangers and HeII lines will be close to the edge – End covers of same design as other magnets may be required
Similar to what exists today in LHC SSS
Q1
Q2a
Q2b
Q3
CP
D1

## Slide 32: Q1 IP end
Module required for integration of phase separators and pumping line
Cold to warm transition
RF bellows inside cryostat
BPM
Q1
Q2a
Q2b
Q3
CP
D1

## Slide 33: D1-DFX extremity (non-IP side)
Various configurations under discussion taking into account integration, accessibility, pressure loads, etc.
See talk by Yann Leclercq on WP6a
Ex. in this configuration the vacuum force is taken by the D1 vacuum vessel and its supports. Q1 support scheme may be used.
Q1
Q2a
Q2b
Q3
CP
D1

## Slide 34: Present circuit for busbar routing
As of October 2016
The approach being to route the larger and stiffer 18 kA busbars inside the cold masses and the remaining in auxiliary lines

## Slide 35: This is probably not the last iteration…
Pressure drop calculations must now be updated taking into account proposed diameters, bends, bellows, etc.
We need to design the bellows in order to evaluate the distances available for tooling and estimate interconnect forces.
Some interconnect lines will need stiffening supports.
CAD is not enough for the design of interconnects - we build mockups.
Finding a solution for the busbar routing and splicing is very much related to the circuit and busbar characteristics.
Very compact interconnects – intervention time and accessibility will be a challenge when minimising radiation doses to personnel.
There will be opportunities for improvement - let’s give ourselves some more time before agreeing on the cold mass interfaces.