## Slide 1: Preliminary integration of Hollow e-lenses EDMS No: 1764989 v.1 References: 1765930.v.1
M. Alcaide Leon, Paolo Fessia
Contributions
HEL conceptual design and parameters: D. Perini, C. Zanoni Beam optics and HEL technical coordination: Adriana Rossi
HEL 3D Modelling: Antti Kolehmainen
3D Integration Modelling: M. Gonzalez QPS: D. Wollmann, R. Denz, A. Verweij
Power Converters requirements: M. Martino & Y. Thurel Vacuum requirements: Pablo Santos
Cryogenics requirements: Serge Claudet
EDMS No: 1764989 v.1. 16/03/2017

## Slide 2: INDEX
    Introduction to HEL
    Preliminary integration of HEL in HL-LHC machine and technical services in the tunnel of 4L
    Preliminary integration of technical services in service caverns of 4L
    Conclusions

## Slide 3: REMARK
    This is a preliminary integration study of the Hollow e-lenses in the machine lay-out for HL-LHC and its technical services in the tunnel and service caverns with the present conceptual design of the device (EDMS No: 1765930.v1). The conceptual design is subject to change due to further technical optimizations and definitions by the WPs involved in its design. In particular possible integration in the Hollow e-lenses of Beam Instrumentation that are not accounted here and for which the possible impact on the device and layout is not known.

## Slide 4
Introduction to HEL

## Slide 5: HEL- Components
Sector valve for e-gun
1764989 v.1

## Slide 6: HEL- Parameters
Nominal magnetic field of the main solenoid | 4 T
Inner radius of the hollow electron beam @ nominal fields | 0.9 mm (3 σ)
Outer radius of the hollow electron beam @ nominal fields | 1.8 mm (6 σ)
Nominal magnetic field in the e-gun cathode | 0.2 T
Inner diameter of the cathode | 8.05 mm
Outer diameter of the cathode | 16.10 mm
Inner radius of the hollow electron beam @ 4 T with 0.1 T @ cathode | 0.635 mm
Outer radius of the hollow electron beam @ 4 T with 0.1 T @ cathode | 1.275 mm
Nominal current at the cathode | 5 A
Dimensions of the hollow electron beam and of the emitting cathode. As an example we give the dimensions that can be obtained changing the e-gun tuneable solenoid from the nominal level of 0.2 T to 0.1 T.

## Slide 7: HEL- Optics
Courtesy of Adriana Rossi

## Slide 8
Preliminary integration of HEL in HL-LHC machine and technical services in the tunnel of 4L*
*Please note that 4R is symmetric to 4L

## Slide 9: Overview of LSS4 P4L
UA43
RA43
UJ44
UL44
US45
RB44
B2
D3L4
HEL
ADT
ACS
B1
ST0676534_01

## Slide 10
HEL - Dimensions

## Slide 11
HEL - Dimensions
Conceptual design!

## Slide 12: Sketch layout with HEL - 4L
Distance from IP4: 42809 mm

## Slide 13: Sketch layout in case of possible RF upgrade

## Slide 14: Sketch layout in case of possible RF upgrade with arbitrarily longer HEL (+500 mm for instrumentation)

## Slide 15: Layout integration in HL-LHC machine
ST0676534_01
D3
DFB
HEL
V.C Supports
Ventilation door
ADT
ST0676534_01

## Slide 16: Layout integration in HL-LHC machine
ST0574939_01
New design of vacuum chamber supports

## Slide 17: Interface of HEL with other equipment
    Vacuum pressure during operation must be lower 10-11 mbar.
    Vacuum chamber NEG coated.
    Vacuum chamber inner diameter: 80 mm.
    Vacuum chamber material: cooper.
    Bake-out temperature: 250°C.
    25 mm bake-out jacket.
    Sector valve for the e-gun.
      Exchange procedure to be study.
    The design of the collector should avoid degassing.
      In case of collector degassing, ion pumps or in worst case 1 m length NEG coated vacuum pipe on both sides of the HEL should be installed. (Not in present layout proposal) → to be studied by the HEL team and WP12.
    BPM, BCM  Integration to be studied by BE-BI (might increase the lenght of the device)
    Optional: Gas Jet Monitor (will increase the lenght of the device)
135mm
Vacuum:
BI:
454 mm

## Slide 18: Interface with other equipment in the tunnel
  Cryogenics supply:
    Option 1: from existing jumpers coming from D3 or RF modules (first one to be checked but improbable)
    Option 2: New dedicated service module and jumper
      Possibility to install one dedicated service module for HEL leaving space for a future service module for new xxxMHz module or,
      install a double service module with two jumpers for HEL and future xxxMHz module
~14 m
Option 1
Option 2
ST0676534_01
ST0676534_01

## Slide 19: Tunnel general services
  Water cooling pick up for collector
  Water cooling pick up for magnets if they would become resistive
  Services for e-gun powering:
    to be identified

## Slide 20
Preliminary integration of technical services in Service caverns of 4L*
*Please note that 4R is symmetric to 4L

## Slide 21: Power supplies - Circuit rating
450 A
450 A

## Slide 22: Power supplies - Circuit rating
450 A
450 A
  Total number of independent circuits: 17
      7 PC x HL-LHC600A-10V
      10 PC x Cancun 50
  Total number of racks: 6 PC racks + 1 control rack
    Spare slots taken into account
    Water cooling for HL-LHC600A-10V

## Slide 23: Power supplies - Characteristics
  Cabling characteristics:
    Waiting for AC and DC cabling definition and integration
    First check from EN-EL Installed power in UA43/47 should be enough

## Slide 24: HEL – Other racks needs
  QPS:
    EE system needed? Study by WP7 to see if they are self protected
    Racks  2 min, 6 max (if EE needed)
    Location: together with the PCs
  BI: 2 racks for control (Integration educated guess)
  E-gun: sofisticated system, maybe in-kind contribution reserve 2 racks for control

## Slide 25: Racks needs summary
System | Min. racks | Max. racks
Power converters | 7 | 8
QPS | 2 | 6
BI | 1 | 2
E-gun | 1 | 2
Total | 11 | 18

## Slide 26: Option 1: UA43 & UL44 (P4L) / UA47 & UL46 (P4R)
UA43
14 racks
4 racks
Racks- Location
UL44

## Slide 27: Option 2: UA43 (P4L) / UA47 (P4R)
Racks- Location
4 racks or more
UA43
14 racks
4 racks or more

## Slide 28
Conclusions

## Slide 29: Overview of LSS4 P4L until D4 for HL-LHC
BSR - New extraction and hutch
BSR - Old extraction and hutch
NEW ADT: existing reservation
B2
B1
HEL and racks
UA43
ST0676534_01

## Slide 30: HEL – Conclusions
System | Type | Description | Actions
Gas Position Monitor | Open option | It will increase the length of the device, therefore decrease space between HEL and BPM after ADT | Wait to see if it is going to be included
Gun and collector degassing | Design optimization | Design of electrons gun and collector to avoid degassing, otherwise 1m of vacuum chamber in both extremes of HEL with NEG coating needed | Design of the collector avoiding degassing
Space for pumps | Design optimization | Not so much space for the ion pump in e-gun | Interaction with Vacuum for HEL design
Supports for vacuum chamber | Design optimization | Support of vacuum chamber between HEL and Valve takes space maybe needed | Design of new supports
Racks options | Integration study | Two options for racks, depending on total number of racks needed and space availability | Conduct integration studies
Cryogenic supply | Technical study | Two options for cryogenic supply | Conduct studies
EE | Technical study | On-going study to see if the coils are self-protected, it will save space for EE racks | Wait for results
DC Cabling | Study | DC cabling and integration has to be studied | Conduct studies

## Slide 31: HEL – Conclusions
  In view of a possible technological and integration review in autumn this year the integration and service analysis should be updated taking into account:
    Results of EE computation
    Addition of Beam Instrumentation equipment and its impact on the HEL design and of the general services requirements
    A detailed analysis of other ancillary equipment that should be placed in the LHC tunnel (e-gun ancillaries?)
    Cabling routing from PC to HEL should be defined and integrated

## Slide 32
Thank you

## Slide 33: Interface of HEL with other equipment
135mm
BI:
454 mm
From inside to outside in grey the room temperature vacuum tank, in brown the thermal screen, in grey the helium tank wall, in orange the main solenoid, in blue the corrector coils generating a horizontal and a vertical dipole. Then follow the helium tank wall, the thermal screen and the vacuum tank. The overall external diameter is 454 mm.