## Slide 1: FLUKA studies on alternative designs
Jose L. Abelleira on behalf the JAI-FCC team
University of Oxford
7 November 2016
Thanks to Ilaria Besana and Francesco Cerutti (CERN)

## Slide 2: The new triplet
Nominal triplet
JAI Nov 2016 triplet
42 m shorter
Q1
Q2A
Q2B
Q3
Q1
Q2A
Q2B
Q3
IP
The question is if this new, short triplet will withstand the high radiation, already considerable for the nominal triplet
A new triplet is proposed*
*See talk by Leon Van Riesen-Haupt: Global chromatic aspects, L*, triplet lenght, etc.

## Slide 3: The new triplet
 | g [T/m] | L [m]
Q1 | 110 | 23.5
Q2A | 143 | 21.0
Q2B | 143 | 21.0
Q3 | 157 | 23.5
Comparison of the FF quadrupoles
Q1
Q2
Q3
 | g [T/m] | L [m]
Q1 | 107 | 30.8
Q2A | 88.8 | 26.4
Q2B | 88.8 | 26.4
Q3 | 85.8 | 30.8
Nominal triplet
JAI-Nov 2016 triplet
*See talk by Leon Van Riesen-Haupt: Global chromatic aspects,L*, triplet lenght, etc.
Shorter and stronger magnets

## Slide 4: The new triplet
Nominal triplet
JAI Nov 2016 triplet
Abs: 3.45-6.42 cm
Abs: 8.0 - 9.50 cm
Abs: 10.01 - 11.51 cm
For the magnet coil: changed inner diameter of inner layer only. Valid as peak dose occurs in the inner part of the coil.
Q1
Q2-Q3
Q2-Q3
Q1
Apertures reduced
Vacuum pipe
Vacuum pipe
Shielding increased

## Slide 5: The new triplet
2 m
Q1
Q2A
0.9 m
corrector
Free space to add an additional TAS
For the moment not needed if Q1 shielding is as in Q2-Q3 (slide 4)
JAI-Nov 2016 triplet

## Slide 6: The new triplet
Nominal triplet
JAI-Nov 2016 triplet
* Leon Van Riesen-Haupt: Global chromatic aspects,L*, triplet lenght, etc.
Beta functions reduced at Q1 and Q2

## Slide 7: FLUKA simulations
The increased shielding at Q1 aimed a reduction of the dose in Q2A (otherwise the peak goes very high)
Simulated dose for 3 ab-1
Model parametrized for fast iteration with optics
Parameters: magnet length, position, B, absorber, quadrupole coils
Spectrometer off
(Half) Crossing angle 89.15 μrad both horizontal and vertical crossing
L integrated: 3 ab-1
Cross section : 108 mbarn

## Slide 8: The new triplet: dose
horizontal
vertical
Localized maxima at a single side of the magnet
Q1
Q2A
Q2B
Q3
Q1
Q2A
Q2B
Q3

## Slide 9: Variation of the absorber
This case is limited in acceptance
r = 3.45 cm, A = 12σ
r = 4.0 cm, A = 16σ
r = 4.5 cm, A = 19σ
Other two cases have been simulated. Same magnets, varying the thickness of the absorber.
Q1
Q2-Q3
Q1
Q2-Q3
Q1
Q2-Q3

## Slide 10: Variation of the absorber: dose
Maximum dose 10-25 MGY for the vertical crossing and 8-15 for the horizontal.
Simulated dose for 3 ab-1
Excessive at Q3 (large beta function), specially for the vertical crossing.
Comparison with the results of the nominal triplet (Ilaria, FCC week 2016)

## Slide 11: Variation of the absorber: dose
As the maxima are localized within one side of the magnet, alternating crossing plane reduces the peak dose [Ilaria*].
Maximum dose for 50% time horizontal crossing and 50 % vertical.
Peak dose reduced and more evenly distributed across the quadrupoles
*Ilaria Besana: FCC week 2016: Collision debris on the triplet quadrupoles

## Slide 12: Variation of the absorber: dose
Inner radius [cm] | Shielding thickness [cm] | Beam stay clear [σ] | Max dose H [MGy] | Max dose V [MGy] | Max. dose 50% hor 50% ver [MGy]
4.5 | 1.9 | 19 | 25 | 15 | 14
4.0 | 2.4 | 16 | 15 | 10 | 10
3.45 | 3.0 | 12 | 10 | 7 | 7
Even for the highest acceptance the peak dose is reduced to 14 MGy
Comparison with the results of the nominal triplet (Ilaria, FCC week 2016)

## Slide 13: Other studies
Trying to get an solution for the energy dose profile
  Identifying main parameters that play a role:
    Crossing angle
    Beam size and beam divergence
    Magnet strength (k changes for different p)
    Shielding thickness
    Inner radius
Example: simulation without k=0 for the quads

## Slide 14: Other studies
Muons through rock
  Simulations ongoing, two step method
    Simulate pp collision and dump muons at the end of the detector
    Transport muons through the tunnel model
Elliptical optics
  Each triplet configuration needs now 4 simulations: left/right and hor/ver.

## Slide 15: Conclusions
A new triplet ‘JAI November 2016’ has been designed.
This triplet is more compact that the nominal one.
After some iteration with optics, three different variations in the quadrupoles have been presented.
The dose is reduced with respect to the original case thanks to the increased shielding in pipe and magnets.
The results improves considerably if alternating crossing is used.
Dose does not represent a stopper for shortening the triplet.