## Slide 1: WP13 – JRA 1
WP13 = JRA1 = Innovative gas detectors
WP COORDINATORS:
Silvia Dalla Torre, Imad Laktineh

## Slide 2: WP13, SCIENTIFIC ASPECTS
2 TECHNOLOGIES: the future of GAS DETECTORS
  RPCs
  MPGDs
TASKs grouped in 3 major sectors
  Advanced detector developments, namely detector R&D:
    TASK 13.2, including 5 activities
  Tools to facilitate the detector development, namely technological R&D oriented to detector development by realizing dedicated lab instruments:
    TASK 13.3, including 3 activities
  Preparation for large series production, namely establishing techniques and protocols for large size/series construction, QA, production transfer to industry:
    TASK 13.4, including 7 activities
The program is a good balance between
  R&D for better and better detector performance matching the requirements of present and future experiments
  Tool development and TT to ensure the construction of large experimental set-ups (and facilitating applications beyond research)
1/4
REMINDER

## Slide 3: INSTITUTIONS & ACTIVITIES
11 beneficiary groups
9 partner groups
In total : 13 Institutions

## Slide 4: THIS REPORT
The focus of the activity report is on
  last year activity
  deliverables and milestones expected in the next months
    2 DELIVERABLES, M24
    4 MILESTONES, M24
    1 MILESTONE, M26

## Slide 5: RPCs

## Slide 6: RPCs vs AIDA2020-WP13
what is strategic and how WP13 answers to the quest
Low resistivity RPCs for high rates TASKs 13.2.1, 13.2.3
Fast timing RPCs TASK 13.2.2
Large RPCs TASKs 13.2.2, 13.4.1
Eco-friendly gases TASKs 13.2.3
Large production TASK 13.4.6
REMINDER

## Slide 7: Low resistance RPCs for high rates
Test at CERN SPS
~1010 W/cm
~1012-1013 W/cm

## Slide 8: Low resistance RPCs for high rates
Test at CERN SPS
~1010 W/cm
~1012-1013 W/cm
1 m2
This activity results in a fully satisfactory matching of the milestome MS52

## Slide 9: Fast timing RPCs
1 m2
Reading out the strips at the 2 ends
s = 202 ps
Evaluation of the PETIROC ASIC

## Slide 10: ANOTHER INGREDIENT TOWARDS HIGH RATES

## Slide 11: LARGE SIZE RPCs
Towards large size also with new low R materials:
Enginering mosaic-type layers (gas tight!)
Dedicated large-size clean room with specific equipment

## Slide 12: ECO-FRIENDLY GASSES

## Slide 13: LARGE PRODUCTION, ENGINEERING PHASE

## Slide 14: LARGE PRODUCTION, QC
Detector quality control:
Measurements of the electrode resistivity
Control of the gap production

## Slide 15: MPGDs

## Slide 16: MPGDs vs AIDA2020-WP13
what is strategic and how WP13 answers to the quest
Novel architectures TASKs 1.2.4, 1.2.5
    Finer time resolution
    Finer space resolution
    Higher gain
    Higher rate capability
    Simplified construction
Tools for lab and experiments TASKs 1.3.1, 1.3.2, 1.3.3
Quality Control TASKs 1.4.3, 1.4.4, 1.4.5
Large production and TT TASKs 1.4.2, 1.4.7
Applications beyond science TASKs 1.2.4, 1.2.5, 1.4.3, 1.4.4, 1.4.5, 1.4.2, 1.4.7
REMINDER

## Slide 17: mR-WELL
Home house
REMINDER
local high rate, so far
large area irradiation at test beam, next June

## Slide 18: mR-WELL
Home house
REMINDER
local high rate, so far
large area irradiation at test beam, next June
Home house
This recent activity is more advanced respect to the milestone MS53.
Previously presented results fully match of the milestome MS53.

## Slide 19: HIGH GAIN MPGD
Staggered THGEMs
REMINDER
THGEMS by Permaglas ME730
by RESARM Engineering Plastics SA
Raw material characterization
Electrostatic properties by Paschen test
GAIN UNIFORMITY SCAN: s: 13%
ENERGY RESOLUTION: 20 %
GAIN vs TIME
  Charging-up
  Ion motion in the bulk material
Nominal thickness 0.7 mm
  /D/ < 4%; s < 2%
Nominal thickness 1 mm
  /D/ < 2%; s < 1%
90% PASCHEN limit
Conclusions:
Robust material, remarkable uniformity performance
Easy to operate and limited gain dependence vs time
Good potentialities for high gain multilayer devices
Interesting as a replacement for THGEM by etchableglass
approaches: much cheaper !

## Slide 20: HIGH GAIN MPGD
Staggered THGEMs
REMINDER
THGEMS by Permaglas ME730
by RESARM Engineering Plastics SA
Raw material characterization
Electrostatic properties by Paschen test
GAIN UNIFORMITY SCAN: s: 13%
ENERGY RESOLUTION: 20 %
GAIN vs TIME
  Charging-up
  Ion motion in the bulk material
Nominal thickness 0.7 mm
  /D/ < 4%; s < 2%
Nominal thickness 1 mm
  /D/ < 2%; s < 1%
90% PASCHEN limit
Conclusions:
Robust material, remarkable uniformity performance
Easy to operate and limited gain dependence vs time
Good potentialities for high gain multilayer devices
Interesting as a replacement for THGEM by etchableglass
approaches: much cheaper !
Nominal thickness 0.7 mm
  /D/ < 4%; s < 2%
Nominal thickness 1 mm
  /D/ < 2%; s < 1%
This activity results in a fully satisfactory matching of the milestome MS61

## Slide 21: INTEGRATION OF FE-chips IN SRS

## Slide 22: DEVELOPMENT OF MPGD-dedicated ELECTRONIC TOOLS
 | Task 13.3.2
Deliverable [M24] | High Voltage Power Supply for MPGD
LAST YEAR
NOW
NEXT STEP

## Slide 23: DEVELOPMENT OF MPGD-dedicated ELECTRONIC TOOLS
 | Task 13.3.2
Deliverable [M24] | High Voltage Power Supply for MPGD
LAST YEAR
NOW
NEXT STEP
This activity results in a fully satisfactory matching of the DELIVERABLE D13.6

## Slide 24: DEVELOPMENT OF MPGD-dedicated ELECTRONIC TOOLS
 | Task 13.3.2
Deliverable [M24] | High Voltage Power Supply for MPGD
 | (Floating) Pico ammeter
 | Signal Processing
 | Monitoring and Control Unit
FemtoBox: femto-ammeter
APIC:
Charge Preamplifier
– Shaper Amplifier
Chain
Chips
commercially
available
Microcontroller
of environmental parameters:
Present version WIN_CC OA
Next version: Raspberry Pi

## Slide 25: Development of a general purpose readout electronics for MPGDs
Chip SALTRO16 ASIC
Status summary
The packaging of the SALTRO16 ASIC:s is underway.
Delivery expected mid June.
The design of the Development Board is ready
A first version of the DAQ system enables readout of data
NOW smaller packing possible
To avoid carrier difficulties:
Chips at NOVAPACK

## Slide 26: QA: Control of foil/micromesh mechanical tensioning
Moiré fringe interferometry ON LARGE SIZE, engineered  resolution: 31 mm
Fiber Brag Grating
(FBG) sensors
embedded in MPGDs
and tested

## Slide 27: QA: Control of foil/micromesh mechanical tensioning
Moiré fringe interferometry ON LARGE SIZE, engineered  resolution: 31 mm
Fiber Brag Grating
(FBG) sensors
embedded in MPGDs
and tested
This activity result in a fully satisfactory matching of the milestome MS54

## Slide 28: QA: Leopard scanning system for THGEMs/GEMs
Small size prototype of optical / gain scanning, high resolution

## Slide 29: QA: the electrical integrity of electrode patterns
automatic system to ensure the electrical integrity of electrode patterns by pulse reflection method
EXAMPLE:
2D readout geometry

## Slide 30: QA: the electrical integrity of electrode patterns
automatic system to ensure the electrical integrity of electrode patterns by pulse reflection method
EXAMPLE:
2D readout geometry
EXAMPLE:
2D readout geometry
This activity result in a fully satisfactory matching of the milestone MS55

## Slide 31: LARGE PRODUCTION: RESISTIVE LAYERS

## Slide 32: LARGE PRODUCTION: RESISTIVE LAYERS
This activity result in a fully satisfactory matching of the DELIVERABLE D13.7

## Slide 33: LARGE PRODUCTION: TOWARDS INDUSTRIALIZATION
Anode PCB for ATLAS NSW
Now standard production at ELVIA and ELTOS
THGEM INDUSTRIAL TRANSFER
First example:
THGEM for COMPASS RICH produced by ELTOS
30x60 cm2, thickness 0.4 mm
  Hole pitch 800 µm and diameter 400 µm, no rim
  Large production of THGEM (LEM) for WA105,
  Both ELTOS and ELVIA production satisfactory

## Slide 34: MANAGEMENT & ADMINISTRATIVE ASPECTS

## Slide 35: DELIVERABLES, NEXT MONTHS
= 30/4/2017
report already submitted
to AIDA2020 management

## Slide 36: MILESTONES, NEXT MONTHS
report already submitted
to AIDA2020 management
= 30/4/2017
= 30/6/2017
REMINDER:
Milestone successfully matched (1 May 2016)
report already to be submitted
to AIDA2020 management

## Slide 37: WP13 papers (Dec. 2016)
1 | F. Lagarde, M. Gouzevitch, I. Laktineh, V. Buridon, X. Chen et al. High rate, fast timing Glass RPC for the high {\eta} CMS muon detectors XIIIth Workshop on Resistive Plate Chambers and related detectors, Feb 2016, Ghent, Belgium. Journal of Instrumentation, 11, pp.C09006, 2016
2 | The μ-RWELL: “A compact, spark protected, single amplification-stage MPGD”, Nucl. Instr. & Meth A 824 (2016) 565.
3 | M. Alexeev et al., ”The gain in Thick GEM multipliers and its time-evolution”, 2015 JINST 10 (2015) P03026.
4 | M. Alexeev et al., “Status of the Development of Large Area Photon Detectors based on THGEMs and Hybrid MPGD architectures for Cherenkov Imaging Applications”, Nucl. Instrum. Meth. A824 (2016) 139.
5 | S. Dalla Torre, “The brilliant present and the promising perspectives of the Micropattern Gaseous Detectors”, Nuclear Physics News, Vol 26 (2016), no 3.
6 | L. Benussi for the CMS GEM collaboration, « A novel application of Fiber Bragg Grating (FBG) sensors in MPGD », arXiv:1512.08529 [physics.ins-det] INFN-15-10-LNF To be published in JINST (http://cds.cern.ch/record/2118619)

## Slide 38: SURVEY of RESOURCES
third survey with confirmation of previous indications
(previous surveys on 4/6/15, on 15/6/16)
  Manpower available for the various activities
    No critical issue detected
  Complementary (respect to EC contribution) financial resources for equipment and consumables:
    In general they look available
  Laboratory infrastructures
    Adequate labs and related equipment available (all partners)

## Slide 39: WP13 MANAGEMENT
Coordination strategy and its implementation:
  Close activity monitoring by regular meetings
    In the last year: 20/1/2017, 5/4/2017
  Help line:
    The task coordinators are invited to promptly contact the WP coordinators if difficulties arise (technical, financial, manpower)
      No need in the past year
  Facilitate the integration of the community:
    facilitate the implementation of all potential synergies also between the different technologies
      Several appearing: resistivity, screen printing and sputtering, foil planarity, lab equipment, novel eco-friendly gas mixtures, …
    WP13 meetings useful also from this point of view

## Slide 40: WP13 MANAGEMENT
WP13 within AIDA2020
2 reports (talks) by WP13 at the AIDA2020 Steering Committee meetings
  On 23/9/2016
  On 2/2/2017
Written periodical reports
  P1 report (18 months); WP13 contribution sent to management on 5/12/2016
  WP14 mid term report (2 years): WP13 contribution sent to management on 28/3/2017
Synergies with WP4 (Micro-electronics)
Possibility of synergies with WP8 (Large scale cryogenic liquid detectors)
Arising synergies with WP2 (Innovation and Outreach)
  related to WP13 dedication to TT

## Slide 41: SUMMARIZING
WP13 : 20 groups from 13 different Institutions
  AIDA2020-WP13 is cultural common house for the gas detector community in Europe
All the activities (tasks) are progressing well and there is no delay respect to the foreseen planning
  For both technologies: RPCs and MPGDs
  Activity progress also tested by matching DELIVERABLES and MILESTONES:
  In WP13 so far: 2 deliverables, 6 (1+4+1) milestones
  Resources available as required by the work planning
  Some examples of novel investigation domains originally not foreseen: vitality !
Synergies with different WPs within AIDA2020 also present:
  There is space to improve further

## Slide 42
Advertisement :
MPGD2017 – 5th international Conference on MPGDs
at Temple University (Philadelphia)
May 2017
It follows:
MPGD2009, Kolympari-Crete, Greece
MPGD2011, Kobe, Japan
MPGD2013, Zaragoza, Spain
MPGD2015, Trieste, Italy
MPGD2015 - TRIESTE

## Slide 43: BACK-UP

## Slide 44: WP13, SCIENTIFIC ASPECTS
2/4

## Slide 45: WP13, SCIENTIFIC ASPECTS
3/4

## Slide 46: WP13, SCIENTIFIC ASPECTS
4/4