## Slide 1: WP5: Data Acquisition System for Beam Tests
D. Cussans, on behalf of WP5

## Slide 2: Outline
Introduction:
  Aim of WP5: Common DAQ
  Enhancements with respect to AIDA
Status
  Hardware – Trigger/Timing Logic Unit (TLU)
  DAQ – EUDAQ 2
  Data model –
    mixing triggered, self-triggered, continuously integrating detectors
  Data Quality Monitoring – DQM4HEP
Project Planning
Conclusion

## Slide 3: Aims
Make software and hardware tools to make beam-test DAQ : Easier / Better / Nicer
Focused on supporting Linear Collider R&D, but aiming to be general.
A tool-kit for making DAQ systems
  Inspired by XDAQ package
Tools to build common DAQ systems from existing DAQ systems
  Common run-control

## Slide 4: Enhancements - Highlights
 | AIDA | AIDA-2020
DAQ software (EUDAQ) | Single data collector Fixed FSM Focused on beam telescope | Scalable data collector Flexible state machine General
Data Model | Tag event with trigger number | Tag event with trigger and/or timestamp
Data Quality Monitoring | Dedicated to pixel detectors | Use DQM4HEP framework - general
Hardware (TLU) | Aging FPGA family 4 trigger inputs | Current model FPGA 6 trigger inputs Low jitter clock
Beam telescope | Trigger rate < O(10kHz) | Trigger rate < O(1MHz)

## Slide 5
Hardware
New hardware based on the successful miniTLU one
More trigger inputs (46)
Increased number of DUT (34)
Multiple clock generation options
  On-board oscillator
  DUT
  Differential LEMO
  Highly configurable clock chip
mini-HDMI  HDMI connectors
Fast threshold discriminators for trigger detection
Firmware ported to Xilinx series 7 devices
Launching production in 2 weeks – contact us if interested in a unit

## Slide 6: Latency test (non optimized)
~116 ns
TRIGGER TO DUT
INPUT PULSE
40 MHz clock
Delay
~25 ns
PULSE GENERATOR
TLU
OSCILLOSCOPE
TRIGGER IN
DUT signal

## Slide 7
RunControl maintains a database about the address of clients and sends command to them.
The Standard RunControl EUDAQ is enough for most user cases.
FSM state
New in EUDAQ2
QT GUI is decoupled from RunControl and EUDET-telecope
User can reuse the GUI with their own RunControl without touch GUI code.
Provide flexible to have dedicated RunControl to integrate with other DAQ system .
The FSM states EUDAQ clients are checked by RunControl
04/04/2017 Yi Liu DESY EUDAQ: A common data acquisition framework 5/14
DAQ Software –
Run Control

## Slide 8
DAQ Software –
EUDAQ 1 Event building
EUDAQ 1 philosophy : common readout frames in synchronization with trigger id driven by the TLU → trigger number and event number are the same !
DUT1Producer:
DUT1
RawDataEvent
Trigger ID
DataCollector,
Merges together
RawDataEvents
With the same
Trigger ID
Online conversion to other formats
(LCIO, etc) is possible with
The converters but not necessary
DUT2Producer:
DUT2
TLUProducer:
Creates TLUEvents
(basically trigger ID and
timestamp)
TLU
RawDataEvent
Trigger ID
RawDataEvent
Trigger ID

## Slide 9
Using only a trigger ID to merge multiple data sources inefficient when integration time is different ( externally triggered / self-triggered / continuous integration
- Users can write their own event builder
- Generic DataCollectors for direct synchronization by timestamp and trigger number cases are provided. (next page)
Stream 0
Stream 1
Stream n
……
Time
How to defined a physical event?
How to defined a valid trigger?
Which detector is the trigger device?
In generic case, sub events can arrives in any random time.
04/04/2017 Yi Liu DESY EUDAQ: A common data acquisition framework 8/14
DAQ Software –
Event Building

## Slide 10: Event sync by Timestamp-pair
√
Event N-1
Time slice
Event N
Time slice
Producer A B C D E F G
Time
ts_end n
ts_end n-1
ts_begin n
√n
√n
√n
√n
√n
√n
n-1
n-1
n-1
n-1
n-1
Time length of incoming Event is flexible.
Time slice of merged event is variable
All Producers are equal to each others
Can cope with unmatched data (e.g. noise hits)
Xn
04/04/2017 Yi Liu DESY EUDAQ: A common data acquisition framework 9/14
DAQ Software –
Event Building

## Slide 11
Event Model for Common Beam Tests
Data Collector of all producers + conversion to LCIO file
Detector 1
Detector 2
Detector N
…
Producer 1
Producer 2
...
Producer N
EUDAQ 2
RunControl
+Logger N
Data Collector Producer X, file format Y
...
RawDataEvents
(TS &/or trigger ID)
LCIO objects,
built events
Analysis module for
common DQ 1
...
Analysis module
for common DQ 2
...
Analysis module
for detector X DQ
Events of detector X saved in format Y
EUDAQ 2 – DQM4HEP interface (to be done)
EUDAQ 2
Devices under test
DQM4HEP
AHCAL vs telescope spatial correlations using common (time) events
Adrian Irles

## Slide 12: Data Quality Monitoring
Using DQM4HEP framework from IN2P3
Interface to EUDAQ based system underway
  Reading from files already works
  Providing method for serialization of event data being developed
    Will allow true online monitoring
  Integration with EUDAQ run control underway
DQM4HEP can also be used for environmental parameter monitoring for DESY test beam areas
  See WP15.3.2
Tom Coates. Remi Ete, Antoine Pingault

## Slide 13
CALICE AHCAL / AIDA Beam-telescope combined beam-test
KLAUS
box

## Slide 14
CALICE AHCAL / AIDA Beam-telescope combined beam-test
3 Synchronizations: TriggerID or Readout cycle(ROC) or TimesStamps(TS)
EUDET Trigger Logic Unit (TLU): TrigID (+TS)
AHCAL (CCC+LDA+DIFs): TrigID+ROC+TS
Beam Telescope: Event# (~TrigID)
2017: Mini-TLU (BIF): ROC+TS
2017: Klaus: ROC
DIF
DIF
DIF
DIF
DIF
CCC
LDA
DIF
TLU
Telescope
Mimosa
Mimosa
Mimosa
Mimosa
Mimosa
Mimosa
6x
EUDAQ
TrigID
TrigID
6x
BIF
KLAUS
ROC
+TS3
ROC+
TrigID
+TS2
ROC
ROC
+clk
event#
ROC+ TrigID+
clk
TrigID+ TS1
Jiri Kvasnicka , Katja Kruger

## Slide 15
CALICE AHCAL / AIDA Beam-telescope combined beam-test
3 Synchronizations: TriggerID or Readout cycle(ROC) or TimesStamps(TS)
EUDET Trigger Logic Unit (TLU): TrigID (+TS)
AHCAL (CCC+LDA+DIFs): TrigID+ROC+TS
Beam Telescope: Event# (~TrigID)
2017: Mini-TLU (BIF): ROC+TS
2017: Klaus: ROC
DIF
DIF
DIF
DIF
DIF
CCC
LDA
DIF
TLU
Telescope
Mimosa
Mimosa
Mimosa
Mimosa
Mimosa
Mimosa
6x
EUDAQ
TrigID
TrigID
6x
BIF
KLAUS
ROC
+TS3
ROC+
TrigID
+TS2
ROC
ROC
+clk
event#
ROC+ TrigID+
clk
TrigID+ TS1
Jiri Kvasnicka , Katja Kruger

## Slide 16
CALICE AHCAL / AIDA Beam-telescope combined beam-test
3 Synchronizations: TriggerID or Readout cycle(ROC) or TimesStamps(TS)
EUDET Trigger Logic Unit (TLU): TrigID (+TS)
AHCAL (CCC+LDA+DIFs): TrigID+ROC+TS
Beam Telescope: Event# (~TrigID)
2017: Mini-TLU (BIF): ROC+TS
2017: Klaus: ROC
DIF
DIF
DIF
DIF
DIF
CCC
LDA
DIF
TLU
Telescope
Mimosa
Mimosa
Mimosa
Mimosa
Mimosa
Mimosa
6x
EUDAQ
TrigID
TrigID
6x
BIF
KLAUS
ROC
+TS3
ROC+
TrigID
+TS2
ROC
ROC
+clk
event#
ROC+ TrigID+
clk
TrigID+ TS1
Jiri Kvasnicka , Katja Kruger

## Slide 17
BIF (Beam Interface): Timestamping external signals
Modified firmware of the AIDA mini-TLU
  Receives AHCAL clock
  Knows AHCAL fast commands from HDMI
Records timestamps from 4 inputs (lemo) + start&stop of acquisition
  Estimated time jitter: 1 ns
acquisition is gated (=records only when AHCAL active)
Implemented in the “slave mode” - acts like another LDA/DIF
CCC
LDA
DIF
PC
…
Up to 8 LDAs
Trigger
Spill
BIF
beam
triggers
difference
BIF time-
stamps
[ns]
Jiri Kvasnicka , Katja Kruger

## Slide 18
CALICE AHCAL / AIDA Beam-telescope combined beam-test
3 Synchronizations: TriggerID or Readout cycle(ROC) or TimesStamps(TS)
EUDET Trigger Logic Unit (TLU): TrigID (+TS)
AHCAL (CCC+LDA+DIFs): TrigID+ROC+TS
Beam Telescope: Event# (~TrigID)
2017: Mini-TLU (BIF): ROC+TS
2017: Klaus: ROC
DIF
DIF
DIF
DIF
DIF
CCC
LDA
DIF
TLU
Telescope
Mimosa
Mimosa
Mimosa
Mimosa
Mimosa
Mimosa
6x
EUDAQ
TrigID
TrigID
6x
BIF
KLAUS
ROC
+TS3
ROC+
TrigID
+TS2
ROC
ROC
+clk
event#
ROC+ TrigID+
clk
TrigID+ TS1
Jiri Kvasnicka , Katja Kruger

## Slide 19
CALICE AHCAL / AIDA Beam-telescope combined beam-test
3 Synchronizations: TriggerID or Readout cycle(ROC) or TimesStamps(TS)
EUDET Trigger Logic Unit (TLU): TrigID (+TS)
AHCAL (CCC+LDA+DIFs): TrigID+ROC+TS
Beam Telescope: Event# (~TrigID)
2017: Mini-TLU (BIF): ROC+TS
2017: Klaus: ROC
DIF
DIF
DIF
DIF
DIF
CCC
LDA
DIF
TLU
Telescope
Mimosa
Mimosa
Mimosa
Mimosa
Mimosa
Mimosa
6x
EUDAQ
TrigID
TrigID
6x
BIF
KLAUS
ROC
+TS3
ROC+
TrigID
+TS2
ROC
ROC
+clk
event#
ROC+ TrigID+
clk
TrigID+ TS1
Jiri Kvasnicka , Katja Kruger

## Slide 20
AHCAL_same_bxid ROC
TS_start,
TS_bxid (opt. TS_trig)
triggerID
AHCAL_same_bxid ROC
TS_start,
TS_bxid (opt. TS_trig)
triggerID
LDA ROC,
TS_start,
TS_trig,
triggerID
LDA ROC,
TS_start,
TS_trig,
triggerID
EUDAQ2: New event building
LDA TS ROC,
TS_start,
TS_trig,
triggerID
ROC= ROC,
TS_trig=bxid
TS
overlap
TrigID= Event#
EUDAQ_evt
TrigID(Event#)
Timestamp
ASICs
ROC,
BXID
ASICs
ROC,
BXID
ASICs
ROC,
BXID
ASICs
ROC,
BXID
Mimosa
Event#
Mimosa
Event#
Telescope
Event#
AHCAL_same_bxid
BIF (opt.)
LDA TS
Telescope
AHCAL producer
AHCAL custom data collector
AHCAL data from Labview
BIF producer
Telescope producer
AHCAL_same_bxid ROC
TS_start,
TS_bxid (4 us range)
triggerID
BIF
ROC
TS_start
TS_trigger
simple data collectors available in EUDAQ (triggerID sync / timestamp sync)
here event building is more complex → need a custom data collector
data format kept compatible with EUDAQ1 → analysis in DQM4HEP unchanged
Adrian Irles, Jiri Kvasnicka

## Slide 21
Event building of AHCAL
BXID 0
BXID 42
BXID 140
BXID 0
BXID 80
BXID 108
BXID 140
ASIC1
LDA trigger Timestamp
ASIC2
TS_start
trigger
trigger
BXID 0
BXID 108
BXID 140
ASIC2
BXID 42
BXID 0
BXID 140
BXID 0
BXID 108
BXID 140
BXID 42
BXID 0
BXID 80
BXID 108
BXID 140
BXID 42
BXID 140
BXID 42
time
Same BXIDs
put together:
Built
“Validated AHCAL BXID
Events”
Building

## Slide 22: Combined Beam Tests CMS HGCAL / CALICE AHCAL
Correlations - AHCAL and telescope are synchronous
We look at the spatial correlation of x and y axes of:
  Pixel telescope (1x2 cm)
  Ahcal (36x36 cm, 3cm granularity)
Beam aims at corner between 4 tiles
pix
pix
pix
pix
AHCAL
12x12 tiles
36x36 cm
x
y
x
y
beam
Dec 2016
beam

## Slide 23: Combined Beam Tests CMS HGCAL / CALICE AHCAL
EUDAQ already used by ATLAS and CMS pixel beam test communities
CMS HGCAL planning to use EUDAQ for combined beam-test with Calice AHCAL:
Tanmay Mudholkar , CMS

## Slide 24: Combined Beam Tests – CMS HGCAL / CALICE AHCAL
… including DQM tool
Andrey Pozdnyakov , CMS

## Slide 25: Project Planning - Deliverables
D5.1 Interface Definitions ( M15 , Done ).
D5.2 Trigger Logic Ready ( M30 ).
  Testing prototypes
  Will make modifications and produce TLUs for AIDA-2020 beam-lines.
    Units are costing more than expected  Will have to have a tight definition of AIDA-2020 beam-line
    Will manufacture TLUs for other users at “Cost price”
    May add features to make TLU useful for DUNE as well  larger production run Lower cost. (… and risk of design problems in final unit not borne by AIDA-2020 WP5 … )
D5.3 DAQ Software ( M30 ).
  Basically, EUDAQ 2.0
D5.4 , D5.5 Data acquisition hardware ( M30 )
  Linked to D5.2
D5.6 Common DAQ system used in combined beam tests ( M45 )
  Already running combined beam tests between different Calo systems.
  Integration of Silicon strip tracker progressing

## Slide 26: Project Planning - Milestones 1/2
MS43 , M21 ( TLU Design ready ) reached.
  Prototype TLU exists. Report written
MS46 , M24 ( EUDAQ interfaces to other DAQs available. )
  Reached after release of EUQDAQ 2.0
    EUDAQ 2.0 release due this month.
    Reaching milestone on time will be tight.
MS47 , M24 ( Online event data model available. )
  Linked with EUDAQ 2.0 release
MS62 , M27 ( Development of run control ready )
  Reached when EUDAQ 2.0 is released
MS66 , M30 ( TLU ready hardware )
  See D5.2
MS67 , M30 ( Data quality tools ready )
  Using DAQ4HEP tools ( Ete, Pingault , Mirabito. IN2P3 ) and enhancing integration with EUDAQ
  Looks OK.

## Slide 27: Project Planning - Milestones 2/2
MS68 ( Slow control system ready ) , M30
  Linkage toWP15.3.2
  Can use DQM4HEP framework
MS80 (Common DAQ system ready for combined beam-tests) , M36
  Already mounting common beam-tests between different ILC detector prototype DAQ systems.

## Slide 28: Conclusion
Common DAQ work-package exists to provide tools for beam-test users
  Linkage with many AIDA-2020 work-packages ( e.g. , beam-line infrastructure , calorimeter )
  Linkages outside AIDA-2020 – e.g. LHC groups using beam-telescopes.
Work on
  Hardware for synchronization (TLU)
  Data model for in-homogenous detectors
  DAQ Software (EUDAQ 2) – WP15.2
  DQM Software (using DQM4HEP)
…. going well. Expect to meet milestones on time ( or with only small delay )