## Slide 1
The µ-RWELL (13.2.4) and Tools for its large scale implementation (13.4.5)
LABORATORI NAZIONALI DI FRASCATI
www.lnf.infn.it
AIDA2020 WP13 - Paris, Apr. 5th,2017
G. Bencivenni1
R. De Oliveira2, P. De Simone1, G. Felici1 , M. Gatta1 G. Morello1,
A. Ochi3 , M. Poli Lener1, A. Ranieri4,,V. Valentino4
Laboratori Nazionali di Frascati - INFN
CERN
Kobe University
INFN Sezione di Bari

## Slide 2: WP 13.2.4: the µ-RWELL detector

## Slide 3
  The R&D on µ-RWELL is mainly motivated by the wish of improving the
  stability under heavy irradiation
  & simplify as much as possible
  construction/assembly procedures
Motivation

## Slide 4
The detector architecture
The µ-RWELL is composed of only two elements:
the µ-RWELL_PCB and the cathode
The µ-RWELL_PCB, the core of the detector, is realized by coupling:
a “WELL patterned kapton foil” as “amplification stage”
a “resistive layer” for discharge suppression & current evacuation:
  “Single resistive layer” (SL) <<100 kHz/cm2: single resistive layer  surface resistivity <<100 M/☐ (CMS-phase2 upgrade; SHIP)
  “Double resistive layer” (DL) >> 1 MHz/cm2: more sophisticated resistive scheme must be implemented (MPDG_NEXT- LNF) suitable for LHCb-Muon upgrade
a standard readout PCB
Copper top layer (5µm)
DLC layer (<0.1 µm)
R ̴100 MΩ/□
Rigid PCB readout
electrode
Well pitch: 140 µm
Well diameter: 70-50 µm
Kapton thickness: 50 µm
1
2
3
µ-RWELL PCB
Drift cathode PCB
G. Bencivenni et al., 2015_JINST_10_P02008
(*) DLC = Diamond Like Carbon
High mechanical & chemical resistant material
4

## Slide 5: Principle of operation
Applying a suitable voltage between top copper layer and DLC the “WELL” acts as multiplication channel for the ionization.
The charge induced on the resistive foil is
dispersed with a time constant, τ = ρC ,
determined by
the surface resistivity, 
the capacitance per unit area, which depends on the distance between the resistive foil and the pad readout plane, t
the dielectric constant of the insulating medium, r [M.S. Dixit et al., NIMA 566 (2006) 281]
The main effect of the introduction of the resistive stage is the suppression of the transition from streamer to spark
As a drawback, the capability to stand high particle fluxes is reduced, but an appropriate grounding of the resistive layer with a suitable pitch solves this problem (see High Rate scheme)
top copper layer
kapton
resistive stage
Insulating medium
Pad/strip r/out
HV

r
t
Not in scale

## Slide 6
Main detector features
The µ-RWELL is a single-amplification stage, intrinsically spark protected MPGD characterized by:
simple assembly procedure:
  only two components  µ-RWELL_PCB + cathode
  no critical & time consuming assembly steps:
    no gluing
    no stretching ( no stiff & large frames needed)
    easy handling
  suitable for large area with PCB splicing technique w/small dead zone
cost effective:
  1 PCB r/o, 1 µ-RWELL foil, 1 DLC, 1 cathode and very low man-power
easy to operate:
  very simple HV supply  only 2 independent HV channels or a trivial passive divider (while 3GEM detector  7 HV floating/channels )

## Slide 7
  µ-RWELL: the AIDA program (2016/17)
Optimization of the detector parameters:
  surface resistivity vs gain, rate capability, charge spread, space resolution (completed – paper to be submitted)
  study & implementation of the resistive layer segmentation vs rate capability (completed - paper to be written )
Work to be done in the first 24 months (M24) of the project

## Slide 8
The Low Rate scheme (CMS/SHiP)
3
1
2
DLC layer: 0.1-0.2 µm (10-200 M/☐)
Kapton layer 50 µm
Copper layer 5 µm
DLC-coated base material after copper and kapton chemical etching (WELL amplification stage)
DLC-coated kapton base material
PCB (1-1.6 mm)
Insulating medium (50 µm)

## Slide 9: Detector performance: Lab Tests

## Slide 10
Detector Gain
Prototypes with different resistivity (12-80-880 M/☐) have been tested with X-Rays (5.9 keV), with different gas mixtures, and characterized by measuring the gas gain in current mode.
WELL kapton thickness = 50µm
Ar/iC4H10= 90/10

## Slide 11: Rate capability with X-rays (single layer)
Rate for a drop G = -3%
Φ = 77 kHz/cm2 - 880 MΩ/☐
Φ = 850 kHz/cm2 - 80 MΩ/☐
Φ = 3.4 MHz/cm2 - 11 MΩ/☐
Rate capability fitted with the function:
local irradiation ≠ global irradiation
The gain decrease is correlated with the voltage drop due to the resistive layer: larger the resistivity lower the rate capability.
local irradiation
for m.i.p.×7

## Slide 12: Detector performance: Beam Tests

## Slide 13
GEMs Trackers
BES III-GEM chambers
-RWELL prototype
12-80-880 MΩ /□
400 µm pitch strips
APV25 (CC analysis)
Ar/iC4H10 = 90/10
H4 Beam Area (RD51)
Muon beam momentum: 150 GeV/c
Goliath: B up to 1.4 T
Beam tests results
RWELL = (52+-6) µm
@ B= 0T after TRKs contribution subtraction

## Slide 14
Space resolution vs resistivity
The “space resolution” (σ of the residual – no subtraction of the external trackers contribution) exhibits a minimum around 100MΩ/□.
 at low resistivity the charge spread increases and then σ is worsening.
 at high resistivity the charge spread is too small (Cl_size  1 fired strip) then the Charge Centroid method becomes no more effective (σ  pitch/12)
CC analysis

## Slide 15: Technology Transfer to Industry
In the framework of the CMS-phase2 muon upgrade we have developed large size µ-RWELLs , in strict collaboration with Italian industrial partners (ELTOS & MDT).
The work is performed in two years with following schedule:
Construction & test of the first 1.2x0.5m2 (GE1/1) µ-RWELL 2016 - DONE
Mechanical study and mock-up of 1.8x1.2 m2 (GE2/1) µ-RWELL 2017 - DONE
Construction of the first 1.8x1.2m2 (GE2/1) µ-RWELL (only M4 active) > 2018
~200 times larger than small protos !!!
1.8x1.2m2 (GE2/1) µ-RWELL
~40 times larger than small protos !!!
DONE
mock-up
ELTOS tests

## Slide 16: Towards a High Rate scheme
single resistive layer, edge grounding,
2D evac.
current
Ω ~ ρs x d/2πr
Ω’ ~ ρs’ x 3d’/2πr
Ω/ Ω’ ~ (ρs / ρs’) x d/3d’
If ρs = ρs’  Ω/ Ω’ ~ ρs/ρ’s * d/3d’ = 50/3 = 16.7
(*) point-like irradiation, r << d
Ω is the resistance seen by the current generated by a radiation incident in the center of the detector cell
(*) Morello’s model: appendix A-B (G. Bencivenni et al., 2015_JINST_10_P02008)
r
d
d (50cm)
r
top layer
conductive vias
bottom layer
d’
(1cm)d’
double resistive
layer, 3D grounding
Notes: Let’s switch to the high rate scheme.
To do that try to compare a single resistive layer detector 50x50 cm2 large , with grounding all around its edge and 2D current evacuation,
with a second 50x50 cm2 detector, “orthogonally” grounded every cm2, by means “through-vias” between the top resistive layer
and a second bottom resistive layer. In this second scheme we can imagine that from the point of view of
the resistive layer the detector is practically divided in basic cells 1 cm2 large, and we can speak about a sort of 3D grounding scheme.
The two versions (the single layer & the double layer with through vias) have clearly different performance.
The ratio between the resistance …. Comes out to be of the order of 20 … (under the assumption that the resistivity is the same).
The double layer clearly allows better performance in terms of uniformity response (or equivalently in terms of rate capability).

## Slide 17
DLC layer: 0.1 – 0.2 µm
(10-200 M/☐)
Kapton layer 50 µm
Copper layer 5 µm
The High Rate scheme (LHCb)
insulating layer
DLC-coated base material after copper and kapton chemical etching ( WELL amplification stage)
2nd resistive kapton layer with ∼ 1/cm2 “through vias” density
1
2
4
DLC-coated kapton base material
3
2nd resistive kapton layer
“through vias” for grounding
pad/strips readout on standard PCB

## Slide 18: Rate capability with X-rays (double layer)
Φ = 3.4 MHz/cm2; Φ = 2.8 MHz/cm2; Φ = 1.6 MHz/cm2
Double resistive layer w/ 1x1 cm2 through-vias grounding pitch
local irradiation
for m.i.p.×7
Local irradiation is practically equivalent to global irradiation

## Slide 19
3 -RWELL prototypes
40-35-70 MΩ /□
VFAT (digital FEE)
Ar/CO2/CF4 = 45/15/40
H8 Beam Area (18th Oct. – 9th Nov 2016)
Muon/Pion beam: 150 GeV/c
Beam Test (CMS/LHCb collaboration)
Beam
GEM Tracker 1
N° 2 µ-RWELL protos
10x10 cm2
40-35 M/☐
Double resistive layer scheme
400 µm pitch strips
S3
S1
S2
GEM Tracker 2
N° 1 µ-RWELL proto
100x50 cm2
70 M/☐
Single resistive layer scheme
800 µm pitch strips
GOAL: time resolution measurement (never done before)
Trigger=S1+S2+S3

## Slide 20
97%
Time Performance
5.7ns
Different chambers with different dimensions and resistive schemes exhibit a very similar behavior although realized in different sites (large detector realized @ ELTOS)
The saturation at 5.7 ns is dominated by the fee (measurement done with VFAT2).
To be compared with a measurement done with GEM by some of us in 2004 (LHCb) giving a σt = 4.5 ns with VTX chip [1].
[1] G. Bencivenni et al, NIM A 494 (2002) 156

## Slide 21
Performance vs Rate
The detectors rate capability (with Ed=3.5 kV/cm) has been measured in current mode with a pion beam and irradiating an area of >3 x 3 cm2 (FWHM) (medium size irradiation, ~10 cm2 spot)
Single resistive layer
(Low Rate scheme)
Double resistive layer
(High Rate scheme)

## Slide 22: SUMMARY of WP13.2.4
The µ-RWELL R&D in AIDA2020 is matching the schedule, with very good results.
The most important performance of the detector have been measured:
  gas gain > 104
  intrinsically spark protected
  rate capability >> 1 MHz/cm2 (HR version)
  space resolution < 60µm
  time resolution < 6 ns
The 1st milestone has been succesfully fulfilled:
MS13.3: Small-size prototype of the  -RWELL (built and qualified prototype - M24)
The 2nd milestone foreseen for M44:
D13.4 : Large-size prototype of -RWELL (a large-size fully engineered and validated prototype of the -RWELL - demonstrator)

## Slide 23: WP 13.4.5: tools for readout PCB QC

## Slide 24: Task 13.4.5 Design of an automatic system to check the electrical integrity of electrode patterns by pulse reflection method
Partecipants: INFN-Bari, INFN-LNF
Preparation of tools for large series production
Activity 2016-2017 subdivided in two sub-tasks:
Design and implementation of a TDC embedded structure in the Time Domain Reflectometer (TDR) control logic
Construction of the prototype chamber with -RWell technology & related readout PCB for CMS R&D phase_2, as proof of concept for the TDR
AIDA2020 Mid-term report WP13, task 13.4.5, PARIS2017 meeting

## Slide 25
EXAMPLE:
2D readout geometry
ISSUE: Temperature stability:
  The only reliable method is to put one TDC/channel
1’st TDR proto’s
TDR exploits time measurements -> TDC
Design of a TDC embedded structure in control logic (I)
The drawing shows the run of a signal, in this case a transition from low to high state, injected into an un-terminated transmission line
The first edge occurs when the signal is injected at the input while the second edge is observed after that the signal reflected comes back (in red a threshold level)
Example: 2D readout geometry
AIDA2020 Mid-term report WP13, task 13.4.5, PARIS2017 meeting
The aim of this work is the development of a device capable to find defects on a micro-strips readout plane of a MPGD under test through the search of discontinuities in the impedance profile which cause reflection of injected pulses.
A time resolution of about 100 ps is required to appreciate length differences of about 1 cm

## Slide 26
By analysing the delay of the reflected signal, it is possible to evaluate the length of a transmission line, a micro-strip in the device under test. This length will be as expected by design if the micro-strip is intact, then shorter if there is an interruption somewhere along the strip and longer or shorter, due to multiple reflections, whether some close strips are shorted together
EXAMPLE:
2D readout geometry
Temperature stability issue solved with new release:
  The only reliable method is to put one TDC/channel
  The new release contains one TDC per channel
  32 channels embedded in one FPGA
TDR exploits time measurements -> TDC
Design of a TDC embedded structure in control logic
Workbench with 7 TDR modules connected to an anodic sheet under test and through Ethernet to PC for logging and control
AIDA2020 Mid-term report WP13, task 13.4.5, PARIS2017 meeting
2’nd TDR electronics card
A 2nd release of the TDR board has foreseen n.4 TDCs per FPGA , so that each TDC sequentially read/out n.32 strip channels. Wrt the previous version, the new board is more stable and precise and doesn’t require tedious repeating calibration procedures, having solved the problem of thermal instability.

## Slide 27: Summary Milestones & Deliverables
MS13.10 - Quality control system to ensure the electrical integrity of readout electrode for MPGDs (prototype of a Time Domain Reflectometer: M24)  succesfully fulfilled
  Designed a new TDC scheme inside the FPGA (firmware) to overcome the temperature instability
  As soon as new anodic foils will be delivered for a GE2/1 CMS chamber based on the µ-RWell technology, tests with TDR device will be performed and results will be reported
AIDA2020 Mid-term report WP13, task 13.4.5, PARIS2017 meeting

## Slide 28: Thanks for the attention

## Slide 29: backup

## Slide 30: WELL amplification stage: thickness studies
The increase of the thickness of the amplification stage (Kapton base material thickness) from the standard (GEM like) 50 µm up to 125 µm should result in a increase of the detector gain.
The program for THICK µ-RWELL was started by the end of 2016
BUT
We discovered etching problem with single mask technique (the natural one for µ-RWELL): the needed etching along the whole thickness (125 µm) results in a too large diameter hole (> 100 µm) thus strongly affecting the effective GAIN of the hole itself (exactly the opposite of the desired goal)
THEN
Some change in the manufacturing of the high gain detector is clearly required ( double mask etching + floating amplification stage; …)
Anyway we have demonstrated that using suitable gas mix the detector achieve a Gain 2-3 x 104

## Slide 31
AIDA2020 Mid-term report WP13, PARIS2017 meeting
EXAMPLE:
2D readout geometry
New architecture characteristics
Design of a TDC embedded structure in control logic (II)
Reference clock 320 MHz (better than that previous version: 250MHz)
Measured (after simulation) timing resolution:  100ps
5 bits fine counter + 16 bits coarse counter
33 channels (32 comparator + 1 test input)

## Slide 32
DLC sputtering on large Kapton foils (w/copper on one side) completed @ Be-Sputter Co., Ltd (Japan)
 | Foil 1 (800A) | Foil 2 (1300A) | Foil 3 (1800A) | Foil 4 (1500A) | Foil 5 (1500A)
Average Surface Resistivity M/ | 433±90 | 68±9 | 41±12 | 122±22 | 180±17
Ar/ISO=90/10
DLC sputtering on Kapton foils (supervised by A.Ochi)

## Slide 33: Surface resistivity map (A. Ochi, Kobe – Univ., Japan)
Surface resistivity measured on a 18 points of the 600x1200 mm2 kapton base material

## Slide 34
Ageing test @ GIF++

## Slide 35
Detector engineering for large area tracking & digital calorimetry applications:
    Design of large area demonstrator
    Large area readout design
    Study of FEE-detector coupling
  Work to be done in the second 24 months (M24-48)
  µ-RWELL detector: the AIDA2020 program (II)

## Slide 36: MILESTONES
MS13.3: Small-size prototype of the -RWELL (a built and qualified prototype - M24)
D13.4 : Large-size prototype of -RWELL (a large-size fully engineered and validated prototype of the -RWELL (demonstrator - M44)

## Slide 37
Too low
Too high
strip/pixel r/o
pad r/o
Combining the information
Qualitatively: low resistivity  pad r/out & higher rate
high resistivity  strip/pixel r/out & lower rate