## Slide 1: RFD Experience for SPS and Evolution to LHC
Subashini De Silva
Center for Accelerator Science
Old Dominion University
International Review of the Crab Cavity Performance for HiLumi
CERN – April 3-5, 2017

## Slide 2: Content
RF-Dipole (RFD) Cavity Designs
  Proof-of-principle (PoP) Design (ODU)
  SPS Design (ODU/SLAC)
SPS-RFD Cavity Performance
  Cavity Processing Plan
  RF Test Results
SPS-RFD Cavity Lessons Learned
Recommendations and Evolution to LHC-RFD Cavity Design
  RF Design Modifications
  Engineering Design Modifications

## Slide 3: PoP-RFD Cavity: Design
PoP-RFDCavity – 2010-2012
Operates in TE11-like mode
  Cylindrical shaped design
Fabricated by Niowave Inc. and tested at Jefferson Lab
Frequency | 400.0 | MHz
Aperture | 84 | mm
Nearest HOM | 590 | MHz
Ep* | 4.02 | MV/m
Bp* | 7.06 | mT
[R/Q]t | 287 | Ω
Geometrical Factor (G) | 120 | Ω
RtRs | 3.4×104 | Ω2
At Et* = 1.0 MV/m |  | 
Vt | 3.4 | MV
Ep | 36.5 | MV/m
Bp | 64 | mT
53 cm
34 cm
E Field
B Field

## Slide 4: PoP-RFD Cavity: Performance Results
Processing and rf testing done at Jefferson Lab
RF tests
  Test I – Jefferson Lab – April, 2012
  Test II – Jefferson Lab – June, 2014
  Test III – CERN – October, 2014
Cavity reached a Vt of 7.0 MV
Processed multipacting easily and did not reoccur
Test II and III  Cavity was retested with Nb coated blank flanges at beam ports, provided by CERN
  Q0 increased by a factor of 3 from 4×109 to 1.2×1010
  Reduced Q0 at Test III (at CERN) due to inadequate magnetic shielding (30 mG)
3.4
CERN
3.4 MV
JLab

## Slide 5: SPS-RFD Cavity: Design
Next HOM is 1.5 times fundamental mode
Lower surface fields compared to PoP cavity
Higher shunt impedance
Improved multipacting
Reduced multipoles components with curved poles
 | PoP | SPS | 
Frequency | 400 | 400.79 | MHz
Aperture | 84 |  | mm
Nearest HOM | 590 | 633.5 | MHz
Ep* | 4.02 | 3.6 | MV/m
Bp* | 7.6 | 6.2 | mT
[R/Q]t | 287 | 429.7 | Ω
Geometrical Factor (G) | 120 | 106.7 | Ω
RtRs | 3.4×104 | 4.6×104 | Ω2
At Et* = 1.0 MV/m |  |  | 
Vt | 3.4 | 3.4 | MV
Ep | 36.5 | 33 | MV/m
Bp | 64 | 56 | mT
281 mm
281 mm
194 mm
Operates in TE11 like mode
E Field
H Field
SPS-RFD Cavity for
Crabbing in horizontal plane

## Slide 6: Final SPS-RFD Cavity
Electromagnetic and mechanical design completed by ODU/SLAC team
Interfaces to Helium vessel completed by CERN
Fully integrated design:
  Includes FPC and HOM couplers
  Reinforcements to reduce pressure sensitivity and Lorentz detuning due to radiation pressure
  Tuner interfaces
SPS-RFD Specifications Drawing - CERN

## Slide 7: FPC and HOM Couplers for SPS-RFD Cavity
Couplers are at locations of low field region on cavity body
  Minimizes RF heating on the coupler components
  Location preserves the field symmetry
Two HOM couplers (HHOM and VHOM)
  HHOM  High pass filter
  VHOM  Simple coax coupler
ZL < 50 kΩ per cavity and ZT < 1 MΩ/m per cavity except for two HOMs near 2.0 GHz
Hook shaped FPC coupler  QL = 5.0×105
Reduced rf heating at hook (69 W)

## Slide 8: SPS-RFD Cavity: Processing Path
Reprocessing
steps for
RFD-CAV-001/002

## Slide 9: SPS-RFD Cavity: RF Test Preparation
Accommodate both tests without and with HOM couplers
Measured Qext
  Input probe  Qext ~ 5×109
  Pick Up probe  Qext ~ 2×1011
VHOM and HHOM ports are blanked
  HHOM blanked with a Nb coated flange
FPC Port
Qext ~ 5×109
Pick Up Port
Qext ~ 2×1011
Safety valve
 | Port | Power Loss [W]* | Q
(A) | Beam Port (HHOM) | 3.0×10-4 | 9.5×1013
(B) | Beam Port (VHOM) | 3.1×10-3 | 9.3×1012
(C) | FPC Port | 6.7×10-4 | 4.4×1013
(D) | HHOM Port | 7.5×10-3 | 3.9×1012
(E) | VHOM Port | 3.5×10-8 | 8.3×1017
(F) | Pick Up Port | 2.0×10-17 | 1.5×1027
(A)
(B)
(C)
(D)
(E)
(F)
* At 3.4 MV
Total losses expected 12 mW at 3.4 MV
- Losses at SS flanges (σ = 6.99×106 S/m)

## Slide 10: SPS-RFD Cavity: Performance
At low fields for both rf tests Q0 is > 1.0×1010
Multipacting was processed easily and didn’t reoccur
No field emission observed during Test 2
At 2.0 K | Test 1 | Test 2
Max Vt [MV] | 4.0 MV | 4.4 MV
Ep [MV/m] | 38 | 42
Bp [mT] | 66 | 73
Q0 at 3.4 MV | 5.5×109 | 8.5×109
Pdiss ar 3.4 MV [W] | 4.9 | 3.2

## Slide 11: SPS-RFD Cavity: More Measurements
Lorentz detuning
  Simulated  -122 Hz/(MV/m)2
  Measured –> -112 Hz/(MV/m)2
Pressure sensitivity
  Simulated  -80 Hz/torr
  Measured  -56 Hz/torr
Good agreement with simulations

## Slide 12: SPS-RFD Cavity: Frequency Recipe
Step (Recipe for 20 C, 50 % and 1013.25 mbar) | Δf [kHz] | fn [MHz]
Cavity after trimming and thinning |  | 399.840296
Shift due to bulk BCP (140 microns) | -39.441 | 
Cavity after bulk BCP |  | 399.800855
Weld shrinkage | 115.645 | 
Weld bead | 5.000 | 
Cavity after final weld |  | 399.921500
Shift due to light BCP (20 microns) | -5.762 | 
Cavity after light BCP |  | 399.915738
Shift due to mounted couplers | 4.906 | 
Fully assembled cavity with HOM couplers |  | 399.920644
Pressure effect (760 torr differential) | -60.800 | 
Dielectric effect air to vacuum | 130.341 | 
Evacuated cavity at 20 C |  | 399.990185
Thermal shrinkage | 572.877 | 
Cooled down cavity at 4.2 K |  | 400.563062
Shift due to change in skin depth | 28.000 | 
Pressure from 760 torr to 23 torr in He tank | 58.960 | 
Cooled down cavity at 2.0 K |  | 400.650022
Shift due to tuner activation to its mid range | 150.000 | 
Cavity with tuner activated |  | 400.800022
Lorentz detuning | -10.022 | 
Operational cavity with RF on |  | 400.790000

## Slide 13: SPS-RFD Cavity: Trimming Sensitivity
Trimming sensitivity for RFD cavities
df/dz = -119.85 kHz/mm
Measured sensitivity:
  CAV001: -129.3 kHz/mm
  CAV002: -116.1 kHz/mm
dz/2
dz/2

## Slide 14: SPS-RFD Cavity: Frequency Measurements
Frequency shifts are in agreement between simulation and measurements
Step (Recipe for 20 C, 50 % and 1013.25 mbar) |  | Simulated |  | Measured | 
 |  | Δf [kHz] | fn [MHz] | Δf [kHz] | fn [MHz]
Cavity after trimming and thinning |  |  | 399.840296 |  | 399.846841
Shift due to bulk BCP |  | -39.441 |  | -21.924 | 
Cavity after bulk BCP |  |  |  |  | 399.824917
Shift due to frame |  |  |  | -765.648 | 
Cavity after removing fixture |  |  | 399.800855 |  | 399.059269
Weld shrinkage and weld bead |  | 120.645 |  | 114.686 | 
Cavity after final weld |  |  | 399.921500 |  | 399.173955
Shift due to heat treatment |  |  |  | -10.743 | 
Cavity after heat treatment |  |  |  |  | 399.163212
Shift due to light BCP |  | -5.762 |  | -16.473 | 
Cavity after light BCP |  |  | 399.915738 |  | 399.146739
Pressure effect (23 torr) | -1.84 |  |  |  | 
Dielectric effect air to vacuum | 130.341 |  |  |  | 
Thermal shrinkage | 572.877 |  |  |  | 
Shift due to change in skin depth | 28.000 |  |  |  | 
 |  | 729.378 |  | 755.615 | 
Cooled down cavity at 2.0 K |  |  | 400.645116 |  | 399.902354
The unaccounted frequency shift was due to the use of the frame during some of measurements [400.645 – 399.902 = 743 kHz]

## Slide 15: SPS-RFD Cavity: Lessons Learned
Bulk BCP on sub-assemblies provides no benefit
Bulk BCP of the two SPS-RFD cavities were done before final weld to control frequency shift due to processing
Due to quality of final welds additional bulk BCP was done on both RFD cavities
Frequency shift due to bulk BCP  40 kHz (140 microns uniform removal)
Frequency shift is comparatively small  Not a critical parameter in frequency control
RFD-001
RFD-002
RFD-002
RFD-002

## Slide 16: Recommendations for LHC-RFD: Cavity Processing
Currently bulk BCP, light BCP and HPR are done in vertical orientation
Recommendation  Perform chemical processing in horizontal orientation with rotation and tilting
  Allows more uniform removal
  Better acid circulation and drainage
Use of a high pressure rinse set-up using multiple ports e.g. MSU (Rinsing through FPC and HHOM ports)
  Allows minimizing field emission
Horizontal BCP/EP tool – (ANL)
Stains left from BCP

## Slide 17: Recommendations for LHC-RFD: Warm Tuning
Warm tuning of RFD cavity to achieve target frequency  By pushing/pulling at the top and bottom surface of the center body
Experience from
  Fixing the center body of RFD-CAV-001
  Use of fixtures during trim tuning of sub assemblies
Profile held at the edge
Jack mechanism
Frequency shift after fixing center body = 1.84 MHz
Fixture on center body to match end profiles for trimming
Frequency shift with and without fixture = -0.77 MHz

## Slide 18: LHC-RFD Design: Modifications (1)
LHC-RFD design under US-HL-LHC-AUP
No major modifications are required for LHC-RFD cavity design
Proposed changes are not radical (to be confirmed with CERN)
Change 1: Modify pick up port diameter
  Pickup port radius increased to 40 mm from 20 mm for easier cavity cleaning
  Pickup probe coupling: 2.7×1010 to extract 1 W at operating field
  No change has been seen in simulations on cavity properties or on HOM spectrum and damping

## Slide 19: LHC-RFD Design: Modifications (2)
No major modifications are required for LHC-RFD cavity design
Proposed changes are not radical (to be confirmed with CERN)
Change 2: Increase FPC, HHOM and VHOM ports flange location
  Present design gap between flange and NbTi adapter ring is tight
  Would ease and speed assembly in cleanroom
  Doesn’t change the cavity to He vessel interface locations
  Need to cross check the flange location of demountable HHOM coupler
Tight gap between SS flange and
NbTi adapter ring

## Slide 20: Conclusions
Two SPS-RFD cavities have been fabricated and processed
  RFD-CAV-001  Completed
  RFD-CAV-002  Ready to be tested
Performance levels above requirements for HL-LHC
  Cavity (RFD-CAV-001) reached Vt=4.4 MV
  Ep=42 MV/m and Bp =73 mT  Still much room for improvement
  Achieved 3.4 MV (operating Vt) with a Q0 of 8.5×109 (3.2 W)
  Achieved 4.4 MV (maximum Vt) with a Q0 of 8.0×109 (5.6 W)
No major alteration to the cavity processing plan; Recommendations for future cavities
  Do bulk BCP after final welding
  Horizontal orientation while cavity processing (BCP and HPR)
No major modifications to RFD cavity design for LHC
  Increase pick up port diameter
  Increase port height for ease of assembly in clean room

## Slide 21: Collaboration
THANK YOU