## Slide 1: HOMs for RFD
Subashini De Silva
Center for Accelerator Science
Old Dominion University
International Review of the Crab Cavity Performance for HiLumi
CERN – April 3-5, 2017

## Slide 2: SPS-RFD Cavity: Design
Next HOM is 1.5 times fundamental mode
Lower surface fields compared to PoP cavity
Higher shunt impedance
Improved multipacting
Reduced multipoles components with curved poles
 | PoP | SPS | 
Frequency | 400 | 400.79 | MHz
Aperture | 84 |  | mm
Nearest HOM | 590 | 633.5 | MHz
Ep* | 4.02 | 3.6 | MV/m
Bp* | 7.6 | 6.2 | mT
[R/Q]t | 287 | 429.7 | Ω
Geometrical Factor (G) | 120 | 106.7 | Ω
RtRs | 3.4×104 | 4.6×104 | Ω2
At Et* = 1.0 MV/m |  |  | 
Vt | 3.4 | 3.4 | MV
Ep | 36.5 | 33 | MV/m
Bp | 64 | 56 | mT
281 mm
281 mm
194 mm
Operates in TE11 like mode
E Field
H Field
SPS-RFD Cavity for
Crabbing in horizontal plane

## Slide 3: FPC and HOM Couplers for SPS-RFD Cavity
Couplers are at locations of low field region on cavity body
  Minimizes RF heating on the coupler components
  Location preserves the field symmetry
Two HOM couplers (HHOM and VHOM)
  HHOM  High pass filter
  VHOM  Simple coax coupler
ZL < 50 kΩ per cavity and ZT < 1 MΩ/m per cavity except for two HOMs near 2.0 GHz
Hook shaped FPC coupler  QL = 5.0×105
Reduced rf heating at hook (69 W)

## Slide 4: Impedance Update – Elias Metral (LARP CM26, SLAC 2016)

## Slide 5: HOM Couplers
Horizontal HOM Coupler
Vertical HOM Feedthru

## Slide 6: HOM Power Analysis
Zenghai Li/SLAC

## Slide 7: Boundary Conditions
HV joint
Copper gasket
LHe jacket starts ~20mm above copper gasket
Nb can
Nb
Copper
Ceramic
Copper sleeve
Power applied on extremity only for worst case scenario
* 1mohm increased to 2mohm to account the roughness and strain effect of copper. (Anomalous skin effect and resistive wall heating by Weiren Chou and Francesco Ruggiero, 9/8/1995 CERN)
*

## Slide 8: Results
Copper probe
Nb hook
Copper gasket

## Slide 9: Conclusion – Thermal Study
Niobium hook and tee maintains 10 nΩ range temperature (< 2.1 K).
Copper gasket temperature under 2.3K with doubled heat load.
No thermal runaway → Estimated power dissipation all valid.
No internal helium channel is necessary.