## Slide 1: Slotted foil based THz source design
Jürgen Pfingstner,
15. December 2016
Many thanks to Helga Holmestad and Robert Fröschl.

## Slide 2: Overview
Introduction
Imprint optics
Foil design
Conclusions

## Slide 3: 1. Introduction

## Slide 4: THz source for SwissFEL
Request from material scientists:
  fTHz = 1 – 20 THz (λTHz = 300 – 15μm)
  Ep ≈ 100μJ
  Δω/ω0 < 10% (pref. 5%)
  Phase locked
  frep = 100Hz
Motivation:
  Vibrations within the material lattice occur manly in the THz regime:
    Free electrons (plasmon)
    Lattice vibrations (phonon)
    Spin coupling (magnon)
    ...
  To study these effects, material excitation with THz source.

## Slide 5: Undulator-based THZ source
Undulator parameter:
Challenge to go to so large λTHz.
Helical undulator (symmetric strong natural focusing).
γ = 50 (Eb=25MeV, space charge).
λu = 6cm (compactness).
K0 = 0.75 - 4.9 (for tuning); equals to B0 = 0.09T – 0.88T.
Q = 1nC charge necessary.
Phase locking:
SASE: easy, but no phase locking.
Seeding: THz lasers not quite strong enough.
Comb beam: create bunching before undulator.

## Slide 6: Option 1: Comb beam design
S-band
gun
S-band
ACC
X-band
lineariser
undulator
S/X-band
de-chirper
comb laser
Variable bunch
compressor
Current
Current
smearing due to space charge effect
δ=ΔE/E0
z

## Slide 7: Option 2: Slotted foil based design
Taken from P. Emma et al., PRL 92(7), 2004.
Principle pioneered by SLAC for LCLS.
Create beam tilt, due to energy chirp in dispersive region.
Beam is shot on 15um slotted Be foil.
Emittance is strongly increased where beam hits foil.
Only beam in slit participate to FEL process. Used to create very short X-ray pulses.
Could this be used to create a pre-bunched beam for THz generation?

## Slide 8: Imprint tuning
  Create correct micro-bunch distance for 1 - 4Thz.
  For 4-20 THz tune undulator on higher harmonic.
  Minimum 15 micro-bunches to reach Δf/f0 < 10%.
Compression tuning
Foil tuning
Tuning | via optics | via foil pattern
Imprint | same pattern | changing pattern
Nr. micro-bunches | ≈ 15 | 15 to 60
R56 of optics | changing | 0
Δf/f0 | ≈ 10% | ≈ 10 % to 2.5%
EP (rough) | 90-120 μJ | 140-100 μJ
Factor matters

## Slide 9: 2. Imprint optics

## Slide 10: Minimum slit separation and beam size at foil
D ≠ 0
D = 0
beam
slotted foil
σx,s ≠ 0
σx,s = 0
2σx,s
1. Bunching condition:
d/2 ≥ 3σx,s
d/2 ≥ 1mm (β=2m)
2. Bandwidth condition (10-5%):
2σx > 10d to 20d
2σx > 2cm to 4cm
2σx

## Slide 11: Chicane-type system
Parameter choice:
hmax = 26 (energy chirp, given by de-chirper).
d = 2mm by σx condition.
θ for tuning (bend angle).
L of chicane (only free parameter).
Longer L give smaller bandwidth
For 6.5m, BW ≈ 7%.
Tuning curve (6.5m):
Main effect: bunch compression.
R56 = 4cm to 9.5cm.
Dx = 0.24m to 0.37m.
2σx = 3cm to 4.5cm.
No problem due to σE,incoh smearing (5μm).

## Slide 12: Shorter design 1: optical tuning
Defocusing QP to create large dispersion at foil in short distance
Focusing QP to reduce D’ so that the DP can cancel it.
To have the same trajectory keep all DP strength the same.
Tuning: Change dispersion in middle DPs, via two QPs per arm.
Same performance in about 2m length.
Problem: also the matching will have to be tuned to keep beam size at foil constant.
Detail about optimisation:
  Since h is limited, R56 at full compression is fixed.
  R56 = 2*D*θ
  To have large BW, D has to be large, and θ small.
  Therefore, weaker bends are better.

## Slide 13: Shorter design 2: foil tuning
Optics with dispersion at foil, but R56≈0.
Shape dispersion with QPs.
Tuning: only via changing foil pattern, by moving foil.
Advantages:
Fixed optics.
Easy tuning.
Disadvantages:
Large dispersion (1m) and beam (12cm) necessary. Non-linearities.
QD
QD
QF
QF
DP
DP
foil
2 m
0.4 m
z
x
Dx
1m
z

## Slide 14: Foil for 1-4 THz imprint
Foil for continuous, linear frequency tuning.
For mechanical stability a minimum thickness is necessary (>1mm assumed).
Vertical size arbitrary.
For 4-20 THz, tuning the undulator to higher harmonic.
Easy tuning by moving the foil instead of beam.
1 THz
4 THz
3 THz
2 THz

## Slide 15: Non-linearities
Worry due to large beam size at foil (12cm)
3 issues:
  X: Transverse distortions at foil (RF curvature, lineariser and T166).
  Z: Change of final bunching due to longitudinal distortions.
  δ: Energy spread distortion in undulator due to RF curvature, lineariser and de-chirper.
Lineariser:
  Maybe it is possible to make a optical linearisation.
  Compensate non-linear δ with non-linear de-chirper wakefield.
Studies have started, but not ready for presentation yet.

## Slide 16: 3. Foil design

## Slide 17: Foil effect and material options
Two processes are involved:
  Bremsstrahlung decay chain (E>Ec).
  Ionization (E<Ec).
Effect on beam:
  Energy deposition.
  Angle increase.
Beam energy is in the range of Ec depending on material.
Estimates are available, but more secure to have GEANT4 simulation.
Material | Scattering
Be | weak
Al | moderate
Cu | strong
Fe | strong
W | very strong
ρ
Contacted AD people. The local expert is Helga Holmestad. She provided me kindly with here AD degrader foil setup.

## Slide 18: Foil simulations (GEANT4)
dfoil | ΔW [mJ/bunch] | ΔEmedian [%] | θsc [mrad] | rx= θsc/σxp | ry= θsc/ σyp
Be, 0.1mm | 0.03 | 0.08 | 53 | 1302 | 450
Al, 1mm | 0.42 | 1.51 | 180 | 4461 | 1500
Steel, 1mm | 1.23 | 4.79 | 260 | 6421 | 2266
W, 2mm | 7.96 | 47.37 | 1112 | 27506 | 9145
W, 2mm foil, 4 particles, 1mm slit
Beam cannot be stopped by the foil.
Energy loss is moderate, but huge Δε.
Get rid of particles with collimator.
Controlled emittance spoiling seems to be impossible.
Collimator right after the foil.
Favored choice: steel foil of 1mm.

## Slide 19: Collimator design/simulations
Foil choice:
  Be foil: beam is all over the place (too large θsc)
  Better to use steel foil (produced narrower cone).
Collimator thickness:
  Simplified simulations with a cylinder of material.
  W: <1% energy after 5cm
  Steel: < 1% energy after 15cm
Possible geometric layout:
  Two tungsten plates to collimate only vertically.
  10cm downstream of foil: σysc = 2.6cm
  1cm gap should collimate 96% of the beam.
5cm W block, r=10cm, 100 electrons

## Slide 20
Heating
No cooling mechanism:
  Assuming 1mm steel foil.
  Deposited energy per bunch 1mJ.
  1g Fe + 1mJ => ΔT = 0.5mK.
  Heating of 50 mK/s.
Cooling:
  Heating power 0.79W.
  No convection (vacuum).
  To radiate also 0.79W, ΔT from 20° to 69° degree or oxidized steel.
  But heat will also spread via conduction.
Conclusion:
  Foil will warm up a bit (maybe slightly hot).
  Expansion for ΔT=50 is about 1μm.
Other issues (to be studied in more detail)
Activation:
  Discussion with CERN RP expert Robert Fröschl.
  There will be some activation, but surely moderate (low energy electrons, low Iavg).
  It has bee okay at LCLS at much higher energy (4.54 GeV).
Ablation:
  There are OTRs all over the place at all energies.
  There has been no problem at LCLS at much higher energy 4.54 GeV.
Transition radiation:
  Fun to look into, but corresponding wake was no problem at LCLS.

## Slide 21: 4. Conclusions

## Slide 22: Summary of slotted foil design
A design of a THz source based on an 26 MeV electron beam and the slotted foil technique was presented.
Micro-bunching is created by removing parts of the beam with the help of a foil.
Two imprint optics were studied, were the one without bunch compression seems to be favorable:
  No change of optics for tuning.
  Creation of fully bunched beams.
Foil was designed with the help of GEANT4 simulations:
  Foil will in any way not stop the particles directly.
  1 mm steel foil seems to be optimal at the moment.
  Two 5cm long tungsten plates 10cm downstream of foil should collimate 96% of the spoiled beam.
There seem to be no show stoppers so far and the design looks rather easy.

## Slide 23: Comparison of designs
 | Comb beam | Slotted foil (option 2)
Injector: | Additional laser hardware. Tricky to find proper working point. | Standard injector
Bunching: | Mainly stretching of energy modulation (no bunching). But parameter seem okay. | Easy tuning Fixed optics Challenging design and setup of imprint optics.
Undulator: | A bit longer, since only energy modulation. | Rather shorter, since fully bunched beam.
Length: | About 15m. | About 13m.
Comments: | Optical linearisation is difficult, since tuning with bunch compressor. | Maybe optical linearisation instead of X-band lineariser.

## Slide 24: Possible test scenario at CLEAR
Injector:
Much simpler laser system than for Comb beam.
If 50MeV beam instead of 25MeV at SwissFEL.
X-band lineariser probably necessary.
Imprint optics:
Imprint optics, has a dogleg shape for extraction.
Only h/2 and δ/2 compared to SwissFEL. Twice Dx is necessary (3m). Should be possible if design is a bit stretched.
Undulator and de-chirper:
Same de-chirper and undulator as for SwissFEL
Space charge conditions a bit relaxed.
THz frequency is changed from 1-20 THz to 4-80 THz.
But same foil can be used since undulator can be tuned to higher harmonic.

## Slide 25: Further steps
GENESIS simulations:
  Most important task to finally confirm feasibility and quantify the properties of the THz radiation.
  Have been started, but there was a problem with the space charge calculation.
Design improvements:
  Finish the study of nonlinearities.
  Include resistive wakes in de-chirper and get better wake.
  Check if dielectric de-chirper could be shorter than 3.5m.
  Check transition radiation effect of foil.
Detailed optics design (MADX) of imprint optics.
Tracking studies and final optimisation.

## Slide 26: Thank you for your attention!