## Slide 1: SHIELD for 10gr exposure with cooling system
N. D’Ambrosio – V. Tioukov

## Slide 2: SHIELD for 10 gr exposure
Area in Hall B assigned by LNGS
Structure defined by Valery and Nicola and technical project finalised by D. Orlandi (LNGS engineer )
Optimize the use of polyethylene blocks ( from Darkside), use of the OPERA lead sheets and minimize the costs for the structure
Steel structure defined, tomorrow meeting with Orlandi to define the final optimization and schedule for construction
Network connection with temperature log system accessible by network
(System ready)
Optimize the thermal insulation path of the connection tubes
(refrigeration liquid and Nitrogen)

## Slide 3
In this area assigned 5 x 5 m2 to NEWS
XENON
LUNA
Ex BAM Tunnel
NEWS LAB
HALL B
Polyetilene blocks

## Slide 4
Steel structure
with lead sheets
Nitrogen box
(avoid umidity and Radon)
About 35x35x 40 cm3
Cooling system
40 cm
80 cm
244 cm
About 135 cm
SHIELD
SCHEMATIC
view
Connection tubes
and temperature sensors cables
(cooling liquid and nitrogen
circulation)
About 6 connections
…around 4 cm2

## Slide 5
Vista da sopra, sezione C-C
Interno 40x40x80 cm3
La struttura di acciaio
A
A

## Slide 6
SHIELD : Steel structure
10cm
Side view
OPERA lead sheets
(..also for TOP and Bottom)
20 cm
2 lead sheets
Here…
Lead or steel

## Slide 7: Apprximate material budget
Polyethylene
Total polyethylene weight – about 3000-4000 kg
Lead
4 walls 10x92x140 cm - about 1400 kg/wall
bottom 10x80x80 cm
top 10x80x80 cm - about 700 kg of lead, about 1000 – 1100 kg with polyethylene
Totale lead weight: 7000 kg