## Slide 2: CERN IT-Storage Strategy Outlook Alberto Pace, Luca Mascetti, Julien Leduc

## Slide 3: CERN IT-Storage Group

## Slide 4: Storage Services
TSM
CASTOR
AFS
ceph
NFS
CVMFS
RBD
S3
SSD

## Slide 5: Vision for CERN Storage
Build a flexible and uniform
infrastructure
Maintain and enhance (grid) data management tools

## Slide 6: Vision for CERN Storage
  Unlimited storage for LHC experiments, at exabyte scale
    EOS Disk pools (on-demand reliability, on-demand performance)
      currently 165 PB deployed
    CERN Tape Archive (high reliability, low cost, data preservation)
      currently 190 PB stored
  A generic home directory service – currently 3 PB
    To cover all requirements of personal storage
    Shared among all clients and services
    Fuse mounts, NFS and SMB exports,
    Desktop Sync and Web/HTTP/DAV Access

## Slide 7: EOS Development Strategy
Evolve flexible storage infrastructure as scale-out solution towards exabyte scale
  one storage – many views on data – analysis/analytics service integration
  suitable for LAN & WAN deployments
  enable cost optimized deployments
Evolve file-system interface /eos
  multi-platform access using standard protocol bridges CIFS, NFS, HTTP
Evolve namespace scalability
  scale-out implementation
Evolve scale-out storage back-end support
  object disks, object stores, public cloud, cold storage

## Slide 8
Remote access APIs ⇒ filesystem API
Meta data scale-up ⇒ scale-out
  in-memory namespace ⇒ in-memory scale-up namespace cache + persistency in scale-out KV store
EOS Challenges
2nd key project: EOS Citrine & QuarkDB
1st key project: EOS FUSE rewrite

## Slide 9: CERNBox
Strategic service to access EOS storage
  Unprecedented performances
    LHC experiments data workflows
  Access to all CERN physics (and accelerator) bulk data
  Disconnected / Offline Work
  Easy Sharing model
  Main Integration Access Point
    SWAN, Office Online, …
  Checksum and consistency

## Slide 10: Architecture
Disk Pools (EOS)
Sync client (CERNBox)
http sync protocol
(offline access)
(online access)
Web browser access
(web access)
SMB, xroot
CERNBOX web interface
Clusters (Batch, Plus, Analytics, …)
Applications
(Page 1, LHC Logging, …)
Tape
Archive
http, fuse
Webdav, NFS,
Physicists
Engineers
Administrative staff

## Slide 11: Data Archiving evolution
Preserving the past …
  Protect against bit rot (data corruption, bit flips, environmental elements, media wear out and breakage …)
  Migrate data across technology generations, avoiding obsolescence
    Some of our data is 40 years old
Data written to tape 2008-2016
Chart: 
| 2016.0 | 2017.0 | 2018.0 | 2019.0 | 2020.0 | 2021.0 | 2022.0
Total Data (PB) | 200 | 300 | 400 | 410 | 420 | 570 | 720
… and anticipating the future
  2017-2018: 100PB/year
  2021++ : 150PB/year

## Slide 12: Storage Services Evolution
TSM
ceph
NFS
CVMFS
RBD
S3
SSD
CASTOR
CTA

## Slide 13: Data Archiving: Evolution
EOS + tape …
  EOS is the strategic storage platform
  Tape is the strategic long term archive medium
EOS + tape =
  Meet CTA : the CERN Tape Archive
  Streamline data paths, software and infrastructure
Notes: CTA will provide optimise

## Slide 14: What is CTA?
  CTA is
  A tape backend for EOS
  A preemptive tape drive scheduler
  A clean separation between disk and tape
EOS disk server
EOS disk server
EOS disk server
CTA tape server
CTA tape server
Central CTA instance
CTA
front-end
EOS
namespace and redirector
Tape file catalogue, archive / retrieve queues, tape drive statuses, archive routes and
mount policies
Scheduling information
and tape file locations
Tape drive
Tape drive
Tape drive
Tape drive
Tape library
One EOS instance
per experiment
Archive and retrieve requests
Archive and retrieve requests
Tape files appear in EOS namespace as replicas.
EOS workflow engine glues EOS to CTA
CTA tape server
CTA metadata
Files
Files

## Slide 15: What is CTA?
    EOS plus CTA is a “drop in” replacement for CASTOR
    Same tape format as CASTOR – only need to migrate metadata
EOS + CTA
Experiment
Tape
libraries
EOS
Files
Files
Files
Files
CASTOR
Experiment
Tape
libraries
EOS
Files
Files
Files
Files
Current deployments with CASTOR
Future deployments with EOS plus CTA

## Slide 16: When is CTA?
Mid 2018
End 2018
Ready for small experiments
Ready for LHC experiments
Mid 2017
First release for additional copy use cases

## Slide 17: CTA outside CERN
CTA will be usable anywhere EOS is used
CTA could go behind another disk storage system but would require contributing some development:
  The disk storage system must manage the disk and tape lifecycle of each file
  The disk storage system needs to be able to transfer files from/to CTA (currently xroot - CTA can easily be extended to support other protocols)
CTA currently uses Oracle for the tape file catalogue
  CTA has a thin RDBMS layer that isolates Oracle specifics from the rest of CTA
  The RDMS layer means CTA could be extended to run with a different database technology

## Slide 18: Backup Service
TSM cost is proportional to backed up volume
  Minimize backup volume in view of upcoming license retendering
Ongoing efforts to limit annual growth rate: 24% (50% in the past):
  Moved AFS backups to CASTOR
  Working with the two other large backup customers
Backup Service total data since 2012

## Slide 19
Question?