## Slide 2: PSB Recombination kickers rise time (Update January 2017)
L. Sermeus TE/ABT/FPS

## Slide 3: Contents
Installed BT.KFAs systems and measured kick (quick reminder).
Tests performed in the laboratory up to now.
PSB LIU kickers roadmap (update).

## Slide 4: BT.KFA10 as installed
1 vacuum tank installed in ~1970.
4 magnets (2 per transfer line, 2 types) designed for 800 MeV beam deflection.
Glued ferrite C cores of 4L1 type (not optimum for fast kickers and vacuum performance).
No spare.
1 pulse generator per line supplying 2 magnets in parallel.
PFL voltage for 1.4GeV: ~43kV (at 2GeV: ~56kV)
Layout for 1 transfer line

## Slide 5: BT1.KFA10 kick (measured waveform at 50 kV)
Kick rise time: |  |  | (5-95)% | 100ns
 |  |  | (2-98)% | 125ns
Kick measurement in the PSB with a small inductive loop hidden in magnet ground conductor (unknown frequency response , probably not very good)
LIU:105ns
for LHC
Scope: 100MHz BW, 13 bits vertical resolution

## Slide 6: BT4.KFA10 kick (measured waveform at 50 kV)
Kick rise time: |  |  | (5-95)% | 103ns
 |  |  | (2-98)% | 122ns
Scope: 100MHz BW, 13 bits vertical resolution
Kick measurement in the PSB with a small inductive loop hidden in magnet ground conductor (unknown frequency response , probably not very good)
LIU:105ns
for LHC

## Slide 7: BT2.KFA20 present system layout
One generator supplying two magnets in parallel.
Magnets equipped with CMD5005 ferrite blocks.
Magnets are charged with the PFLs up to 36.5 kV (breakdown limit is 37 kV)
LIU 2GeV requires 36.5kV.

## Slide 8: BT2.KFA20 kick (measured waveform at 27 kV)
Kick rise time: |  |  | (5-95)% | 78ns
 |  |  | (2-98)% | ~94ns (LIU 105ns for LHC)
 |  |  | (1-99)% | 270ns
Kick measurement in the PSB with a matched strip-line (Scope: 100MHz BW, 13 bits)

## Slide 9: BT2.KFA20 spare tank in B867 SAL5 test cage. BT.KFA10 test 1 system layout
One generator supplying only one magnet connected the same way as KFA10.
Two cables connected for 12.5Ω impedance.
Magnets equipped with CMD5005 ferrite type.
Filters disconnected.
PFL voltage: 56kV (required for 2GeV beam)
Magnet current: ~4500A (=thyratron current)
Disconnected
First simple layout tested to check PSPICE model

## Slide 10: BT.KFA10 test 1 in B867: kick
Normalised kick of 1 magnet. Measured with strip-line probe – Simulated with PSPICE (~1000 components). Discrepancy in the rise due (I think) to magnet conductor skin effect not modelled in PSPICE due to convergence problems.
Rise (2-96.2)%
Measured
~95ns
Calculated
~95ns
First peak 96.2%
100%
Pre-pulse ripple due to 2-gap thyratron switching
Kick measurement with a matched strip-line (large bandwidth)

## Slide 11: BT.KFA10 test 2 in B867: kick
One generator supplying only one magnet connected the same way as KFA10.
Two cables connected for 12.5Ω impedance.
Magnets equipped with CMD5005 ferrite type.
Filters disconnected. Saturating inductor at magnet input.
PFL voltage: 56kV (required for 2GeV beam)
Magnet current: ~4500A (=thyratron current)
Disconnected
First layout with added saturating inductor (July 2016)

## Slide 12: BT.KFA10 test 2 in B867: kick
Normalised kick of 1 magnet. Measured with strip-line probe – Simulated with PSPICE
Discrepancy in the rise due (I think) to magnet conductor skin effect not modelled in PSPICE + saturating inductor behaviour.
Rise (2-96.6)% (2-95.6)%
Measured
~91ns
Calculated
97.6ns
First peak 96.6%
First peak 95.6%
100%
Pre-pulse ripple cancelled
Undershoot
92.3%

## Slide 13: BT.KFA10 test 4 in B867: kick
One generator supplying only one magnet connected the same way as KFA10.
Two cables connected for 12.5Ω impedance.
Magnets equipped with CMD5005 ferrite type.
Filters added. Saturating inductor at magnet input.
PFL voltage: 56kV (required for 2GeV beam)
Magnet current: ~4500A (=thyratron current)
Disconnected
First layout with added saturating inductor, magnet filters and MS cathode filter

## Slide 14: BT.KFA10 test 4 in B867: kick
Normalised kick of 1 magnet. Measured with strip-line probe – Simulated with PSPICE
This is the best rise time we could achieve with a reasonable overshoot.
Rise (2-98)%
Measured
~89ns
Calculated
90ns
First peak 102.3%
First peak 102.5%
100%
Pre-pulse ripple cancelled
Undershoot
99.2%

## Slide 15: BT.KFA10 test 8 in B867: kick
One generator supplying two magnets connected the same way as KFA10.
Four cables connected for 6.25Ω impedance.
Magnets equipped with CMD5005 ferrite type.
Filters added. Saturating inductor at magnet input.
PFL voltage: 56kV (required for 2GeV beam)
Magnet current: ~4500A (thyratron current: 9000A)
Disconnected
Two magnets connected with saturating inductor and filters, MS cathode filter.

## Slide 16: BT.KFA10 test 8 in B867: kick of upstream magnet
Normalised kick of upstream magnet. Measured with strip-line probe – Simulated with PSPICE
The low system impedance increases the influence of the parasitic inductances, mainly the switch inductance.
Rise (2-98)%
Measured
~107ns
Calculated
117ns
First peak 98.4%
First peak 100%
100%
Pre-pulse ripple cancelled
Undershoot
97.8%
Hole 91.5% due to thyratron inductance

## Slide 17: BT.KFA10 test 7 in B867: kick
One generator supplying two magnets connected the same way as KFA10.
Four cables connected for 6.25Ω impedance.
Magnets equipped with CMD5005 ferrite type.
Filters added. Saturating inductor at magnet input.
PFL voltage: 56kV (required for 2GeV beam)
Magnet current: ~4500A (thyratron current: 9000A)
Disconnected
Two magnets connected with saturating inductor and filters, MS cathode&anode filters.

## Slide 18: BT.KFA10 test 7 in B867: kick of upstream magnet
Normalised kick of upstream magnet. Measured with strip-line probe – Simulated with PSPICE
Rise (2-98)%
Measured
~111ns
Calculated
112ns
First peak 98.4%
First peak 100%
100%
Pre-pulse ripple cancelled
Hole 94%

## Slide 19: BT.KFA10 test in B867: work to be continued
Present status:
Optimisation of kick rise time and flat-top not finished but it appears that the 105ns figure will not be met. 120ns seems to be more realistic to limit the ripple to ±2%. This value will confirm the BT.KFA10 measurements in the PSB.
Next step: add two filters to the main switch output.
Possible solution: add a second main switch to the generator in order to half the switch current and double the impedance of each branch.
The estimated cost is about 160kCHF per generator.
Another option: add a saturating inductor at the main switch output to help the thyratron switching. To be tested without guarantee. A gain of 5 to 10ns is expected but the ripple might increase.
Estimated cost: ~15kCHF per generator.

## Slide 20: BT.KFA10 test in B867: work to be continued
Dual main switch configuration. This is also valid for BT2.KFA20.
Total additional cost would be ~480kCHF for the BT.KFAs.

## Slide 21: PSB-LIU kicker roadmap update
The updated plans for PSB-LIU kickers are:
Measurements in the lab to be continued.
Quick decision to be taken to allow or not ~480kCHF to produce 3 new main switches.
- Production of a spare BT.KFA10 with CMD5005 ferrite blocks. Expected to be ready end 2017. Installation in the ring during LS2.
- Re-cabling of BT2.KFA20 in BT.KFA10 configuration to reduce the risk of magnet breakdown. This was not in the LIU PSB kickers initial plan (only an option).
(- Production of a spare BE.KFA14L1. Expected to be ready end 2017)