## Slide 1: MR-ToF MS prototype for ISOLDE
Frank Wienholtz
- CERN / University of Greifswald -
ISCC 2017-02-07
frank.wienholtz@cern.ch
What is an MR-ToF MS and why do we want one?
Current performance and possible improvements
Constrains at ISOLDE
Test with ISCOOL and ISOLTRAP

## Slide 2
What is a
Multi-reflection time-of-flight Mass spectrometer
and why do we want one?

## Slide 3
ISOLTRAP’s MR-ToF MS

## Slide 4
ISOLTRAP’s MR-ToF MS
After 1000 revs in MR-ToF (R=115k)
Mößbauer spectroscopy

## Slide 5
ISOLTRAP’s MR-ToF MS
After 1000 revs in MR-ToF (R=115k)
Mößbauer spectroscopy
Collection of medical isotopes

## Slide 6
ISOLTRAP’s MR-ToF MS
After 1000 revs in MR-ToF (R=115k)
Mößbauer spectroscopy
Collection of medical isotopes
TISD yield checks

## Slide 7
ISOLTRAP’s MR-ToF MS
After 1000 revs in MR-ToF (R=115k)
Mößbauer spectroscopy
Collection of medical isotopes
TISD yield checks
Release curve

## Slide 8
ISOLTRAP’s MR-ToF MS
After 1000 revs in MR-ToF (R=115k)
Mößbauer spectroscopy
Collection of medical isotopes
TISD yield checks
Release curve
A=70 beam analyses – 70Ni Collaps

## Slide 9
ISOLTRAP’s MR-ToF MS
After 1000 revs in MR-ToF (R=115k)
Mößbauer spectroscopy
Collection of medical isotopes
TISD yield checks
Release curve
A=70 beam analyses – 70Ni Collaps
Support for the Penning trap mass measurements
75Ga
75Cu
molecular contamination

## Slide 10
ISOLTRAP’s MR-ToF MS
After 1000 revs in MR-ToF (R=115k)
Mößbauer spectroscopy
Collection of medical isotopes
TISD yield checks
Release curve
A=70 beam analyses – 70Ni Collaps
Support for the Penning trap mass measurements
75Ga
75Cu
molecular contamination
Decay spectroscopy

## Slide 11
in-trap lift
capture and ejection with one electrode
 simple technique, stable mirror potentials
decouple MR-ToF-MS and adjacent beamline
 independent optimization
adjust ions’ kinetic energy
 ToF focusing, max. mass resolving power
Wolf et al., IJMS 313, 8 (2012)
Injection
Storage
Ejection
 only one parameter to adjust
1
2
3
133Cs, 1000 rev.
The MR-ToF-MS at ISOLTRAP

## Slide 12
Necessary mass resolving power for separation of n-rich Zn beams
Notes: Both plots new

## Slide 13
Ion energy: 2.1keV
Max. mirror potential: 4kV
Pressure: 5E-9mbar
Longitudinal emittance: 100nseV
Transversal emittance: 5 mm mrad
mass resolving power (FWHM)
m/∆m=100 000 at 18ms
m/∆m=300 000 at 35ms
transmission
≈50% at 30ms
ion capacity for multiple species
≈100 000 per second
contamination suppression (BNG)
4 orders of magnitude
operation and tuning
only one parameter to adjust
simple operation
revolutions for 133Cs
The MR-ToF-MS at ISOLTRAP - Performance
Ion energy: 30keV
Max. mirror potential: 60kV
Pressure: 1E-8mbar
Bunching with ISCOOL:
Longitudinal emittance: 500nseV
Transversal emittance: 2-4 mm mrad
Chopping: has to be tested
Decrease time needed for separation by about factor 4
Transmission should be improved
Optimize mirror electrodes and ion optics for large transversal emittance
Increase ion capacity

## Slide 14
ISOLDE MR-ToF-MS

## Slide 15
ISOLDE MR-ToF-MS

## Slide 16
ISOLDE MR-ToF-MS

## Slide 17
ISOLDE MR-ToF-MS
vertical
horizontal

## Slide 18
Tests with the ISCOOL and ISOLTRAP
Shoot the ISCOOL beam through the ISOLTRAP buncher (transmission mode)
Perform beam diagnostic with ISOLTRAP’s tools
  Minimal longitudinal emittance / ToF peak width?
  Investigate fast ions?
Determine the transmission
  through ISCOOL  50%?
  through ISOTLRAP buncher?
  through MR-ToF MS?
Inject ISOOL bunches directly into the MR-ToF MS
  Time scale?
  Maximal R?
  Mirror retune?
  Efficiency of the hole process?

## Slide 19: Acknowledgements
N. Althubiti, P. Ascher, G. Audi, D. Atanasov, D. Beck, K. Blaum, G. Bollen, Ch. Borgmann, M. Breitenfeldt, R. B. Cakirli, T. Cocolios, S. Eliseev, T. Eronen, S. George, F. Herfurth, A. Herlert, D. Kisler, M. Kowalska, S. Kreim, J. Kluge, Yu. A. Litvinov, D. Lunney, M. Mougeot, V. Manea, E. Minaya-Ramirez, S. Naimi, D. Neidherr, M. Rosenbusch, A. de Roubin, L. Schweikhard, F. Wienholtz, M. Wang, A. Welker, R. Wolf, K. Zuber, S. Schwarz
ISOLDE Target
and Technical Group
Grants No.:
05P12HGCI1
05P12HGFNE
http://isoltrap.web.cern.ch
Ulli Köster
IS534 and IS598
Collaboration

## Slide 20
Limitations – peak coalescence

## Slide 21
The MR-ToF-MS at ISOLTRAP – peak coalescence
“Many” ions in one bunch can lead to peak coalescence due to Coulomb interaction
  ToF mass measurements difficult BUT separation still possible
Example: A=152 beam
MCP voltage 2kV
Around 26 ions/shot

## Slide 22
The MR-ToF-MS at ISOLTRAP – peak coalescence
“Many” ions in one bunch can lead to peak coalescence due to Coulomb interaction
  ToF mass measurements difficult BUT separation still possible
Example: A=152 beam
MCP voltage 2kV
Around 26 ions/shot
MCP voltage to 1.8kV
Increase bg by x50

## Slide 23
The MR-ToF-MS at ISOLTRAP – peak coalescence
“Many” ions in one bunch can lead to peak coalescence due to Coulomb interaction
  ToF mass measurements difficult BUT separation still possible
Example: A=152 beam
MCP voltage 2kV
Around 26 ions/shot
MCP voltage to 1.8kV
Increase bg by x50
Increase bg by x500

## Slide 24
The MR-ToF-MS at ISOLTRAP – peak coalescence
“Many” ions in one bunch can lead to peak coalescence due to Coulomb interaction
  ToF mass measurements difficult BUT separation still possible
Example: A=152 beam
MCP voltage 2kV
Around 26 ions/shot
MCP voltage to 1.8kV
Increase bg by x50
Increase bg by x500
Separation still possible
Allows cleaning with
higher throughput

## Slide 25
Resolving power <-> cleaning of the Zn-beam

## Slide 26
Mass resolving power – neutron rich Zn beams
Wolf et al., IJMS 349-350, 123 (2013);
Notes: Both plots new

## Slide 27
Mass resolving power – neutron rich Zn beams
Notes: Both plots new

## Slide 28
ion source
focus
in-trap lift
M1
M2
detector
Wolf et al., IJMS 313, 8 (2012)
In-trap potential lift time focussing

## Slide 29
ion source
focus
in-trap lift
M1
M2
detector
Wolf et al., IJMS 313, 8 (2012)
In-trap potential lift time focussing

## Slide 30
ΔE
ion source
focus
in-trap lift
M1
M2
detector
Wolf et al., IJMS 313, 8 (2012)
In-trap potential lift time focussing

## Slide 31
ion source
focus
in-trap lift
M1
M2
detector
focus
+i
n=0
n=i
ΔE
ΔE
Wolf et al., IJMS 313, 8 (2012)
In-trap potential lift time focussing

## Slide 32
ion source
focus
in-trap lift
M1
M2
detector
focus
focus
+i
+j
n=0
n=i
n=i+j
ΔE
ΔE
Wolf et al., IJMS 313, 8 (2012)
In-trap potential lift time focussing