## Slide 1: Sensitivity of integrated luminosity for beam parameter change
F. Antoniou, R. De Maria, S. Fartoukh, N. Karastathis, Y. Papaphilippou, D. Pellegrini, K. Sjobaek
WP2 meeting, 17/01/2017

## Slide 2: Outline
Xing angle choice during levelling
Impact on levelling (β* vs. separation)
Experience 2016:
  Luminosity lifetime, blow-up, impact on estimated performance
  Levelling tests
  Availability
Projection on integrated luminosity performance

## Slide 3: Global DA scanning of parameters
Tracking set-up:
  HL-LHC optics v1.2, half available crab voltage
Octupoles set to 0, chromaticity of 3, nominal tunes
IP1, IP5 and IP8 head-on, IP2 seperated (halo collisions)
Assuming constant (round) emittance of 2.5μm
Tracking with SixTrack for 106 turns and estimating DA (minimum over 5 angles)
Scanning of crossing angle vs. β* and vs. separation, for various intensities
Superimposing luminosity curves for the various parameters
S.Fartoukh, N. Karastathis, D. Pellegrini

## Slide 4: Global DA scanning of parameters
Tracking set-up:
  HL-LHC optics v1.2, half available crab voltage
Octupoles set to 0, chromaticity of 3, nominal tunes
IP1, IP5 and IP8 head-on, IP2 separated (halo collisions)
Assuming constant (round) emittance of 2.5 μm along stable beams
Tracking with SixTrack for 106 turns and estimating DA (minimum over 5 angles)
Scanning of crossing angle vs. β* and vs. separation, for various intensities
Superimposing luminosity curves for the various parameters
Target DA of 6 σ, as simulation scenario is optimistic (no errors, no octupoles, low chromaticity,…)
S.Fartoukh, N. Karastathis, D. Pellegrini

## Slide 5: Start of levelling Nb = 2.2 x 1011
Full crossing angle could be reduced to 440 μrad (~19.4 σ separation @ 65 cm β*), keeping the 6 σ DA and the luminosity at 5 x 1034 cm-2 s-1
Even for min. β* of 20 cm @ 510 μrad, DA ~5.5 σ
For 7.5 x 1034 cm-2 s-1, the leveling could start at 40 cm with a crossing angle of 480 μrad (16.6 σ)
S.Fartoukh, N. Karastathis, D. Pellegrini

## Slide 6: During levelling, Nb = 1.9 x 1011
Full crossing angle could be reduced to 340 μrad (~13.1 σ separation @ 50 cm β*), keeping the 6 σ DA and the luminosity at 5 x 1034 cm-2 s-1
For 7.5 x 1034 cm-2 s-1, a DA of 6 σ is obtained with a crossing angle of 440 μrad (13.2 σ @ 30 cm)
S.Fartoukh, N. Karastathis, D. Pellegrini

## Slide 7: During levelling, Nb = 1.6 x 1011
Full crossing angle could remain at 340 μrad (~11 σ separation @ 35 cm β*), keeping the 6 σ DA and the luminosity at 5 x 1034 cm-2 s-1
For 7.5 x 1034 cm-2 s-1, a DA of 6 σ is obtained with a crossing angle of 430 μrad (10.5 σ @ 20 cm, i.e. reaching the end of β* levelling)
S.Fartoukh, N. Karastathis, D. Pellegrini

## Slide 8: End of levelling, Nb = 1.275 x 1011
Full crossing angle should be increased to 380 μrad (~9.3 σ separation @ 20 cm), keeping 6 σ DA and luminosity of 5 x 1034 cm-2 s-1
S.Fartoukh, N. Karastathis, D. Pellegrini

## Slide 9: Extra levelling, Nb = 1.25 x 1011
Some extra levelling time can be gained by levelling with the crossing angle at DA close to 6 σ and constant β* of 20 cm
S.Fartoukh, N. Karastathis, D. Pellegrini
Notes: May further include a small crossing angle vs

## Slide 10: A few remarks
Crossing angle can be reduced during levelling to 6 σ DA, reducing pile-up density and triplet irradiation
Full crabbing can be achieved with two cavities (max kick of 380 μrad) for currents < 2 x 1011 almost through the whole levelling process
Some small leveling time (and performance) can be gained @ 20 cm, by levelling with the crossing angle
Need to complement the DA simulations down to 15 cm especially for the ultimate scenario and span also lower crossing angles

## Slide 11: Performance
Estimate impact in integrated luminosity and pile-up density for nominal and ultimate, for mentioned “crossing adaptive levelling”
X. Buffat, HL-LHC meeting 2016

## Slide 12: Separation levelling Nb = 2.2 x 1011
β* kept constant while levelling the luminosity by separation
For 5 x 1034 cm-2 s-1, the leveling could start at 1.8 σ separation with a large crossing angle of 550 μrad (13.4 σ)
For 7.5 x 1034 cm-2 s-1, the leveling could start at 1.2 σ with a crossing angle of 580 μrad (14.2 σ)
S.Fartoukh, N. Karastathis, D. Pellegrini

## Slide 13: Separation levelling Nb = 1.9 x 1011
DA seems quite independent on separation
For both nominal (1.6 σ separation) and ultimate (1 σ separation), a crossing of 500 μrad (12.2 σ) maintains DA
S.Fartoukh, N. Karastathis, D. Pellegrini

## Slide 14: Separation levelling Nb = 1.6 x 1011
DA seems again quite independent on separation
For 5 x 1034 cm-2 s-1, the leveling could continue with a 1.2 σ separation with a crossing angle of 450 μrad (11 σ)
For 7.5 x 1034 cm-2 s-1, the leveling can stop @ a crossing angle of 440 μrad (10.8 σ)
S.Fartoukh, N. Karastathis, D. Pellegrini

## Slide 15: Separation levelling Nb = 1.275 x 1011
Separation levelling for nominal scheme ends @ 380 μrad (~9.3 σ)
S.Fartoukh, N. Karastathis, D. Pellegrini

## Slide 16: Separation levelling Nb = 1.2 x 1011
The same crossing angle levelling scheme can be pursued as before to gain some extra levelling time and optimize performance
S.Fartoukh, N. Karastathis, D. Pellegrini

## Slide 17: Levelling experience in 2016
  Levelling by separation demonstrated in test fills during 2016
    Fine tune adjustments and reduction of octupoles/chromaticity necessary to improve lifetime during levelling
  Satisfying possible request of experiments or when reaching cryogenics’ limit
  Changing X-angle from fill-to-fill (adapt H/V emittance ratio or increase peak luminosity) or levelling during stable beams (range of 60 μrad in X/2-angle)
F.Antoniou
D. Pellegrini

## Slide 18: Beam losses
F.Antoniou, Evian 2016

## Slide 19: Beam losses
F.Antoniou, Evian 2016

## Slide 20: Expected Emittance blow-up
F.Antoniou

## Slide 21: Observed Emittance blow-up
F.Antoniou

## Slide 22: Observed Emittance blow-up
F.Antoniou

## Slide 23: Extra Emittance blow-up
F.Antoniou

## Slide 24: Extra Emittance blow-up
F.Antoniou

## Slide 25: Luminosity loss
F.Antoniou

## Slide 26: Availability

## Slide 27: Remarks
Based on observation from 2016
  Estimate luminosity evolution for HL-LHC scenarios by assuming an extra blow-up growth rate based on the data
    Correlated with brightness?
  Including realistic evolution from injection to stable beams
  Including availability observed in 2016

## Slide 28: Impact of LHCb polarity - octupoles

## Slide 29: Effect of octupoles and LHCb
Tune scans for 550A octupole and LHCb on with good polarity, end of levelling parameters, nominal scheme
DA quite limited…
N. Karastathis, D. Pellegrini

## Slide 30: Effect of octupoles and LHCb
Tune scans for 0 octupole and LHCb on with good polarity, end of levelling parameters, nominal scheme
Recovering DA towards the diagonal
N. Karastathis, D. Pellegrini

## Slide 31: Effect of octupoles and LHCb
Tune scans for -550 octupole and LHCb off, end of levelling parameters, nominal scheme
DA even more improved
N. Karastathis, D. Pellegrini

## Slide 32: Effect of octupoles and LHCb
Tune scans for -550 A octupole and LHCb on, with “good polarity” end of levelling parameters, nominal scheme
DA degraded especially close to 3rd and 10th order resonances
N. Karastathis, D. Pellegrini

## Slide 33: Effect of octupoles and LHCb
Tune scans for -550 A octupole and LHCb on, with “bad polarity” end of levelling parameters, nominal scheme
DA degraded mostly close to 10th order resonances
N. Karastathis, D. Pellegrini

## Slide 34: Summary

## Slide 35: Thanks for your attention