## Slide 1: ALICE Upgrade for Run 3 and Run 4 L. Betev

## Slide 2: CERN Schedule
LS2 2019-2020
  Upgrades of ALICE and LHCb
LS3 2024-2026
  Upgrades of ATLAS and CMS (HL-LHC)
ALICE upgrade ready in Spring 2021 – 4 years from now, fits well with the CERN openlab next project phase
LS1 Run 2 LS2 Run 3
4 years

## Slide 3: ALICE O2 in a nutshell
New computing system
Read-out the data of all interactions
Compress these data intelligently by online reconstruction
One common online-offline computing system: O2
Paradigm shift compared to approach for Run 1 and 2
Baseline correction and zero suppression
Data volume reduction by zero cluster finder. No event discarded.
Average compression factor 6.6
Unmodified raw data of all interactions shipped from detector to online farm in triggerless continuous mode
Asynchronous (few hours) event reconstruction with final calibration
HI run 3.3 TByte/s
Data Storage: 1 year of compressed data
Bandwidth: Write 90 GB/s Read 90 GB/s
Capacity: 60 PB
90 GByte/s
Tier 0, Tiers 1 and
Analysis Facilities
20 GByte/s
Data volume reduction by online tracking. Only reconstructed data to data storage.
Average compression factor 5.5
500 GByte/s
90 GByte/s
Requirements
LHC min bias Pb-Pb at 50 kHz ~100 x more data than during Run 1
Physics topics addressed by ALICE upgrade
  Rare processes
  Very small signal over background ratio
  Needs large statistics of reconstructed events
  Triggering techniques very inefficient if not impossible
50 kHz > TPC inherent rate (drift time ~100 µs) Support for continuous read-out (TPC)
  Detector read-out triggered or continuous

## Slide 4: Data flow & processing (1)
O2/T0/T1
FLPs
EPNs
FLPs
Detectors electronics
Detector data samples
synchronized
by heartbeat triggers
Buffering
TPC
Detector reconstruction
e.g. track finding
Raw data input
Data Reduction 0
e.g. clustering
Local processing
Time Frame building
Frame dispatch
Global processing
TRD
Sub-Time Frames
Partially compressed
sub-Time Frames
Full Time Frames
Compressed Time Frames
Data Reduction 1
…
Trigger and clock
Calibration 0
on local data,
ie. partial detector
Calibration 1
on full detectors
e.g. space charge distortion
T0/T1
Archive
Time slicing
O(100)
O(1000)
Local aggregation
Storage
Quality Control
Sub-Time Frames
Time Frames
Compressed Time Frames
AOD
QC
QC
Tagging
Synchronous
QC data
ITS
…
CTF
AOD
Storage
Load balancing & dataflow regulation
First-Level Processors (FLPs)
Event Processing Nodes (EPNs)

## Slide 5: Data flow & processing (2)
O2/T0/T1
Reconstruction
passes
and event extraction
Compressed Time Frames
T0/T1
Archive
Analysis
Storage
T2
Simulation
CTF
Simulation
AOD
O(10)
Condition & Calibration Database
Quality Control
Sub-Time Frames
Time Frames
Compressed Time Frames
AOD
CCDB Objects
QC
Asynchronous
QC data
CTF
AOD
Event Summary Data
Analysis Object Data
Analysis Facilities
Storage
Histograms,
trees
O(1)
Analysis
AOD
Storage
Reconstruction
Event building
AOD extraction
Compressed Time Frames
O2/T0/T1
O(1)
Event extraction
Tagging
Global
reconstruction
QC
ESD, AOD
AOD extraction
Calibration 2
ESD, AOD

## Slide 6: Challenges
Rates to storage – write 90GB/sec , read 20GB/sec out (+ delta)
Capacity – 60PB in a single instance (first year)
High availability – on the critical path for data taking
Complex interactions with various systems – experiment/Grid/analysis
Current experience (borrowed from EOS)
ALICE needs factor 4 in rate in 2021 (reversed)