## Slide 1
Electron cloud instability studies for the LHC
A. Romano, G. Iadarola, G. Rumolo
Many thanks to: X. Buffat, P. Dijkstal, K. Li, L. Mether, E. Métral

## Slide 2
Outline
Overview on my PhD work
  Topics studied
  Ongoing studies
  Activities and conferences
Electron cloud induced instability in the LHC during collisions at 6.5TeV
  Instability observations: background and history
  Simulations studies and challenges
  Comparison of simulation results with the available experimental observations
Highlights from ongoing studies and next steps

## Slide 3
Outline
Overview on my PhD work
  Topics studied
  Ongoing studies
  Activities and conferences
Electron cloud induced instability in the LHC during collisions at 6.5TeV
  Instability observations: background and history
  Simulations studies and challenges
  Comparison of simulation results with the available experimental observations
Highlights from ongoing studies and next steps

## Slide 4
My PhD work
TOPICS STUDIED SO FAR
ELECTRON CLOUD BUILD-UP
  Effect of the LHC beam screen baffle on the electron cloud buildup (Electron_cloud_Meeting_18.09.15, Proceedings_IPAC16)
  Electron cloud build up simulations in the SPS MKP and MKE (MKP_Strategy_Meeting_30.06.16, MKP_Strategy_Meeting_7.11.16)
ELECTRON CLOUD EFFECTS ON THE BEAM DYNAMICS
Incoherent effects
  Effect of the electron cloud on the tune footprint in the LHC arcs at injection energy (LBOC_Meeting_27.10.15)
  Effect of the electron cloud on the tune footprint in the LHC Interaction Regions at high energy (Electron_Cloud_Meeting_3.06.16)
Simulated detuning does match with the analytical equation

## Slide 5
2. ONGOING STUDIES
ELECTRON CLOUD EFFECTS ON THE BEAM DYNAMICS (coherent and incoherent effects)
  Understanding of the EC driven instabilities in the arcs together with chromaticty, octupoles and transverse feedback  long simulations run to approach the time scale of machine observations
  3. ACTIVITIES and CONFERENCES
  Experiment at LHC (MD, Scrubbing run)
  KWT (2015, 2016, 2017), IPAC ‘17, ICFA
My PhD work
  Coherent effects
  Overview on the Electron cloud effect on the LHC beam dynamics (e.g preliminary results obtained using new developed tools) (Electron_Cloud_Meeting_30.09.16)
  Investigations on the electron cloud impact on the observed instabilities at high energy (1/2_Day_Internal_review_29.11.16)
  Subject of this presentation and potential peer reviewed paper

## Slide 6
Outline
Overview on my PhD work
  Topics studied
  Ongoing studies
  Activities and conferences
Electron cloud induced instability in the LHC during collisions at 6.5TeV
  Instability observations: background and history
  Simulations studies and challenges
  Comparison of simulation results with the available experimental observations
Highlights from ongoing studies and next steps

## Slide 7
Key findings for instabilities in 2015
2015 was successful for LHC operation: deployment of the 25 ns beams and operation at 6.5 TeV  stable foundation for the 2016 physics run but the e-cloud remains still a challenge for the machine operation
  scrubbing is not sufficient to achieve a full e-cloud suppression  but conditioning effect throughout the year has been observed
2015
(See G.Iadarola_Chamonix2017 talk)

## Slide 8
Key findings for instabilities in 2015
2015 was successful for LHC operation: deployment of the 25 ns beams and operation at 6.5 TeV  stable foundation for the 2016 physics run but the e-cloud remains still a challenge for the machine operation
  scrubbing is not sufficient to achieve a full e-cloud suppression  but contiditiong effect throughout the year has been observed
  Establish operable machine settings to ensure the beam stability
    Chromaticity: Q’H,V = 15/15
    Octupoles current: ~20 A  corresponds to ΔQoct,spread ~ 1 x 10-3
    Transverse feedback: high gain, maximum achievable bandwidth
  Further studies has been carried out in order to evaluate the contribution of these settings, together with the detuning induced by the e-cloud, on the tune footprint

## Slide 9
Key findings for instabilities in 2015
2015 was successful for LHC operation: deployment of the 25 ns beams and operation at 6.5 TeV  stable foundation for the 2016 physics run but the e-cloud remains still a challenge for the machine operation
  scrubbing is not sufficient to achieve a full e-cloud suppression  but contiditiong effect throughout the year has been observed
  Establish operable machine settings to ensure the beam stability
    Chromaticity: Q’H,V = 15/15
    Octupoles current: ~26 A
    Transverse feedback: high gain, maximum achievable bandwidth
  Further studies have been carried out in order to evaluate the contribution of these settings, together with the detuning induced by the e-cloud, on the tune footprint
    large tune footprint at injection which could reach the third order resonance
Q’v=10
Qv=.305
Q’v=15
Qv=.300
Q’v=15
Qv=.305
Q’=15/20, Octupole at 20A , EC central density in dipoles 5 x 10e11 e/m3
Optimization of the working point to improve life time and avoid linear coupling

## Slide 10
Moving from 2015 into 2016 LHC operation
In 2016, all performance optimizing measures worked out in 2015 have been applied
Observations at the beginning of the run
  in spite of high value of chromaticity (15 units in both planes) and high Landau octupoles current, a new type of instability was showing up after few hours in stable beam (i.e stable condition with collisions in the experiments)
LHC beam mode:
E-cloud?
Instability observations

## Slide 11
BCMS
Instabilities observation in stable beam - history
72 bpi
2x48
11/05/16
Instabilities were observed in collisions at 6.5 TeV in most of the fills with trains of 72b.
Several bunches blew-up in the vertical plane, as observed on bunch by bunch luminosity and BSRT data  affecting only bunches at tails of the trains (e-cloud?)
X. Buffat
Fill 4979 - Beam 1
Red spots are the unstable bunches
Notes: BSRT: Beam Synchrotron Radiation Telescope
Beam transverse profile monitoring with synchrotron

## Slide 12
11/05/16
Instabilities were observed in collisions at 6.5 TeV in most of the fills with trains of 72b.
Several bunches blew-up in the vertical plane, as observed on bunch by bunch luminosity and BSRT data  ecloud?
Data analysis showed that most of instabilities occurred for bunch intensities between 0.7e11 and 1.1e11
Instabilities observation in stable beam - history
72 bpi
2x48
X. Buffat
Notes: First observations were made during the intensity ramp-up of the physics fills with trains of 72 bunches. These instabilities affected almost all fills with more than 601bunches and intensities between …... Per bunch, as shown in the plot on your right

## Slide 13
Instabilities observation in stable beam - history
72 bpi
2x48
02/06/16
Vertical chromaticity increased from 15 to 22 units after going in collision
  blow-up mitigated, instability still sporadically detected on the bunch-by-bunch luminosity data
  clear improvement on the number of unstable bunches
12
X. Buffat
Fill 4988, Q’v = 22
Fill 4964, Q’v = 15
Notes: INTENSITY RAMP UP

## Slide 14
Instabilities observation in stable beam - history
72 bpi
2x48
25/06/16 ...
Physics fills with trains of 48b
  No instability observed
  Vertical chromaticity brought down to 15 units in collision still with no sign of instability
Notes: INTENSITY RAMP UP

## Slide 15
Instabilities observation in stable beam - history
72 bpi
2x48
19/08/16
MD fills with trains of 72b. and bunch intensities 1.1e11, 0.9e11 and 0.7e11
Chromaticity could be reduced to 5 units in stable beams without any sign of instabilities (scrubbing?)
L. Mether
Notes: INTENSITY RAMP UP

## Slide 16
How the e-cloud can drive an instability?
When a proton bunch passes through an e-cloud, electrons are attracted towards the transverse center of the beam
    electron density increases within the bunch inducing coherent bunch oscillations, e.g transverse instability
Understanding of these phenomena relies on numerical simulations (PyECLOUD-PyHEADTAIL)
Electron cloud driven instabilities
Electron density during a bunch passage
e-cloud driven instability
In space: small beam (~100 mm) in a big chamber (4 cm)
In time: 1 ns for the e- motion, 1 to 10 s for instability development
Multi-scale problem:

## Slide 17
Simulation studies
Recent work at CERN focused on increasing the performance of our simulation tools:
  Introduced a “ telescoping” grid in the Particle in Cell solver
  Exploit parallel computing through a new parallelization layer (PyPARIS)
Typical simulation study: ~400 CPU cores (8-16 cores per job)
  Allowed gaining new insight on scenarios that were previously inaccessible (e.g. 10k turn simulations for LHC at 6.5 TeV)
Long term effects, like incoherent emittance growth and interplay with other non-linearities, are practically unexplored in simulations (computationally very heavy)

## Slide 18
To check the potential role played by the e-cloud on the instabilities observed in stable beam, long simulation runs have been carried out  more than 10k turns (~1 s) to approach the timescale of the instabilities observations (~2.5s)  3-4 weeks of computing time on the CNAF cluster
  Simulations were performed using realistic machine settings and a beam parameters
Simulation studies
Machine and beam settings:
Beam parameters: 1.0e11 ppb, 1 ns bunch length, 2.5 mm transverse emittance
    Octupole current set to 470 A  corresponds to ΔQoct,sread ~ 1 x 10-4
Chromaticity 15/15
Transverse damper (100 turns of damping time)
E-cloud configurations:
e-cloud in dipoles: uniform electron density scan  good approximation*
e-cloud in quadrupoles: self consistent simulation from buildup (SEY 1.30)  significant impact on the EC pinch dynamics **
  * H. Bartosik, proceedings of the ECLOUD12 Workshop, Elba, 2012
  **G. Iadarola, presentation at Joint HiLumi-LARP Meeting, Fermilab, 2015

## Slide 19
Simulation studies: 1e11 p/bunch
EC quadrupoles
EC dipoles
Chromaticity
Oct.
Damper
Density scan
15/15
470 A
Sim.Turns
100 turns
10k
SEY 1.30
An electron density of 5x1011 p/m3 in the central region of the dipoles is sufficient to induce a vertical instability (in spite of the high chromaticity and high octupole settings)

## Slide 20
Simulation studies: 1e11 p/bunch
EC quadrupoles
EC dipoles
H Chromaticity
Oct.
Damper
Density scan
15
470 A
Sim.Turns
100 turns
10k
SEY 1.30
An electron density of 5x1011 p/m3 in the central region of the dipoles is sufficient to induce a vertical instability (in spite of the high chromaticity and high octupole settings)
Increasing Q’v up to 22 units, the emittance growth becomes slower, expecially at low electron densities
This instability could not be detected over our usual simulation runs of 500-1000 turns  we need run more than 10k turns for a better understanding of the instability process
Q’v = 22
Q’v = 15

## Slide 21
Simulation studies: different bunch intesity
EC quadrupoles
EC dipoles
Chromaticity
Oct.
Damper
Density scan
15/15
470 A
Sim.Turns
100 turns
10k
SEY 1.30
In the machine instabilities were observed for bunch intensities below than 1e11 ppb
The impact of the beam intensity on the instability threshold has been investigated by running the same simulations with beam intensity of 0.7e11 ppb
   Instability threshold basically unchanged!
0.7e11 p/bunch
1.0e11 p/bunch

## Slide 22
Central density from PyECLOUD simulations
From PyECLOUD simulations we can estimate the electron density profile in the dipoles for different beam intensities
   When the bunch intensity decreases, the central density increases significantly
Simulations settings
SEYDIP = 1.4
1 ns bunch length
2.5 um transverse emittance

## Slide 23
Instability threshold estimated by PyEC-PyHT simulations
For bunch intensities below than 1.0e11 ppb, the central density increases rapidly crossing the instability threshold
For bunch intensities larger than 1.0e11 ppb, the estimated electron density is well below the instability threshold
0.7e11
1.0e11
Central density from PyECLOUD simulations

## Slide 24
Average bunch intensity (between B1 and B2) during the collisions has been used to infer the evolution of the central density
Evolution of the central electron density: the central density increases over the fill time and crosses the instability threshold when the intensity has dropped to ~0.8e11 p/bunch
Central density from PyECLOUD simulations
From PyECLOUD simulations (SEYdip= 1.40)
As measured in LHC
Instability threshold
Good agreement between machine observations and simulations results
Physics fill where we observed instabilities

## Slide 25
Summary and conclusions
In spite of the high chromaticity and high octupole settings, a vertical emittance blow up of bunches at the end of the 72b trains was observed during the stable beam in most of the fills at the beginning of the year
  An increase of the vertical chromaticities after going in collision was needed to avoid instabilities
The potential role of the e-cloud has been investigated in simulation
  According to machine observations, two different settings for the beam instensity were simulated showing a weak dependence of the instability thresholds on the bunch intensity
Build-up simulation results showed that when the beam intensity decreases, the electron density in the center can become sufficiently high to drive an instability

## Slide 26
Outline
Overview on my PhD work
  Topics studied
  Ongoing studies
  Activities and conferences
Electron cloud induced instability in the LHC during collisions at 6.5TeV
  Instability observations: background and history
  Simulations studies and challenges
  Comparison of simulation results with the available experimental observations
Highlights from ongoing studies and next steps

## Slide 27
Ongoing studies
GOALS FOR ONGOING STUDIES:
check the impact of the EC in the LHC arcs (dipoles and quadrupoles) both at injection and flattop on the beam stability (e.g nominal LHC bunch)
   at injection, the work has been done in collaboration with Kevin Li
improve the understanding of machine settings on the instability threshold  chromaticity, octupoles and trasverse feedback are simulating together with the EC
 A full picture of the EC driven instabilities in the arcs and an optimiziation of machine settings to ameliorate LHC operation!

## Slide 28
450 GeV vs 6.5 TeV: e-cloud in arc dipoles
FLATTOP
INJECTION: both planes are unstable  H instabilities are much slower (~2000 turns )
FLATTOP: vertical plane predomintly unstable

## Slide 29
450 GeV vs 6.5 TeV: e-cloud in arc dipoles
FLATTOP
INJECTION: both planes are unstable  H instabilities are much slower (~2000 turns )
FLATTOP: vertical plane predomintly unstable
Horizontal instabilities are mode-0 like  they are not observed in the machine because are damped by the transverse feedback
Vertical instabilities develop for higher frequencies which can not be dealt by the stranverse feedback

## Slide 30
H. threshold ~ 5e11
V. threshold ~ 7e11
V. threshold ~ 2.6e12
450 GeV vs 6.5 TeV: e-cloud in arc dipoles
EC instability threshold defined as density needed to generate 10% emittance growth over 9000 turns
INJECTION
FLATTOP

## Slide 31
H. threshold ~ 5e11
V. threshold ~ 7e11
V. threshold ~ 2.6e12
450 GeV vs 6.5 TeV: e-cloud in arc dipoles
INJECTION
FLATTOP
Comparison with the estimated EC density from PyECLOUD (SEYdip 1.4):
  Injection: Estimated density ~5e8 < instability th
  Flattop: : Estimated density ~2e10 < instability th
   No EC induced instabilities can be explained over 9000 turns
At flattop Large EC densities are needed to drive an instability  effect of the beam rigidity
EC instability threshold defined as density needed to generate 10% emittance growth over 9000 turns

## Slide 32
450 GeV vs 6.5 TeV: e-cloud in arc quadrupoles
INJECTION: both planes are simmetrically unstable
FLATTOP: no clear instability can be detected

## Slide 33
v
FLATTOP
450 GeV vs 6.5 TeV: e-cloud in arc quadrupoles
EC instability threshold defined as density needed to generate 10% emittance growth over 5000 turns
INJECTION

## Slide 34
450 GeV vs 6.5 TeV: e-cloud in arc quadrupoles
EC instability threshold defined as density needed to generate 10% emittance growth over 5000 turns
v
INJECTION
FLATTOP
Sensitivity of the instability threshold to the quadrupoles weight
  Injection: instability threshold below the effective weight  very sensitive
  Flattop: no emittance blown-up is observed
   EC in quadrupoles key driver of instability at injection
Strong impact of the beam rigidity on the beam stability

## Slide 35
Summary and further studies
Chromaticity
Landau octupoles
Transverse feedback
EC in DIPOLES
EC in QUADRUPOLES
key driver of instabilities at injection  at flattop due to the magnetic rigidity of the beam no clear instability can be observed
EC in DIPOLES
Estimated EC density < instability th
Instabilitiy observations cannot be explained (over 9000 turns) by the EC in dipoles alone  unless the beam intesity decreases
Next steps  How different machine settings together with e-cloud affect the beam stability?
Electron Cloud

## Slide 36
Thanks for your attention

## Slide 37
Instabilities in stable beam

## Slide 38
Instabilities in stable beam
Fill 4979 – Beam 2

## Slide 39
Instabilities in stable beam – beam intesity
X. Buffat

## Slide 40
Instabilities in stable beam – bunch length
X. Buffat

## Slide 41
HEADTAIL simulations
Fast vertical instability is driven by the central density of electron in dipoles

## Slide 42
Arc Quadrupoles: realistic e- distribution
z [m]
y [m]
z [m]
y [m]
First test performed with self consistent distribution from buildup simulation
  Electrons trapped along the magnetic lines  pinch is attenuated
Uniform initial distribution
Initial distribution from buildup simulation

## Slide 43
Electron trajectories are strongly influenced by externally applied magnetic fields
Electrons spin around the field lines
In quadrupole magnets magnetic trapping can occur with electrons surviving several bunch passages being accelerated up to a few keV
  Much stronger heat loads compared to dipoles
LHC Arc Dipole
LHC Arc Quadrupole
Maximum Secondary Electron Yield (dmax)
Magnetic field

## Slide 44
Horizontal instabilities @ 6.5TeV
EC only in dipoles density fixed at 3.8e12
Horizontal chromaticity is scanned between -20 and 20
Vertical chromaticity is kept at 0
No emittance blown up observed in the vertical plane
Strong horizontal emittance growth when increasing the horizontal chromaticity

## Slide 45
Horizontal instabilities – Possible mechanism
Transverse wake function (dipolar)
Stability criterion for mode-0 assuming constant wake (see Chao, eq. 6.216)
Sign of the wake
Wx<0, i.e. tail gets kicked in phase w.r.t. the head displacement
Positive chromaticity
Stability condition
(above transition)
Wx >0, i.e. tail gets kicked in counter-phase w.r.t. the head displacement
Negative chromaticity

## Slide 46
Horizontal instabilities – Possible mechanism
Bunch head
Bunch tail
Δx α σ x
(e.g positive head displacement)
Tail gets kicked in counter - phase with the head displacement so we need negative chromaticity for stabilizing
Δx’ <0

## Slide 47
Horizontal instabilities – effect of the damper
EC dip
EC density 3.8e12

## Slide 48
Horizontal instabilities – effect of the damper
EC dip, Chroma
EC dip
EC density 3.8e12

## Slide 49
Horizontal instabilities – effect of the damper
EC dip, Chroma
EC dip, Chroma, damper
EC dip
EC density 3.8e12
This type of instability is not observed in the machine because of the strong stabilizing effect of the transverse damper