## Slide 1: Development of a high-efficiency klystron based on the kladistron principle
Antoine Mollard1, Claude Marchand1, Franck Peauger1, Juliette Plouin1 Armel Beunas2, Rodolphe Marchesin2
1DRF/Irfu/SACM/Lisah
CEA Saclay 91191 Gif-sur-Yvette Cedex
2Thales Electron Devices 2 Rue Marcel Dassault 78140 Vélizy-Villacoublay
Eucard2 WP12 Annual Meeting 2017| Mollard Antoine antoine.mollard@cea.fr

## Slide 2: Development of a high-efficiency klystron based on the kladistron principle
CLIC and the Kladistron project
TH2166 klystron and the kladistron prototype design
TH2166 kladistron cavities development
TH2166 kladistron fabrication and testing

## Slide 3: CLIC and the Kladistron project

## Slide 4: The high-efficiency klystron project
« In this sub-task, CEA will develop and search for innovative concepts of X band RF power sources and components. The objective is to propose affordable and reliable solutions for future testing capabilities for the CLIC accelerating structures. The task includes the design and the fabrication of prototype RF devices to demonstrate the feasibility of the new concepts proposed. » Budget available to build a (small) part of the RF power source or component
WP12 : Innovative RF Technologies
2013 - 2017
 Activity fully oriented towards R&D
Collaboration with THALES ELECTRON DEVICES :
PhD funding : 50% CEA/50% Thales (Contrat de Thèse CEA Industrie)
Co-supervisation :
Juliette Plouin/Franck Peauger/Claude Marchand @ CEA
Armel Beunas/Rodolphe Marchesin @ Thales
Collaboration with CERN : Igor Syratchev, Walter Wuensch…
MAGIC bought by CEA with “contribution exceptionnelle de la France au CERN”

## Slide 5: Klystron principle
Linear-beam vacuum device which is used as a narrow bandwidth amplifier for high radio frequencies (100 MHz-100GHz)
Creation of a stream of electrons by the electron gun (thermionic emission)
Confinement by an external magnetic field
Triggering of the beam modulation by the wave in the input cavity
Modulation of the beam into a set of electron bunches in the gain cavity/ies
Drifting of the electron bunches
Energy transfer between the bunches and the output antenna
Absorption of the lower energy electron beam by the collector
Klystron efficiency is the ratio of the output power to the electron gun supply power.
6
5
4
3
2
1
7
Ps
Pe
Vk Ib
Cold water
Hot water
Collector
Middle cavity
Electron beam
Control anode
RF input
Solenoid
RF output
Ionic pump

## Slide 6: Kladistron principle
A Kladistron (Kl-adi(adiabatic)-stron) is a high-efficiency klystron with a large number of cavities (at least twice as many as in a classical klystron).
=> Efficiency (η=)
20 cavities – 12GHz
µP = 1.5 A.V^-3/2 Efficiency 78 % (AJDisk simulation)
Length 285 mm
CLIC Project needs a 12GHz-high-efficiency klystron, with a microperveance of 1.5 A.V^-3/2. Our preliminary AJDisk results show a higher efficiency than what we can expect from a klystron with such a high microperveance.

## Slide 7: Kladistron and classical klystrons
12GHz
« KLADISTRON »
4.9GHz « KLADISTRON » (technical demonstration)

## Slide 8: TH2166 klystron and the kladistron prototype

## Slide 9: TH2166 Klystron
Features | 
Frequency | 4.9 GHz
Output power | 56 kW
Efficiency | 50%
Ibeam | 4.3 A
Vk | 26 kV
µP | 1.066
Number of cavities | 6
Interaction line length | 233mm
TH2166 klystron was designed by Thales electron devices (TED) for Mainz Microtron.
233mm
TH2166 front view
This klystron will be modified to verify the kladistron principle.

## Slide 10: klystron TH2166 enhancement Cavities preliminary design
The design we are looking for would let us :
Use the TH2166 klystron test and conditioning bench  Total interaction line length of 233mm, same input and output cavities, same solenoid
Use the TH2166 klystron electron gun and collector  Same microperveance of 1µA.V^(-3/2)
Check the kladistron principle  More than 6 cavities
Avoid cavities coupling  Drift space between cavities larger than 9mm
Avoid gain peaks  Low coupling cavities (low R/Q and Q0 values)
Thales-provided elements

## Slide 11: Th2166 Klystron and Kladistron Comparison MAGIC2D Simulations
Chart: MAGIC2D simulations results Laminar beam – Uniform magnetic field
| 0.05 | 0.1 | 0.3 | 0.5 | 0.7 | 0.9 | 1
Kladistron | 0.13483 | 0.24019 | 0.4753 | 0.55485 | 0.58 | 0.58843 | 0.59047
TH2166 | 0.047021 | 0.19562 | 0.44669 | 0.5025 | 0.52522 | 0.53309 | 0.53175
Our kladistron simulation results reach an efficiency of six points above TH2166 simulation results.
The electron bunching and the beam current growth are also smoother.
TH2166 electron beam
Kladistron electron beam
Chart: z(mm)
TH2166 beam current along the interaction line
Kladistron beam current along the interaction line

## Slide 12: TH2166 kladistron cavities development

## Slide 13: klystron TH2166 enhancement Cavities preliminary design
Type 1
Type 1
Type 2
Type 3
Type 4
Type 1
Type 2
Type 4
TH2166 cavity shape
Low-coupling cavity shapes
According to our COMSOL simulations, these low-coupling cavities are fit for smooth electron bunching.
Type 3
16 cavities interaction line
Tuning system

## Slide 14: Frequency shift : a reliable tuning system is required
Chart: Klys2D (TED code) simulation results Optic2D (TED code) beam Measured magnetic field
"-10MHz" | 0.0002 | -0.0006 | -0.0041 | 0.0005 | 0.0003 | 0.0005 | 0.0003 | -0.001 | -0.0016 | -0.0037 | -0.0041 | -0.0053 | 0.0013 | 0.0044 | -0.0466 | 0.0065
"-5MHz" | 0.0001 | 0.0006 | -0.001 | 0.0004 | 0.0002 | 0.0004 | 0.0003 | -0.0002 | -0.0004 | -0.0016 | -0.0015 | 0.0002 | 0.0013 | 0.0025 | 0.0058 | 0.0081
"-2MHz" | 0.0003 | 0.0004 | -0.0009 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0 | -0.0001 | -0.0005 | -0.0011 | -0.0004 | 0.0007 | 0.0011 | 0.0052 | 0.0043
"+2MHz" | -0.0002 | -0.0007 | 0.0005 | -0.0001 | 0 | -0.0001 | -0.0001 | -0.0002 | 0.0001 | 0.0004 | 0 | 0.0002 | -0.0007 | -0.0011 | -0.007 | -0.0054
"+5MHz" | -0.0007 | -0.0008 | -0.0006 | -0.0002 | -0.0001 | -0.0003 | -0.0003 | -0.0006 | 0 | 0.0006 | 0.0007 | -0.0002 | -0.0021 | -0.0028 | -0.0194 | -0.0157
"+10MHz" | -0.0002 | -0.0001 | 0.0008 | -0.0005 | -0.0002 | -0.0007 | -0.0006 | 0.0007 | -0.0002 | 0.0015 | 0.0015 | -0.0018 | -0.0049 | -0.0058 | -0.0406 | -0.0377
For each computation we shift the frequency of one of the cavities.
Kladistron efficiency is sensitive to its cavities frequency shifts, especially at the end of the interaction line.
→Δzgap ≈ -4µm
Zgap
Δf/Δzgap ≈ 2.5MHz/µm
The cavities fabrication must also be accurate: a 1-µm error might induce a 2,5MHz frequency-shift (COMSOL).

## Slide 15: tuning system design and test
Tuning system (x4 at 60°)
The tuning system we designed is inspired by CLIC accelerating cavities design; a thigh copper membrane is misshaped to adjust cavities frequencies. This strain is controlled by an accurate screw thread.
Although the airtightness had been preserved during our tests, the pin’s thread had been broken. The tuning system assembling is too rigid and the extra mechanical stress is reported on the screw thread.
Cooling system channels (4)
Copper
Beam drift tube
Prototype test bench
Chart: Screw revolutions
| 0 | 0.5 | 1 | 1.5 | 2 | 2.5 | 3 | 3.5 | 4
1 | 0 | 0.05 | -0.075 | -0.475 | -0.762 | -0.925 | -1.237 | -1.4625 | -1.6125
2 | -0.1 | -0.65 | -0.9 | -1.2625 | -1.35 | -1.4625 | -1.525 | -1.5125
3 | 2.1375 | 1.8125 | 1.7125 | 1.3 | 0.7625 | 0.3375
3' | 2 | 2.0375 | 2.1375
4 | 1.95 | 1.9625 | 1.9 | 1.975 | 1.9625 | 1.9625 | 1.9625 | 1.9625
4
1
2
3
Pin’s thread broken
Screw thread
Threaded Cupronickel pin brazed on the membrane
Misshaped membrane
Cavity
Beam drift tube
Bronze bearing

## Slide 16: tuning system design and test
Tuning system (x4 at 60°)
Cooling system channels (4)
Copper
Beam drift tube
Prototype test bench
Chart: Screw revolutions
| 0 | -0.5 | -1 | -1.5 | -2 | -2.5 | -3 | -3.5 | -4 | -4.5
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
1' | 0 | 0.3 | 0.55 | 0.775 | 1.225 | 1.35 | 1.6 | 1.8625 | 2.025 | 2.2125
2 | 2.1 | 2.0375 | 2.05 | 2.05 | 2.05 | 2.05 | 2.05 | 2.1 | 2.1 | 2.1
2' | 0.2375 | 0.5 | 0.75 | 0.95 | 1.225 | 1.4587 | 1.7625 | 1.9 | 2.1
3 | -1.4625 | -1.1875 | -0.925 | -0.6375 | -0.3875 | -0.1
3' | -1.5375 | -1.5375 | -1.4625
4 | -1.3125 | -1.3125 | -1.3125 | -1.3125 | -1.3125 | -1.3125 | -1.375
5 | -1.3375 | -1.35 | -1.2875 | -1.2875
5' | -1.2875 | -1.15 | -0.95 | -0.725 | -0.675 | -0.4 | -0.175 | 0.15 | 0.45 | 0.9625 | 1.3375 | 1.725 | 2.1875 | 2.55 | 2.975
6 | 2.875 | 2.9125 | 2.9125 | 2.9125 | 2.9125 | 2.9125 | 2.9125 | 2.975 | 2.975
6' | 0.825 | 1.125 | 1.4375 | 1.675 | 2.0125 | 2.2625 | 2.4625 | 2.7875 | 2.875
1
2
3
4
5
6
Screw thread
Threaded Cupronickel pin brazed on the membrane
Misshaped membrane
Cavity
Beam drift tube
Bronze bearing
Bronze bearing removed
We then removed one of the bronze bearing to make the assembling more flexible. We tested our tuning system on two complete cycles (+4/-8 screw revolutions). The overall frequency shift is +3MHz/-1,5MHZ.
Despite the hysteresis induced by the assembling modification, the overall frequency shift after two complete cycles is negligible. We validate our tuning system design.

## Slide 17: Multipactor and titanium deposition Musicc3D simulations
Our preliminary Musicc3D (CNRS code) simulations demonstrated that we would face multipactor phenomenon in our cavities’ gaps. We then designed new asymmetrical cavities to apply a titanium layer.
The graph on the left is the number of charges generated in the cavity’s gap, in a Musicc3D simulation: an electron is sent from a chosen area; an electric field with a given phase and amplitude is applied on the charge. The simulation stops after the 20th electron impact, if it has not been absorbed by the material.
Without titanium, a single electron in an electric field of 2MV/m can extract up to 106 charges in the cavity’s gap. With a titanium layer, the maximum number of charges extracted drops to 60.

## Slide 18: Multipactor and titanium deposition Prototype tests
Chart: Frequency (GHz)
Ti1MB1 before titanium deposition | 4.968
Ti1MB1 after titanium deposition | 4.9167
Ti6MB6 before titanium deposition | 4.9709
Ti6MB6 after titanium deposition | 4.9152
COMSOL before titanium deposition | 4.9588
COMSOL after titanium deposition | 4.8717
We designed and ordered 6 prototype cavities to test our titanium deposition method. The “flat” parts (Ti1 to Ti6) have a 0,1mm deflection for the titanium deposition. We cut and brazed titanium discs on these parts. The “flat” and the “concave” parts were assembled to form a cavity to test.
The titanium sheet was misshaped during the brazing process therefore the frequency shift is below our expectations. Although these pieces are being machined to fit the drawings dimensions, we are also working on the improvement of this brazing process to guarantee the adequate cavity geometry.
Flat part without titanium
Concave part
Flat part with a titanium sheet brazed

## Slide 19: TH2166 kladistron fabrication and testing

## Slide 20: Thales-provided elements
Collector
Wave guide,
Output cavity and Output antenna
Steel rods and Ionic pump
These elements have already been delivered.

## Slide 21: Cavities and tuning system fabrication and assembling
The company VDL (Netherland) won the call for tenders and will machine the pieces of the interaction line and the tuning system. We expect the pieces to be delivered by the end of the month. Assembling and brazing operations and the kladistron tests will stand at Thales Electron Devices Vélizy. We are working on the assembling, brazing and test procedure.
Pieces provided by VDL
TH2166 kladistron interaction line and tuning system

## Slide 22: Conclusion and outlook
Tuning systems and titanium deposition method tested
TH2166 kladistron’s cavities fabrication almost finished
Assembling, tuning and test procedure validation
TH2166 Kladistron to be assembled and tested in April, May and June.

## Slide 23
Thank you for your attention