## Slide 2: UFO Buster analysis tool A brief introduction
Martyna Dziadosz
TE-MPE-PE | martyna.dziadosz@cern.ch
Notes: Hi, Today I would like to give you a brief introduction to the project I’m working on – the UFO Buster analysis tool

## Slide 3: Motivation
We want an analysis tool which is:
Fast
Easy
Reliable & reproducible
Enables advanced analysis
Focus on real UFO data
All in one place + manual/readme
One module for frequent analyses
Search for correlations
Notes: Let’s start with familiarizing you a little bit more with the project itself by presenting it’s motivations.
Hence, what are do we await from the tool ?
The aim is to develop the analysis tool for the UFO Buster data from LHC, that will allows fast and easy advanced analysis
focused on UFO events independently from UFO Buster software. Which has to be reliable and reproducible.
Obtaining mentioned requirements throught the application of certain conditions (that I’ll present on one of the consecutive slides) the tool will be focused on real UFO data
All necessary data are stored in one place and do not interfere with UFO Buster original data itself
The tool consist of several, independent from each other moduls, which allow for quick analysis and provide/ensure rreproducibility.
thanks mentioned moduls inependence, the tool allows for repeatablility of steps, which are of our interest without need to reapeat all if them
What is more it provide searching for the correlations in UFO events

## Slide 4: Structure of the UFO Buster analysis tool
Data Extraction
Raw Data Analysis
Collimator Losses
Advanced Analysis
Select only real UFO events
Reduce data volume
Plot UFO event
Analysis signal shape
Correlation with elastic losses (IP7/IP3/IP6)
Statistical analysis (UFO rates etc.)
Correlations to LHC parameters
Determination of UFO location
Discard empty and fishy files
Group like events
Notes: Giving the big picture of the toolkit the structure of the UFO Buster analysis tool is presented at the following slide.
As I’ve mentioned before it contains, several modules, that can be grouped as followed: data extraction, raw data analysis, collimator losses and advanced analysis.
Data extraction is aimed at selection real UFO events, reducing data volume and discard of empty and fishy files
Next step is focused on analysis the signal shape and consequently creating the group like events
It is followed by looking for the correlations in collimator losses and execution the advanced analysis

## Slide 5
Step 1
  DATA EXTRACTION
Retrieve original UFO Buster data
Merge only relevant info into one file F3
Notes: 1 step is to extract data from UFO Buster files F1 (UFO file, which contains max losses for all BLMs for 12 RS together with important prameters, such as verification level, beam mode, UFO BLM names, fillnumber) and F2 (capture buffer file with recorded losses for all BLMs registered with RS2 for 4369 points with timestamp of 80 us) and merge information into one file - F3 (extract/ …).
To give you the feeling of data extraction step the following slide presents the scheme visualizing code structure

## Slide 6
F1 with the corresponding F2
CONDITION 1:
CONDITION 2:
Beam_mode: STABLE
VerificationLevel: UFO_verified
CONDITION 3:
F2 for which max loss for UFO BLM match the value for RS2 in the corresponding F1
losses > threshold (5 * 10-3)
CONDITION 4:
At least 2 point nearby each other for which condition 3 is fulfilled
INPUT
~2000
~60

## Slide 7
Step 1
  DATA EXTRACTION
Basic info (timestamp, fill number, machine parameters)
UFO BLM + neighbours (losses + DCUM)
Time-resolved data (capture buffer)
Notes: Presented at the previous slides consecutive steps and applied conditions for F1 and F2 yield in a result to creating file F3, which contains necessary for the further steps
-> basic informations, such as timestamp, fill number and machine parameters
-> registered by BLMs losses for UFO BLM + it’s neighbours and selected BLMs localized in the collimators area

## Slide 8
Step 1
  DATA EXTRACTION
Reduces data volume for quick analysis
ü
Notes: As F3 is created only for event fulfilling certain conditions,
Data volume has been reduced, what allows for quick analysis

## Slide 9
Step 2
  RAW DATA ANALYSIS
Plot UFO event from F3
Losses in Gy/s
Time (here in 80 µs bits)
Compare with UFO Buster output for confirmation
Notes: After extracting the interesting data we can move to the next step – analysis of the raw data
Initially our attention was focus on creating the plot of losses [Gy/s] of/for the UFO event in a timescale (which at the presented photo is given in bits – 80us)
And them compare achieved results with the UFO Buster output in order to confirm the corectness of conducted analysis

## Slide 10
Step 2
  RAW DATA ANALYSIS
Losses in Gy/s
Time (here in 80 µs bits)
UFO Buster from capture buffer
Plot time-resolved UFO event
ü
Notes: Here is present results achieved using the develop tool and the corresponding plot from UFO Buster software

## Slide 11
Step 2
  RAW DATA ANALYSIS
Losses in Gy/s
Time (here in 80 µs bits)
Analyse and group UFO events
Notes: subsequently we’re going to make the analysis of the UFO events in terms of signal changes

## Slide 12
Step 2
  RAW DATA ANALYSIS
Losses in Gy/s
Time (here in 80 µs bits)
Analyse signal shape & group (FWHM, max, symmetry)

ONGOING
Notes: This is the ongoing step, which will includes signal shape analysis and then consectively storing into the group by
Certain conditions such as the value max losses and symmetry

## Slide 13
Step 3
  STATISTICAL ANALYSIS
UFO rate vs. time or location
number of UFOs
Location in LHC [m]
on reduced sample size
number of UFOs
Notes: The next step are statistical analysis, which are partialy made. So far on a very reduced sample size, which will be changed by the applicatin of slightly different analysis conditions.
On this slide the UFO rate vs time and location has been presented.
The location of the UFO events might tell us a little bit more about area, which are more pronounced to the UFO occurnece
It may give us a bit more information about the regions where UFO evety more often

## Slide 14
Step 3
  STATISTICAL ANALYSIS
ü
Total UFO losses vs. Location (2016)
on reduced sample size
Integrated losses[Gy/s]
Location in LHC [m]
2016
Plot of loss distribution along LHC

## Slide 15
ROMAN POT AREA
Chart: summary losses over 2016
| BLMEI.07L1.B2E20_XRP-RUN1 | BLMQI.24L5.B1I10_MQ | BLMQI.10L2.B1E10_MQML | BLMQI.27R3.B1I10_MQ | BLMQI.10L8.B2I10_MQML | BLMEI.04L5.B2I10_X5FCB.A4L5 | BLMQI.32R1.B2I10_MQ | BLMQI.18L8.B1E10_MQ | BLMQI.31L4.B1I10_MQ | BLMEI.07L1.B2E10_XRP | BLMQI.21R2.B2E10_MQ | BLMQI.14L2.B1E10_MQ | BLMQI.33R6.B2I10_MQ | BLMQI.12R1.B2I10_MQ | BLMQI.28R7.B2I10_MQ | BLMQI.05L5.B1I30_MQML | BLMQI.04L1.B2E30_MQY | BLMQI.20R3.B1I10_MQ | BLMQI.09L2.B2I10_MQM | BLMQI.17L7.B2I10_MQ | BLMQI.16R3.B1I10_MQ | BLMQI.13L4.B2E10_MQ | BLMQI.28L8.B2I10_MQ | BLMQI.13L1.B1I10_MQ | BLMQI.04L5.B2E30_MQY | BLMQI.32L6.B2I10_MQ | BLMQI.17L8.B1E10_MQ | BLMQI.13R4.B1I10_MQ | BLMQI.11L7.B1E10_MQ | BLMQI.29R2.B2E10_MQ | BLMQI.31L1.B1I10_MQ | BLMQI.17R7.B2I10_MQ | BLMQI.23L5.B2E10_MQ | BLMQI.29L6.B2I30_MQ | BLMQI.07R1.B1E10_MQM_XRP
 | 0.029367 | 0.26806 | 0.034888 | 0.026245 | 0.049594 | 0.18448 | 0.034073 | 0.13218 | 0.010589 | 0.023983 | 0.035657 | 0.045929 | 0.022308 | 0.088916 | 0.20109 | 0.072038 | 0.20982 | 0.055567 | 0.015838 | 0.017285 | 0.052128 | 0.029413 | 0.936 | 0.018055 | 0.042716 | 0.033123 | 0.11729 | 3.5071 | 0.11475 | 0.04534 | 0.058327 | 0.03715 | 0.039322 | 0.06068 | 0.034661
 | 0.016471 | 0.017829 | 0.01086 | 0.024797 | 0.0089143 | 0.39856
 | 0.05421 | 0.032489 | 0.009593
 | 0.03629 | 0.03715
 | 0.037558
Integrated losses of all UFOs per BLM
Notes: Hot spots, where more than one UFO event occured during 2016 LHC-working time
Those are mainly the roman pots area, where we can expect such an behaviour

## Slide 16: Summary of Achievements
ü
Plot of loss distribution along LHC
UFO rate plots (vs time, location or BLM name)
ü
BLM losses vs time
→ UFO event visualization
ü
Reduced data volume → faster analysis
ü
07/12/2017 | Schematic overview of UFO Buster analysis tool
Notes: Summarizing, until know it has been reached :
-> that allow
Versus/in reference

## Slide 17: Conclusion
Data extraction and visualization working
Basic functionality validated with reduced data set
Extension for big data needed
Statistical analysis available
UFO shape analysis still to be implemented
… to be continued!
Notes: To conclude now we have principally working tool created within usage of Python software.
With working data extraction and visualzation. Furthermore, basic functionality was validated on the reduced sets of data.
It worth to mentioned that’s so far we are workig with the skretch/test version to get the feeling of the data in order to
Apply the precise conditions for the final software layout.
What is more, some of the modules still recquires to be applied and will be shown on one of the consective presentations

## Slide 18
Thank you for your attention. 

## Slide 19: www.cern.ch

## Slide 20: APPENDIX

## Slide 21: Appendix – F1 structure

## Slide 22: Appendix – F2 structure

## Slide 23
Step 1
  DATA EXTRACTION
List of files type F1 for which the exist the corresponding file type F2
F1
F2
find the corresponding file type 2
EXTRACT
DECONVERSION -> JAVA
look for F2 with the same timestamp and fillnumber
Fillnumber, Timestamp, UFO_BLM_Expert_name, Dcum, VerificationLevel, beam_mode, Expert Name
Java objects:
String[] header
(1D matrix with BLMs names)
Int[][] value
(2D matrix with BLMs signal losses)
Notes: Initially we have 2 files
the 1 step is to extract data from retrieved from UFO Buster files F1 and F2 and merge information of our interest in F3 (extract/ …).
To give you a broader impression of that step the following slide presents the diagram visualizing code structure

## Slide 25
Step 1
  DATA EXTRACTION
Retrieve original UFO Buster data
Merge only relevant info into one file F3
Basic info (timestamp, fill number, machine parameters)
UFO BLM + neighbours (losses + DCUM)
Time-resolved data (capture buffer)
ONGOING

## Slide 26: INPUT FILES
UFO file (.sdds ASCII)
max losses [Gy/s] for
12 RS for 3929 BLMs
important parameters:
VERIFICATION LEVEL
BEAM MODE
UFO BLM name
FILLNUMBER
F1
F2
Capture Buffer (.sdds binary)
F2
losses [bits] recorded for every 6912 BLM
data registered with RS2 time resolution for 4369 timestamps

## Slide 27: Diagram visualizing code structure

## Slide 28
F1
F2
find the corresponding file type 2
2 WAYS
1) looking for F2 with the same timestamp and fillnumber
2) go to an appropriate path using fillnumber. Then look for the corresponding F2 using naming convention
.sdds ASCII file
.sdds binary file
EXTRACT
DECONVERSION !!!
JAVA
Fillnumber
Timestamp
UFO_BLM_Expert_name
Dcum []
VerificationLevel
beam_mode
Expert Name
Java objects:
String[] header (1D matrix with BLMs names)
Int[][] value (2D matrix with all BLMs signal losses)
List of files type F1 for which the exist the corresponding file type F2
OUTPUT:

## Slide 29
F1 with the corresponding F2
CONDITION 1:
CONDITION 2:
Beam_mode: STABLE
VerificationLevel: UFO_verified
CONDITION 3:
F2 for which max loss for UFO BLM match the value for RS2 in the corresponding F1
losses > threshold (5 * 10-3)
CONDITION 4:
At least 2 point nearby each other for which condition 3 is fulfilled
INPUT

## Slide 30
excel file (.csv)
F3
Basic info (timestamp, fill number, machine parameters)
UFO BLM + neighbours (losses + DCUM)
Time-resolved data (capture buffer)
excel file (.csv)
F3

## Slide 31: OUTPUT FILES
+
F4
excel file (.csv)
F3
F4
losses over time for:
UFO BLM
20 neighboring BLMs
selected list of BLMs in collimator’s area
parameters for filtered in UFO BLMs:
  UFO BLM
  fillnumber
excel file (.csv)

## Slide 32: Analysis results

## Slide 33: STEP 2 – plot comparison (UFO Buster vs achieved plots)
Ufo_2016_05-09_01-49-42.0_BLMQI.28L8.B2I10_MQ

## Slide 34: LHC location vs number of UFO events

## Slide 35: LHC location (in terms of BLMs names) vs (integrated) losses in 2016
ROMAN POT AREA
Chart: summary losses over 2016
| BLMEI.07L1.B2E20_XRP-RUN1 | BLMQI.24L5.B1I10_MQ | BLMQI.10L2.B1E10_MQML | BLMQI.27R3.B1I10_MQ | BLMQI.10L8.B2I10_MQML | BLMEI.04L5.B2I10_X5FCB.A4L5 | BLMQI.32R1.B2I10_MQ | BLMQI.18L8.B1E10_MQ | BLMQI.31L4.B1I10_MQ | BLMEI.07L1.B2E10_XRP | BLMQI.21R2.B2E10_MQ | BLMQI.14L2.B1E10_MQ | BLMQI.33R6.B2I10_MQ | BLMQI.12R1.B2I10_MQ | BLMQI.28R7.B2I10_MQ | BLMQI.05L5.B1I30_MQML | BLMQI.04L1.B2E30_MQY | BLMQI.20R3.B1I10_MQ | BLMQI.09L2.B2I10_MQM | BLMQI.17L7.B2I10_MQ | BLMQI.16R3.B1I10_MQ | BLMQI.13L4.B2E10_MQ | BLMQI.28L8.B2I10_MQ | BLMQI.13L1.B1I10_MQ | BLMQI.04L5.B2E30_MQY | BLMQI.32L6.B2I10_MQ | BLMQI.17L8.B1E10_MQ | BLMQI.13R4.B1I10_MQ | BLMQI.11L7.B1E10_MQ | BLMQI.29R2.B2E10_MQ | BLMQI.31L1.B1I10_MQ | BLMQI.17R7.B2I10_MQ | BLMQI.23L5.B2E10_MQ | BLMQI.29L6.B2I30_MQ | BLMQI.07R1.B1E10_MQM_XRP
 | 0.029367 | 0.26806 | 0.034888 | 0.026245 | 0.049594 | 0.18448 | 0.034073 | 0.13218 | 0.010589 | 0.023983 | 0.035657 | 0.045929 | 0.022308 | 0.088916 | 0.20109 | 0.072038 | 0.20982 | 0.055567 | 0.015838 | 0.017285 | 0.052128 | 0.029413 | 0.936 | 0.018055 | 0.042716 | 0.033123 | 0.11729 | 3.5071 | 0.11475 | 0.04534 | 0.058327 | 0.03715 | 0.039322 | 0.06068 | 0.034661
 | 0.016471 | 0.017829 | 0.01086 | 0.024797 | 0.0089143 | 0.39856
 | 0.05421 | 0.032489 | 0.009593
 | 0.03629 | 0.03715
 | 0.037558

## Slide 36: LHC location vs total losses in 2016

## Slide 37: Fill number vs number of UFO events

## Slide 38: Conclusions & outlock
Now we have principally working tool created mainly in Python (plus Java in order to decode F2). Currently we are working with an initial version (sketch) which gives us the first feeling of the data being still under development.
Future steps:
playing around with data making further analysis with changed parameters & conditions
precise the conditions for the final software layout