## Slide 2
Availability estimation methods
based on systems complexity
Odei Rey Orozco
July 2017, MPE-PE Section meeting
Acknowledgments: Andrea Apollonio, Jan Uythoven

## Slide 3
Outline
Introduction
Procedure to allocate Complexity
Applications
Conclusions and Outlook

## Slide 4
Introduction

## Slide 5
Introduction
LHC Root Cause Fault time by system 2016
-Chamonix Workshop-
How to make fault time data comparable?

## Slide 6
Introduction
Literature review: Reliability/ Availability allocation methods
Methods combine several criteria for obtaining an allocation weight
Chart: 
| 1st Qtr | 2nd Qtr | 3rd Qtr | 4th Qtr
Sales | 8 | 2 | 0 | 0
Chart: 
| 1st Qtr | 2nd Qtr | 3rd Qtr | 4th Qtr
Sales | 9 | 1 | 0 | 0
Expected
according to complexity
Real fault time of subsystem i
High complexity allocated
Idea:
  Apply the methods to evaluate “complexity” of each system
  Compute “expected fault time” according to the complexity weight
  Compare “expected” and achieved/real fault time for each system
Performed better

## Slide 7
Introduction
Other applications:
System under design
Target availability -> Allocate availability requirements for each subsystem
TARGET AVAILABILITY
LOWER availability requirements
Higher complexity
Lower complexity
HIGHER availability requirements
System A
Allocated complexity
Know availability
System B
Allocated complexity
Availability??
Estimate future machine performance from similar operating technologies

## Slide 8
Procedure to allocate complexity

## Slide 9
Procedure to allocate complexity
Step 1: List the structure of system and subsystems
Step 2: Determine the scales for the selected factors
Perform the DEMATEL procedure
Step 3: Computation of complexity index
( Next: Applications)

## Slide 10
Factors
j | Factor | Scoring scale
1 | Repair time | Scale from 1 to 10 10: highest repair time 1: lowest repair time
2 | Criticality | Logarithmic scale: 10 (1) 100 (4) 1000 (7) 10000 (10)
3 | Intricacy | Scale from 1 to 10 10: highly intricate system 1: less intricate system
4 | State of art | 1: Innovative 0.67: existing 0.33: established
5 | Performance time | 1: whole mission time 0.67: Continuous and long times 0.33: instantaneous
6 | Environment | 1: highly radioactive 0.67: average radioactive 0.33: low radioactive

## Slide 11
Computation methods
FOO technique – ISPE factors – Factors product
  Intricacy, State of Art, Performance Time, Environment
Average weighting allocation method
  Factors product (Karmiol method, Geometric)
  Factors sum (Karmiol method, Arithmetic)
  Bracha Method (State of Art higher importance)
  + + + DEMATEL procedure
  An expert evaluates the relationship between subsystems of paired alternatives
  The pair wise comparison scale is designated into 10 levels
  Higher indirect relationship, higher complexity weight allocation

## Slide 12
Applications
Expected availability based on complexity
Use case: LHC 2016

## Slide 13
LHC Root Cause Fault time 2016

## Slide 14
Step 1: List the LHC systems
i | System
1 | Accelerator controls
2 | Access System
3 | Beam Exciters
4 | Beam Instrumentation
5 | Collimation
6 | Cooling and Ventilation
7 | Cryogenics
8 | Electrical Network
9 | Experiments
10 | Injection Systems
11 | Injector Complex
12 | IT Services
13 | LBDS
14 | Machine Interlocks System
15 | Magnet circuits
16 | Power Converters
17 | QPS
18 | Radio Frequency
19 | Transverse Damper
20 | Vacuum
21 | Ventilation Doors

## Slide 15
Step 2: Determine scales

## Slide 16
Step 2: DEMATEL procedure

## Slide 17
Step 3:
Computation of complexity index
Four different methods + DEMATEL

## Slide 18
Application: Computation of expected unavailability
For each system i with allocated complexity :
Expected unavailability according to system i complexity
  Compare the expected unavailability with the real unavailability:
      If , system i performed worse than expected
      If, system i performed as expected
      If , system i performed better than expected
Note that
Machine performance:
Machine total downtime
Total machine unavailability
System i performance:
From AFT → Downtime
Unavailability

## Slide 19
Real vs Expected Unavailability 2016

## Slide 20
Unavailability Difference Real –Expected 2016
Better performance than expected
Worse performance than expected

## Slide 22
Applications
Allocate availability based on complexity
Use case: Linac4

## Slide 23
Complexity allocation
Step 1. List the Linac4 systems
Step 2. Determine scales and DEMATEL procedure
Step 3. Computation of complexity index

## Slide 24
Application: Availability allocation
For each system i with allocated complexity :
Target availability
Allocated availability for system i :
Note that

## Slide 25
Allocated availability I – Target: 95%

## Slide 26
LINAC4 Availability model
Linac4 failure behaviour modelled by Reliability Block diagrams in Isograph®
Each block can be assigned a failure mode…
  Failure distribution
  MTTF
  Consequences
…and a maintenance strategy

## Slide 27
Allocated availability I – Target: 95%
From simulations

## Slide 28
Applications
Availability estimation based on complexity
Use case: Linac4

## Slide 29
Predict Linac4 availability
from Linac2 performance data
based on complexity

## Slide 30
Complexity allocation Linac2 and Linac4
LINAC4 complexity index
LINAC2 complexity index

## Slide 31
Application: Availability estimation
With complexity and availability , theoretical machine total availability:
With complexity and considering the same , estimated availability:
Known System/ technology i performance:
From AFT → Downtime
Unavailability
Allocated complexity weight
Future technology i :
Allocated complexity weight

## Slide 32
Estimated Availability based on complexity
SIMULATIONS
LINAC2
ESTIMATIONS
LINAC4
SOURCE | Availability
LINAC2 | 0.997
LINAC4 Simulations | 0.985
LINAC4 Estimations | min = 0.978 max = 0.995 Average = 0.985

## Slide 33
Estimated Availability based on complexity
SIMULATIONS
LINAC2
ESTIMATIONS
LINAC4
RADIO FREQUENCY | Availability
LINAC2 | 0.995
LINAC4 Simulations | 0.98
LINAC4 Estimations | min = 0.979 max = 0.993 Average = 0.984

## Slide 34
Conclusions
Procedure to allocate complexity
→ In general, factors product and Bracha methods give the most intuitive results
→ More than one expert should evaluate the factors to avoid “subjective” results
Applications based on complexity:
  Compute expected availability and compare, good performance?
  → Results match expectations
  → Good method to evaluate systems performance
  Allocate availability requirements
  → LINAC4 simulation results suggest that the system will operate above required availability
  Estimate availability from existing fault data
  → Estimated availability results go inline with results from simulations

## Slide 35
Outlook
More than one expert will evaluate complexity factors
Evaluate the impact of the complexity factors on the results
LINAC4 – Estimate availability
Validate proposed procedure and model with the Reliability Run data
LHC – Performance evaluation
Validate complexity rating together with system experts
CLIC
Allocate availability requirements to CLIC systems
Estimate future machine performance from similar operating technologies (e.g. Linac4, LHC)

## Slide 36
Thanks for your attention!
Questions?
Remarks?