## Slide 2: Coupling simulation of the HiRadMat-12 experiment to study impact of high energy proton beam on copper (work in progress)
Yuancun NIE
TE-MPE-PE
Acknowledgments:
R. Schmidt, N. Tahir, F. Burkart, D. Wollmann,
L. Mettler, C. Fichera, F. Carra, A. Bertarelli, etc

## Slide 3: Outline
Introduction
A new simulation approach
Progress
Outlooks

## Slide 4: I. Introduction: the worst-case failure mode
At high energy proton accelerator complex, one of the worst-case failure scenarios is that the entire beam (a bunch train) is lost at the same point:
  In the accelerator
    wrong deflecting angle of the extraction kickers
      energy-tracking system failures
      part of the kicker magnets are firing
  In the extraction/beam dump transfer line
    wrong deflecting angle of the septum magnets
      energy-tracking system failures
      septum magnets failures (such as inter-turn short)
  On the beam dump blocks
    dilution kicker failures
The probability is rather low, but the consequences are serious (hydrodynamic tunneling).
Once it happens, we highly rely on passive protections (beam absorbers).

## Slide 5: I. Introduction: the worst-case failure mode (did happen!)
In 2004, the full SPS beam (288 bunches, 3.4×1013 protons, 450 GeV) was once extracted with wrong angle due to switch-off of the septum. Vacuum chamber (stainless steel) of one magnet in the transfer line was severely damaged. Both the vacuum chamber and the magnet had to be replaced. [B. Goddard, et al, AB-Note-2005-014 BT]
  Outside of the vacuum chamber
  Inside, beam impact side
  Inside, opposite to the beam impact

## Slide 6: I. Introduction: hydrodynamic tunneling
What is hydrodynamic tunneling  “simplified picture”:
5 4 3 2 1
8 7 6 5 4
Energy deposition (density-dependent)  temperature/pressure increase  phase transition (solid, liquid, gas, plasma), density reduce (radial shock wave)  new spatial distribution of energy deposition

## Slide 7: I. Introduction: coupling FLUKA with BIG2
FLUKA, a Monte Carlo simulation package, provides energy deposition distributions of protons in target.
BIG2, a two-dimension hydrocode, simulates thermodynamic and hydrodynamic response of the target material using semiempirical equation-of-state (EOS, relations between pressure, density and temperature) models.
The two codes are applied iteratively until the entire beam has been delivered.
FLUKA
BIG2
updated energy deposition
modified density map once the density changes by 10-15%
iterative run till the end of beam impact
target
physical state

## Slide 8
Upper left: three Cu (density 8.93 g/cm3) targets (each with 15 cylinders, every cylinder has R=4 cm, L=10 cm, and the gap is 1 cm which is ignored in the simulation)
Upper right: front and back faces of cylinders 1-3 (a-c) of target 3
Lower: top cover of the three targets (up to down: target 3, 2, 1)
R. Schmidt, et al., Phys. Plasmas 2014
http://dx.doi.org/10.1063/1.4892960
N.A. Tahir, et al., PRE 2014
https://doi.org/10.1103/PhysRevE.90.063112
F. Burkart, et al., J. Appl. Phys. 2015
http://dx.doi.org/10.1063/1.4927721
I. Introduction: HiRadMat experiment in 2012

## Slide 9: I. Introduction: HiRadMat experiment in 2012
Proton energy: 440 GeV
Bunch intensity: 1.5×1011
Bunch length: 0.5 ns
Bunch spacing: 50 ns
The protons were delivered in sets of 36 bunches each, separation between two neighboring bunch packets was 250 ns, total (36×4=144 bunches) beam length ~7750.5 ns

## Slide 10: I. Introduction: existing hydrodynamic tunneling studies
Accelerator | Proton energy | Bunch number | Bunch intensity | Bunch separation | RMS beam size | Target material | Tunneling range | Source
SPS | 440 GeV | 108 | 1.5×1011 | 50 ns | 0.2 mm | copper | 0.8 m | Simulation [1]
SPS | 440 GeV | 108 | 1.5×1011 | 50 ns | 0.2 mm | copper | 0.795 m | Experiment [2,3]
SPS | 440 GeV | 144 | 1.5×1011 | 50 ns | 0.2 mm | copper | 0.9 m | Simulation [1]
SPS | 440 GeV | 144 | 1.5×1011 | 50 ns | 0.2 mm | copper | 0.85 m | Experiment [2,3]
SPS | 450 GeV | 288 | 1.1×1011 | 25 ns | 0.088 mm | copper | 1.3 m | Simulation [4]
SPS | 440 GeV | 288 | 1.15×1011 | 25 ns | 0.2 mm | copper | 1.1 m | Simulation [5]
SPS | 440 GeV | 288 | 1.15×1011 | 25 ns | 0.5 mm | copper | 0.85 m | Simulation [5,6]
LHC | 7 TeV | 2808 | 1.15×1011 | 25 ns | 0.2 mm | copper | 35 m | Simulation [7,8]
LHC | 7 TeV | 2808 | 1.15×1011 | 25 ns | 0.5 mm | graphite | 25 m | Simulation [6]
FCC | 40 TeV | 10600 | 1.0×1011 | 25 ns | 0.2 mm | copper | 290 m | Simulation [9]
FCC | 50 TeV | 10600 | 1.0×1011 | 25 ns | 0.2 mm | copper | 350 m | Simulation [9]
FCC | 50 TeV | 10600 | 1.0×1011 | 25 ns | 0.4 mm | water | 1300 m | Simulation [10]
[1] N.A. Tahir, et al, PRE 2014.
[2] R. Schmidt, et al., Phys. Plasmas 2014.
[3] F. Burkart, et al., J. Appl. Phys. 2015.
[4] N.A. Tahir, et al, NIM A 2009.
[5] N.A. Tahir, et al, High Energy Density Physics 2013.
[6] N.A. Tahir, et al, PRST:AB 2012.
[7] N.A. Tahir, et al, Contrib. Plasma Phys. 2011.
[8] N.A. Tahir, et al, PRE 2009.
[9] N.A. Tahir, et al, PRAB 2016.
[10] N.A. Tahir, FCC Week 2017.
Many other beam parameters need to be studied, but scaling is not obvious.

## Slide 11: I. Introduction: why FLUKA & other hydrocodes?
BIG2 is not commercially available, only limited resources can be used.
It is always good to compare different codes when dedicated experiment is impossible/too expensive.
Therefore, we decided to ‘re-simulate’ the HiRadMat-12 experiment (targets 2&3) coupling FLUKA and ANSYS-Autodyn (commercially available) as a benchmarking study (with EN-MME), so as to develop an alternative solution for other case studies.
Hydrocode | EOS | Mesh
BIG2 | semiempirical | Eulerian
Autodyn | SESAME | Lagrangian

## Slide 12: II. A new simulation approach: workflow
First FLUKA simulation using nominal density (8.93g/cm3) of the (copper) target
Autodyn: dynamic response of material to certain number of bunches
Construction of new FLUKA model (possible extension of fine regions, assign densities to regions, merge/split regions to assure the total number of regions <20000 and density gradient within a few percent.)
Predict beam heated area composed of fine regions (cylinders) that are supposed to undergo density changes
Predefine ~100 density levels (materials) from 0.1 g/cm3 to 10.0 g/cm3. (in maximum 700 materials can be handled by FLUKA)
New FLUKA simulation for the following bunch/bunches
modified density map once the density changes by 10-15%
iterative run till the end of beam impact
updated energy deposition distribution
physical state of the target

## Slide 13: II. A new simulation approach: innovations
Compared to previous coupling between FLUKA and BIG2, the basic principle is similar, but the implementation is quite different. Except for different geometry modelling and data conversion, our method has two main features as follows:
  We don’t define discrete density levels in each iteration. From the accuracy point of view, 100-200 predefined (fixed) densities are sufficient.
    Data analysis and FLUKA modelling are hence significantly simplified, since for each density, different kinds of material & compound have to be defined.
  Previous scripts assign one material to only one region, so the total number of regions is limited to be less than 700. We are able to assign one material to different regions, so that the region number could be up to 20000.
    Regions with the same density may be merged (Boolean Calculation) to save certain simulation time, but we are more flexible (merging regions takes time as well, there is a trade-off).

## Slide 14: III. Progress: static approximation from initial FLUKA map
Linear scaling from one proton (GeV/g/p) to 144 bunches (kJ/g)
Two black curves, upper: melting contour line; down: boiling contour line

## Slide 15: III. Progress: target modelling in FLUKA
Proton beam
×
Proton beam
Cylindrical target: R=4 cm, L=150 cm
Fine regions (beam heated area):
r=0-0.5 cm, z=0-100 cm
(predicted from linear scaling, may need to be extended according to modified density distributions from Autodyn)

## Slide 16: III. Progress: target modelling in FLUKA
Fine regions (beam heated area): Δr=0.01 cm (), Δz=2 cm
2500 fine regions supposed to have modified densities!
(Maximum number of regions can be handled in FLUKA is 20000)

## Slide 17: III. Progress: iteration steps
Proton beam moving to the target
t=7800 ns
Iteration 1 Bunches 1-12
0-600 ns
36 bunches, bunch spacing 50 ns
Bunch packet separation 250 ns
Bunch length 0.5 ns is not shown in the picture
In total, 4 packets, each consists of 36 bunches
The beam pulse length is 35*50*4+250*3=7750 ns for 144 bunches (target 3)
The density drops 13% in max. after the first 12 bunches  12*12 bunches
Iteration 2 Bunches 13-24
600-1200 ns
Iteration 3 Bunches 25-36
1200-2000 ns
Iteration 4 Bunches 37-48
2000-2600 ns
Iteration 5 Bunches 49-60
2600-3200 ns
Iteration 6 Bunches 61-72
3200-4000 ns
Iteration 7 Bunches 73-84
4000-4600 ns
Iteration 8 Bunches 85-96
4600-5200 ns
Iteration 9 Bunches 97-108
5200-6000 ns
Iteration 10 Bunches 109-120
6000-6600 ns
Iteration 11 Bunches 121-132
6600-7200 ns
Iteration 12 Bunches 133-144
7200-7800 ns
t=0 ns

## Slide 18: III. Progress: FLUKA maps [GeV/(g p)]
2D dose distribution for bunches 1-12

## Slide 19: III. Progress: FLUKA maps [GeV/(g p)]
2D dose distribution for bunches 25-36

## Slide 20: III. Progress: FLUKA maps [GeV/(g p)]
2D dose distribution for bunches 49-60

## Slide 21: III. Progress: FLUKA maps [GeV/(g p)]
Dose vs. target axis for different bunches

## Slide 22: III. Progress: temperature (K)
2D temperature distribution after 12 bunches

## Slide 23: III. Progress: temperature (K)
2D temperature distribution after 24 bunches

## Slide 24: III. Progress: temperature (K)
2D temperature distribution after 36 bunches

## Slide 25: III. Progress: temperature (K)
2D temperature distribution after 48 bunches

## Slide 26: III. Progress: temperature (K)
Temperature vs. target axis at different times

## Slide 27: III. Progress: pressure (GPa)
2D pressure distribution after 12 bunches

## Slide 28: III. Progress: pressure (GPa)
2D pressure distribution after 24 bunches

## Slide 29: III. Progress: pressure (GPa)
2D pressure distribution after 36 bunches

## Slide 30: III. Progress: pressure (GPa)
2D pressure distribution after 48 bunches

## Slide 31: III. Progress: pressure (GPa)
Pressure vs. target axis at different times

## Slide 32: III. Progress: density (g/cm3)
2D density distribution after 12 bunches

## Slide 33: III. Progress: density (g/cm3)
2D density distribution after 24 bunches

## Slide 34: III. Progress: density (g/cm3)
2D density distribution after 36 bunches

## Slide 35: III. Progress: density (g/cm3)
2D density distribution after 48 bunches

## Slide 36: III. Progress: density (g/cm3)
Density vs. target axis at different times

## Slide 37: III. Progress: comparison of melting depth
Bunch number | FLUKA (static) | Measurement | Coupling BIG2 | Coupling Autodyn
108 | 63.5 | 79.5 | 80 | ?
144 | 68 | 85 | 90 | ?
Comparison between BIG2 and Autodyn after 36 bunches have been delivered (Thanks to Naeem)

## Slide 38
IV. Outlooks
In collaboration with EN-MME group, a new approach has been developed to simulate the hydrodynamic tunnelling effect, by coupling FLUKA and Autodyn, instead of BIG2.
Compared to the existing method (FLUKA&BIG2), data analysis and target modelling are simplified by predefining a certain number of density levels without influencing the accuracy. Time-consuming ‘region merging’ becomes more flexible since we can assign one material to various regions.
The benchmarking case study validates the approach. Other practical case studies are foreseen, especially for the FCC beam (water dump…).