VELO upgrade: Design updates
Jan Buytaert1, Oscar Augusto2 , Raphael Dumps1,
Wiktor byczynski1 and Wolfgang Funk1
1CERN, 2CERN attached to Liverpool
23/03/17

---
3/8” (9.5 mm) OD input
1/2” (12.7 mm) OD output
Transitions
Input → 5 to 6.223 mm ID
Output → 9.398 to 8 mm ID
Isn’t it better to have a smoother transition?
n = {v%rho} over { M }

---
New proposal
1/4” (6.35 mm) OD input
3/8” (9.5 mm) OD output
Transitions
Input → 5 to 4.572 mm ID
Output → 7.747 to 8 mm ID
Isn’t it better to have a smoother transition?
n = {v%rho} over { M }

---
Design
Raphael is currently updating the design. A new version will be available soon!!!
Filter: 5 μm?
10 μm? 15 μm?
Expected pressure drop due to the filter?
VCR connector

---
VCR gaskets
Which one to use?
Silver plated leak rate:
10-9 std cm3/s
Unplated leak rate:
10-11 std cm3/s
The unplated one might be a problem on the long term
Shall we use the silver plated then?
Signs of interaction of CO2 with the gasket

---
BACKUP SLIDES

---
Swagelok references for the new input and output lines
SS-T4-S-035-6ME
1/4” OD (6.35 mm)
0.035” Wall (0,889 mm)
0.18” ID (4.572 mm)
SS-T6-S-035-6ME
3/8” OD (9.525 mm)
0.035” Wall (0,889 mm)
0.305” ID (7.747 mm)

---
Swagelok references for filter
SS-4TF-TW- … for 5, 10 or 15 μm

---
Previous Pipes dimensions (min)
2.95 ml
(3.48 ml)
CO2GAS
1140 mm (889 mm)
M
0.29 ml
0.69 ml (0.9 ml)
 0.28 ml
(0.33 ml)
41.7 mm
41.7 mm
0.69 ml (0.9 ml)
M
27.2 mm
27.2 mm
0.29 ml
27.6 mm
0.22 ml
0.22 ml
27.6 mm
1140 mm
Output
Split
Input
Split
1/8” (ID 1.397 mm)
1/2” (ID 9.398 mm)
1/16” (ID 0.5715 mm)
Same volume between the valves
1/16” (ID 0.8763 mm or ID 1 mm)
M
* 2x320 mm 1/16 “ to the connector in
   the module
   (Microchannels – Input + output)
3/8” (ID 6.223 mm)
VCR connector 1/8” (~5mm)
1300 mm
1300 mm
20.7 mm
23.9 mm
20.7 mm
25.4 mm