## Slide 1: A High Precision TDC for CMS MG-RPC : Vernier Ring Oscillator based TDC
E.Bechetoille, M.Dahoumane , I.Laktineh, H.Mathez

## Slide 2
Introduction :
  Fast-Timing detector - RPC.
  Requirements
Chronology of TDC works at IPNL (Lyon)
Vernier Ring Oscillator technique
TDC design presentation
Some simulation results
Conclusions and outlooks
Outlines

## Slide 3
Fast Timing Detectors
Double multi-gap RPC: time resolution < 100 ps
Resistive plates
Double single-gap RPC: time resolution < 1ns
Resistive plates
Pick-up
strips
iRPC: well known technology, suited for large detection surface and moderate particle rate.
Charge : few pC
Two scenarios are proposed:
Spacers

## Slide 4
- PETIROC ASIC : 32-channel,
high bandwidth preamp (GBWP> 10 GHz), <3 mW/ch, dual time and charge
measurement (160 fC-400 pC)
vey fast and low-jitter < 25 ps rms
- 24-ch, TDC of 25 ps time resolution developed by the Tsinghua university is being used to demonstrate the RPC/MRPC time capability
New PCB with pick-up strips read from
both sides is being designed
with the aim to achieve Y-position
determination Y= L/2-v*(t2-t1)/2.
Time resolution can be measured: (t1+t2)- L/v
On-detector Strip
Off-detector Strip
Y
1pe=150fc
Electronics for Multi-Gap CMS-GRPC Detectors

## Slide 5
Electronics for Multi-gap CMS-GRPC detectors
32 strips of 3 mm width
(4 mm pitch)
Return strips outside
the detector
32-ch PETIROC
Tsinghua
FPGA TDC
A PCB was conceived to host : Pickup strips, 2 PETIROC, 2 TDC
A DAQ system was developed. The PCB is intended to equip large chambers
50 cm
IPNL
Test points

## Slide 6
LSB < 20 ps, adjustable
  RMS Resolution < 2 ps, including all noise types other than the quantization noise
  Dead time < 1μs
  The RPC output signal frequency is ~1 kHz (ie. the real dynamic range ~1 ms)
  The TDC dynamic range measurement : from 1 ns to 3 ns depending on :
    Gate unity rms Jitter , TDC reference clock frequency and the frequency of the Ring Oscillators
    Low power consumption (the total power (FEE+TDC) < 3 mW/channel)
  TSMC 130 nm process is chosen according to the technology of PETIROC (OMEGA group).
Requirements for the TDC ASIC development

## Slide 7
FPGA :
TDC_Brick ASIC :
TSMC 130 nm process
Vernier Ring Oscillator technique
Standard cells are used to build the Ring Oscillators (Inverters)
Fine adjusting of the oscillators frequency to tune the LSB of the TDC
A prototype was submitted last year - Nov 2nd 2016
Chronology of TDC works at IPNL (Lyon)
A classic Vernier TDC has been used with success in some physics experiments (Cf [1])
An original technique which allows to control and to adjust the TDC resolution to a few ps has been designed. This architecture has already been tested successfully on FPGAs (10 ps RMS resolution over a range of 1 ns)
Main limitation : cumulated Jitter  customized layout may be needed !
[1] Implementation of sub-nanoseconds TDC in FPGA: applications to time-of-flight analysis in muon radiography
  J. Marteau (IPNL), J. De Bremond D'ars (GR), D. Gibert (GR, IPGP), K. Jourde (IPGP), S. Gardien (IPNL), C. Girerd (IPNL), J.-C. Ianigro(IPNL)
TDC Building blocks have been integrated in an ASIC designed in the IBM 130 nm process.
Standard cells were used to build the Ring Oscillators (XORs gates)
Current TDC work :

## Slide 8: Clock reference of 1 GHz is used as stop signal on the fast oscillator
Slow
Oscillator
Fast
Oscillator
Phase
detector
slow
Counter
Enable
fast
Counter
TDC result
Event (start)
D
Vdd
Q
R
Clk_Ref (stop)
D
Q
R
D
Q
R
Vdd
Reset
Ready
T = (N0*T0)-(N1*T1)
t
1
2
3
4
5
Event
Stop
T
Phase detection
Clk ref
Start
Oscillator stop
T0
T1
Vernier Ring Oscillator TDC principle
1
2

## Slide 9
Vernier Ring Oscillator working principal
1
2
3
4
5
--
--
Ns-1
Ns
1
2
3
--
--
--
Nf-1
Nf
Fast
Slow
Start(event)
Stop(Ref_clk)
T
Is the conversion bin (LSB)
Phase Detection
 It is necessary to be able to finely adjust the oscillator frequency
Where,
(1)
(2)

## Slide 10
TDC block diagram (system view for 1 channel )
Simplified TDC channel
Top Clk ref (40 MHz)
Clk ref.
period
1 to 2 ns
Event (Trigger)
Ready
S
E
R
I
A
L
I
Z
E
R
c
start
Osc.
ASIC (1 ch.)
stop count
stop count
Signal processing Board
In slow calib.
Slow
Oscillator
Fast
Oscillator
c
c
c
Calibration
c
Phase
detector
I2C
start
Osc.
In fast calib.
c
Slow counter
10 bits
Fast counter
10 bits
Fine
counter
Coarse
counter
RST global
Fast Clk ref.
Generator (PLL)
TX_SLVS
RX_SLVS
(Clk ref = k * 40MHz)

## Slide 11
Time measurement chronograms
CLK_ref
Fine counter
0
1
2
3
4
--
--
Nf-1
Nf
0
1
23
Nc
0
CLK_CERN
Top Clk ref (40MHz)
Clk ref (1GHz)
Stop coarse counter
Stop fine counter
Coarse counter
TRIGGER (event)
Ttdc
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
21
22
23
24
25
1
2
3
25
T CLK_ref
Nc-1
Result (T)

## Slide 12
Cadence schematic of a Ring Oscillator in TSMC 130 nm process
INVD4
BUFTD4
AN2D2
11 categories of inverters INVDx
11 categories of tristate Buffers BUFTDx
Choice of INVDx type to build the « R.O »
Choice of tristate Buffers to adjust finely the frequency of the two « R.O » :
  5 buffers are connected in parallel and can be activated with a 5-bit word (1024 LSB combinations )
BUFTDX
A Simple Ring Oscillator (odd number of inverters):
Frequency tuning Ring Oscillator :

## Slide 13
Simulation of the LSB tuning in tsmc 130 nm
We proceed to LSB adjustment (quantization step of the TDC) by :
  Selecting either « buffer mode» or « high impedance mode» (HZ) of the tristate BUF.
Effect on the oscillation frequency | Max | Min
Frequency (MHz) | 1140 | 961
Period T (ps) | 875,7 | 1040,9
Tp (ps/gate) | 43,4 | 36,5
Zoom
LSB vs. code
LSB vs. code
Dt = ± 100 ps

## Slide 14
Cumulated Jitter of « R.O » (Ripple, Edge) in TSMC 130 nm
Code 31
Scheme = ring_osc_jitter_power
Output = Out_F
TR Noise sim moderate
Tsim = 150 ns
1 mV cc @ 10 MHz on VDD
Fosc = 1,1 GHz
MOS Noise + Ripple on VDD
Code 31
Scheme = ring_osc_jitter_power
Output = Out_F
TR Noise sim moderate
Tsim = 150 ns
50 mV cc @ 10 MHz on VDD
Fosc = 1,1 GHz
MOS Noise + Ripple on VDD
The ripple effect is weak : Jitter RMS < 2 ps
Jitter = 1,68 ps
Jitter = 1,96 ps
Cumulated Jitter rms [fs] vs. edge number.
Cumulated Jitter rms [fs] vs. edge number.

## Slide 15
Cumulated Jitter of « R.O » (Power, VDD noise, edge) in tsmc 130 nm
Code 31
Scheme = ring_osc_jitter_power
Output = Out_F
TR Noise sim moderate
Tsim = 150ns
50 mV cc @ ≠ F on VDD (6kHz ->200MHz)
PSD VDD = 10 nV/sqrtHz on 10 GHz
 Noise VDD = 1 mV RMS
Fosc = 1,1 GHz
MOS Noise + Ripple on VDD + noise VDD
Jitter < 3,5 ps
Cumulated Jitter
Edge number

## Slide 16
Cumulated Jitter of « R.O » (Power, VDD noise, edge) in tsmc 130 nm
Code 31
Scheme = ring_osc_jitter_power
Output = Out_F
TR Noise sim moderate
Tsim = 150ns
50 mV cc @ ≠ F on VDD
PSD VDD = 100 nV/sqrtHz on 10 GHz
 Noise VDD = 10 mV RMS
Fosc = 1,1 GHz
MOS Noise + Ripple on VDD + noise VDD
Jitter < 30ps
The effect of ripple is negligible compared to the power supply noise (PSD)
! A particular care must be taken when choosing the voltage regulators on PCB boards !
Cumulated Jitter rms vs. edge number@ diff. Freq VDD .
Cumulated Jitter
Edge number

## Slide 17
Intermediate nodes in the phase detector
Global Floor Plan of the TDC

## Slide 18
Digital processing part of the ASIC
Many thanks to my colleague Hervé Chanal from Pole MicRhAu who designed this part.
TDC Core side
Digital processing part
Data : 33 bits
(from msb to lsb)
  5 bits channel address
  6 bits Fine counter
  11 bits slow counter
  11 bits fast counter
Readout Clock : <160 MHz

## Slide 19
Layout of the submitted ASIC
TSMC 130 nm process
Dimensions :
  2400x2450 mm2
Submitted Nov 2nd 2016
ASIC returned from fab by end of January
Packaging is in progress
Test board must be designed, it will start by beginning of March

## Slide 20
Conclusions and outlooks
Conclusions :
A 20 ps LSB and 2 ps rms noise TDC has been designed et sent to fabrication in TSMC 130 nm process
Noise constraints on power supply (VDD) have been identified
Test card design will start by March 2017
ASIC tests will begin by the end of May 2017
Integration of this ASIC and PETIROC ASIC on the same package :
      Quilt Packaging (QP) ?! A new technique !
Integration of the TDC and a PETIROC on a same substrate
A PhD thesis on this design has began in early February (Amina ANNAGREBAH)
Acknowledgment :
  Mr. Marek IDZIK from the Department of Particle Interactions and Detection Techniques (Krakow) for providing us the SLVS receiver block
  CERN electronics group for the I2C slow control block

## Slide 21
Thank you