## Slide 1: Measurement of the 230Th(n,f) reaction cross-section at EAR-1 and EAR-2 of the CERN n_TOF facility
1 National Technical University of Athens (NTUA), Greece
2 European Organisation for Nuclear Research (CERN), Geneva, Switzerland
3 Uniwersytet Lódzki, Lodz, Poland
4 CEA Saclay, Irfu, Gif-sur-Yvette, France
5 Istituto Nazionale di Fisica Nucleare (INFN), Bari, Italy
6 European Commission JRC, Institute for Reference Materials and Measurements, Geel, Belgium
7 University of Ioannina, Greece
R. Vlastou1, M. Diakaki1,2, A. Tsinganis2, M. Kokkoris1, A. Stamatopoulos1, J. Andrzejewski3, E. Berthoumieux4, N. Colonna5, E. Dupont4, J. Heyse6, N. Patronis7, P. Schillebeeckx6, L. Tassan-Got2, E. Chiaveri2
and the n_TOF Collaboration

## Slide 2: Outline
Measurement of the 230Th(n,f) reaction cross-section at EAR-1 and EAR-2 of the CERN n_TOF facility
55th INTC Meeting, CERN, February 2017
Motivation:
nuclear technology applications
fundamental research of the fission process
Status of data
Proposed experiment
Summary

## Slide 3: Motivation (I)
Nuclear technology applications:
Important for the proposed Th-U fuel cycle
(advantages: radioactive waste management,
non-proliferation).
All neutron induced reactions on Th isotopes
are needed with good accuracy
(For neutron energies: thermal to MeV)
Measurement of the 230Th(n,f) reaction cross-section at EAR-1 and EAR-2 of the CERN n_TOF facility
55th INTC Meeting, CERN, February 2017
Notes: ROSA, ejhghsh
th230 mporei na yparxei mesa sto kaysmo apo thn arxh alla kai na paraxthei mesa ston antidrasthra me (n,xn) reactions gia fast reactors

## Slide 4: Motivation (II)
Measurement of the 230Th(n,f) reaction cross-section at EAR-1 and EAR-2 of the CERN n_TOF facility
55th INTC Meeting, CERN, February 2017
Study cross section close to fission barrier:
structural behavior
=> understanding of fission barrier structure
(barrier shape + states in wells)
Th anomaly:
230Th fission at
barrier energies
Subject of extensive theoretical
investigation:
Vibrational states
(bandheads of rotational bands) in:
Second well (James et al.).
Third well (Boldeman et al.).
Phenomenological barriers
from rearrangement of states
during fission - Hybrid model (Mirea et al).
Need for high accuracy + energy resolution
data in order to test the models
fission
Notes: pronounced

## Slide 5
Very scarce + discrepant data (Very rare isotope, very low cross section)
No data below threshold (only one point at thermal)
Status of data (I)
Measurement of the 230Th(n,f) reaction cross-section at EAR-1 and EAR-2 of the CERN n_TOF facility
55th INTC Meeting, CERN, February 2017

## Slide 6
Few datasets at and above the fission threshold up to 25 MeV (surrogate/indirect measurements, many discrepancies)
Status of data (II)
Measurement of the 230Th(n,f) reaction cross-section at EAR-1 and EAR-2 of the CERN n_TOF facility
55th INTC Meeting, CERN, February 2017
Notes: goldblum: surrogate reaction: (3He,3He') and (3He,α) reactions on targets of 232Th and 236U
meadows: direct: p-Li and d-d (0.7-9MeV) / d on t (1988)
blons: indirect 230Th(d,pf) measurement at Saclay
lynn: direct measurement 7Li(p,n)
muir: Underground nuclear explosion as pulsed neutron source. (Veeser.pdf)

## Slide 7
Status of evaluated data
Measurement of the 230Th(n,f) reaction cross-section at EAR-1 and EAR-2 of the CERN n_TOF facility
55th INTC Meeting, CERN, February 2017

## Slide 8
Measurements are proposed to be performed at n_TOF:
EAR-1: high statistics data + excellent energy resolution mainly at and above the fission threshold.
EAR-2 reasonable statistics + good resolution in the resonance and sub-threshold region.
The overlapping data from both areas (mainly from the threshold region to higher energies): validation of the cross section results.
Reference reactions: 235U(n,f), 238U(n,f) and 10B(n,α).
Proposed measurement
Measurement of the 230Th(n,f) reaction cross-section at EAR-1 and EAR-2 of the CERN n_TOF facility
55th INTC Meeting, CERN, February 2017
Difficulties:
high alpha background (natural 230Th radioactivity).
minimization of activity / target =>minimum mass per target
low 230Th(n,f) cross section
maximization of instantaneous neutron fluence => big collimators
maximization of total mass => stack of many 230Th targets
Notes: difficulty to be faced for both areas

## Slide 9
Targets: Joint Research Centre – Geel, Belgium
preliminary agreement with IRMM already exists, to be made official upon approval of this
proposal.
230Th targets:
material available.
Electrodeposition in the form of thorium dioxide (ThO2) on 25 μm Al backing.
Low mass/activity per sample, large surface
Impurity: 232Th (8.46%): contribution very small and easily subtracted (one hyperpure target for cross check).
Reference targets: 235U, 238U, 10B
(same geometry + backing characteristics).
Experimental setup (I)
Isotope | Purity [%] | Thickness [μg/cm2] | Diameter [cm] | Sample Mass [mg] | Sample Activity [MBq] | No. of samples | Total Mass [mg] | Total Activity [MBq]
230Th | 91.54 | 100 | 8.0 | 5.0 | 3.8 | 6 | 30.0 | 23
Courtesy: J. Heyse
Measurement of the 230Th(n,f) reaction cross-section at EAR-1 and EAR-2 of the CERN n_TOF facility
55th INTC Meeting, CERN, February 2017
Notes: total activity is easy to handle????
a-activity

## Slide 10
Detection system: Micromegas microbulk detectors
(already successfully used at n_TOF for fission (237Np,242Pu, 240Pu))
Experimental setup (II)
FF
tare
target
“amplification region”
FF
existing chamber
up to 10 actinide
targets measured
simultaneously
Electronics: existing preamplifiers, some modifications envisaged based on previous experience.
Acquisition: standard n_TOF Data Acquisition System based on flash-ADCs (12- or 14-bit). Analysis routines already developed.
Measurement of the 230Th(n,f) reaction cross-section at EAR-1 and EAR-2 of the CERN n_TOF facility
55th INTC Meeting, CERN, February 2017

## Slide 11
Expected count rates – beam request
EAR-1:
large (“fission”) collimator (8 cm diameter)
3x1018 protons on target
Measurement of the 230Th(n,f) reaction cross-section at EAR-1 and EAR-2 of the CERN n_TOF facility
55th INTC Meeting, CERN, February 2017
High statistics and resolution cross
section data > 600 keV
(investigation of resonant structure
at threshold + data up to high
energies)

## Slide 12
Expected count rates – beam request
EAR-2:
large (“fission”) collimator (6 cm diameter)
calculations based on TENDL-2015
3x1018 protons on target
Measurement of the 230Th(n,f) reaction cross-section at EAR-1 and EAR-2 of the CERN n_TOF facility
55th INTC Meeting, CERN, February 2017
Reasonable statistics and resolution
from thermal to subthreshold region
(no data exist so far!)

## Slide 13
Summary
Measurement of the 230Th(n,f) reaction cross-section at EAR-1 and EAR-2 of the CERN n_TOF facility
55th INTC Meeting, CERN, February 2017
230Th(n,f) cross section measurement: Important for fundamental research on the fission process / nuclear reactor technology.
The availability of the very rare isotope 230Th at JRC-Geel, provides the opportunity to perform high-quality direct measurement at EAR-1 and EAR-2 exploiting their respective features: The first complete high-accuracy dataset from thermal to tens of MeV.

## Slide 14
EXTRA SLIDES

## Slide 15
232Th(n,f) cross section

## Slide 16
230-232Th(n,f) cross section at resonances
232Th(n,f)
230Th(n,f)
T

## Slide 17
n_TOF neutron flux
small collimators
EAR1-185m,
FWHM = 18mm
EAR2-20m,
FWHM = 21mm

## Slide 18
Expected count rates – beam request
EAR-1:
large (“fission”) collimator (8 cm diameter)
3x1018 protons on target