## Slide 1
  Charge sensitive amplifier based on a regulated cascode gain stage and featuring leakage current compensation
  Compact, single-ended threshold discriminator featuring autozeroing, operated with the 40 MHz clock. This implementation is ideally insensitive to device threshold voltage mismatch  trimming DAC not required
  2-bit Flash ADC for digital conversion immediately after the preamplifier
A 65nm CMOS Front-End with Zero Dead Time for Next Generation Pixel Detectors
L. Gaioni1,3, D. Braga4, D. Christian4, G. Deptuch4, F. Fahim4, B. Nodari5, L. Ratti2,3, V. Re1,3 and T. Zimmerman4
Introduction
The Macro Pixel ASIC
The next generation of pixel chips at the High-Luminosity LHC (HL-LHC) will operate with extremely high particle rates and radiation levels. In the so-called Phase II upgrade, ATLAS and CMS will need a completely new tracker detector, complying with the very demanding operating conditions and the luminosity delivered by the machine (up to 5 x 1034 cm−2s−1 in the next decade). The 65 nm CMOS technology node exhibits a high degree of radiation tolerance and allows the integration of very dense in-pixel analog and digital functions. It is the target technology of the design community for the development of readout chips for the innermost pixel layers of ATLAS and CMS at the HL-LHC.
In the framework of CERN’s RD53 Collaboration, a synchronous analog processor with zero dead time has been designed in a 65 nm CMOS technology. Prototyped in a 16x16 pixel matrix, it includes a low-noise, fast charge-sensitive amplifier featuring a detector leakage compensation circuit and a compact, single-ended comparator with autozeroing capabilities. A 2-bit Flash ADC follows the preamplifier for synchronous conversion.
Measurement results
Charge sensitive amplifier
Topical Workshop on Electronics for Particle Physics, Santa Cruz (CA), USA, September 11 - 14, 2017
1 University of Bergamo
Department of Engineering
and Applied Sciences
Dalmine (BG), Italy
2 University of Pavia,
Department of Electrical, Computer
and Biomedical Engineering,
Pavia, Italy
3 INFN
Sezione di Pavia
Pavia, Italy
4 Fermilab
Batavia IL, USA
Analog Front-end
  Regulated cascode design
  Active feedback transistor Mf:
    1/gm resistor for small signals
    Constant current source for large signals
    M1 provides a DC path for the detector leakage current
    Ri + Ci ensure low-frequency operation of the leakage compensation circuit
  Power consumption @ 1.2 VDD = 4.8 µW
Comparator
  ≈ 5 ns rise time @ Qin=750 e-
  Changing slope by adjusting the preamplifier Id feedback current
  Charge sensitivity G (evaluated on 256 pixels):
  Gmean = 11.0 mV/ke-
  σG = 0.21 mV/ke-
  Equivalent noise charge (ENC) smaller than 70 erms for a preamplifier input capacitance CD =35 fF
  From circuit simulations:
  Leakage compensation circuit for leakage currents up to 14 nA
  Regulated cascode forward gain stage:
    DC Open Loop gain  53 dB
    Cutoff frequency  2.3 MHz
  Comparator able to detect hits in two consecutive bunch crossing periods
  Noise and threshold dispersion data extracted from the hit efficiency curves
  Equivalent noise charge ENC  50 erms (σENC =10 erms)
  Threshold dispersion close to 320 erms, significantly higher than expected  bad simulations settings for the comparator’s second stage. Re-design needed
Operated in two different phases:
reset phase  the comparator gets reset and a proper bias is provided to the two stages – S1, S2, S3 closed
active phase  an active comparison takes place by injecting both the input and the threshold signals Vth at the comparator inputs – S1, S2, S3 open
Qin ≈ 30 ke-
Qin1=800e-
Qin2=800e-
QTH=600e-
Hit efficiency
Noise
Threshold
5 Institute of Nuclear Physics (IPNL), CNRS/IN2P3, Lyon, France
Effect of Id feedback current on the preamplifier response
Charge sensitivity across pixels
Equivalent noise charge
Preamplifier output response for small and large signals