## Slide 1: The ND280 Basket Structure
Peter Sutcliffe
University of Liverpool
20th March 2017

## Slide 2: Stainless Steel basket Dimensions
Design comprised of mainly 300 x 100 x 6 and 200 x 100 x 6 Stainless RHS.
6650mm
Internal
2320mm
Internal

## Slide 3: Detector Layout Total mass of detectors for analysis 29,000Kg
D/Stream
ECAL
TPC
FGD
TPC
TPC
FGD
POD
ECAL
POD
ECAL
POD
TARGET
Detector | Mass (kg) | No. Off
ECAL | 6000 | 1
TPC | 1000 | 3
FGD | 1500 | 2
POD ECAL | 3000 | 2
POD TARGET | 11000 | 1

## Slide 4: Stainless Steel basket
Manufactured at Durham Sheet Metal, South Shields’ Near Newcastle

## Slide 5: Basket Stand
Basket stand is manufactured from Carbon steel and was made at Priory Engineering on the south coast

## Slide 6: Services Rack

## Slide 7: Full assembly at Daresbury Lab

## Slide 8: Load testing at Daresbury Lab
Loaded up with concrete blocks in the correct detector positions to 29 tonnes

## Slide 9: Testing at Daresbury
Loaded up to 30 tonnes
Total deflection 12mm
ANSYS analysis shows 9mm

## Slide 10: Detector attachment to Basket

## Slide 11: Basket machined bosses
Basket has several machined bosses which were positioned to attached all the original detectors.

## Slide 12: Downstream ECAL
Main vertical support is on the machined pillar
2 machined location bosses to attach tie bars

## Slide 13: TPC
TPC is attached to two rails supported on two angle brackets and fastened to machined bosses on the basket

## Slide 14: FGD
Attached to two right angle brackets fixed to machined bosses on the basket.
Unsure of final attachment...
Original design
‘Final’ basket design

## Slide 15: P0D detectors
P0D fixed using cross member lower bars and upper bars.
Bars fixed using angle brackets attached to machined bosses on the basket

## Slide 16: STEP files and Drawings
Attached are 2 drawings and step files
  NP48-01-03 Basket
  NP48-01-26 Basket and support bars
Thanks for Listening