## Slide 1: Coming soon… Diagnostics conceptual design for a Eupraxia-like (lite) machine
Alessandro Cianchi
University of Rome Tor Vergata and INFN
With a lot of contributions from Enrica Chiadroni, Nicolas Delerue, Claire Simon, David Alesini, Alessandro Gallo, Massimo Ferrario, James Rosenzweig

## Slide 2: General statements
Conventional accelerators diagnostics is not a big challenge
An X-band accelerator is very compact, small, and also the diagnostics must be compact as well.
There are several challenges for the diagnostics in the PWFA regime:
  The bunch length is very small, down to few mm
  The bunch size is also very small, down to few mm
  SINGLE SHOT!
For the conventional accelerator there are well-known solutions
Diagnostics after the plasma acceleration will be affected by
  Capture Optics
  Driver contamination
  Lack of single shot emittance diagnostics

## Slide 3: Beam size
  Fundamental to measure the envelope and properly match the beam in the different accelerator sections
  Used to measure energy and energy spread in spectrometer also
  Fundamental in several other measurements
  Compact design is required
  COTR mitigation problem: solution available
    But not for small beam size smaller than few um

## Slide 4: Longitudinal diagnostics
X-band RFD (limited to few fs)
EOS (Electro Optical Sampling used also with time of arrival monitor), limited to about 40-50 fs
Coherent radiation spectrum (hopefully single shot, some developed, others in progress): not limited in principle
More to come: ??
  TDP (Transverse Deflecting Plasma) limited to hundreds of as

## Slide 5: Charge and trajectory
Bergoz Turbo- ICT (down to 50 fC, up to 300 pC) for the charge
Stripline BPM or button BPM for S band linac
Cavity BPM (likely C or X band) for the rest of the machine
Possibility to use the X band structures as BPM
  Use of the dipole mode to estimate the beam position
  Needs to be calibrate vs conventional BPM
  Used in Califes@CERN
  Developed at NLC
100 mm
Notes: PSI just an example will not fit, NLC BPM should be ok

## Slide 6: More details
This afternoon in WP5