## Slide 1: 6D Characterization of Witness Beam before Injection in LWFA
B. Marchetti
1st EuPRAXIA Collaboration Week
DESY, 19-23 June 2017

## Slide 2: Characteristics of Witness Beams
At SINBAD we are investigating the range Q=0.5pC-30pC, especially the limit in the characterization of very low charge and ultra-short e-bunches.
From EuPRAXIA parameter table LWFA with external injection:

## Slide 3: 6D e-Beam Characterization includes
Bunch Length and Longitudinal Charge Profile
Longitudinal Phase Space
Slice emittance on different transverse planes
3D Reconstruction of e-Bunch Charge (new technique, relies on novel design of TDS not yet experimentally tested)
original
measured
original
measured
Simulations by D. Marx,
More details in joint WP3-WP5
Meeting Wednesday 16.00-18.00

## Slide 4: General idea of Lattice Design
RF cavity:
Frequency f = ω/(2π)
Peak deflection voltage Vy
Linac
Fig. Credits: D. Malyutin PhD thesis
e-bunch:
Energy E
Vertical emittance εy
RF cavity:
Frequency f = ω/(2π)
Peak deflection voltage Vy
Longitudinal Resolution:
High frequency ~12 GHz (X-band) allows 3-4 times higher resolution than S-band

## Slide 5: Resolution Range EuPRAXIA case
εn=0.3mm*mrad
Δφ = π/2
f=12GHz
εn=1mm*mrad
Δφ = π/2
f=12GHz
Typical β function after bunch compression <30m.
At low energies (100 MeV) the e-beam evolves relatively quickly (the e-bunch properties change along a few m drift or matching lattice).

## Slide 6: Technical Issues to be addressed in the WP5 discussion
Resolution & lattice design:
At which energy is/are the diagnostics line/s?
High β - low V option vs low β - high V option
Integration of diagnostics line with focusing to plasma
Limits high voltage TDS operation:
RF Phase jitter
Arrival time beam jitter
Temperature stability of the cavity
Limits high resolution measurement at low charge
Signal to noise ratio on the measurement screen