## Slide 1: International Review of the Cooling and Ventilation Systems Design for HL-LHC Introduction to the HL-LHC project
Laurent Tavian, CERN, ATS-DO
14 March 2017- CERN

## Slide 2: Table of contents
Main goals and upgrades of the LHC machine
The HL-LHC project structure and the integration of the cooling and ventilation package
The master schedule of the HL-LHC project

## Slide 3: Large project timeline
1980
1985
1995
2000
2005
2010
2015
2020
2025
2030
2035
1990
2040
Construction
Physics
Upgr
LEP
Construction
Physics
Proto
Design
LHC
~25 years
Construct
Physics
Design
HL-LHC
the High-Luminosity LHC project
or
the Hi-Lumi LHC project
Increase by a factor 10 of the integrated luminosity delivered to the experiments

## Slide 4: Paths to high luminosity
Beam-beam effect precludes too low crossing angle
Increase bunch population
(number of protons)
Reduce beta at collision
(bunch size)
Reduce emittance
(spread of particles in position and momentum)
Increase R = reduce crossing angle?

## Slide 5: The HL-LHC project From accelerator physics to technology
Increase bunch population
Reduce beta at collision
Reduce emittance
Reduce crossing angle
Increase intensity & brightness of injectors: the LIU project
Limit beam-beam effect
“Crab” cavities
Accelerator physics
Accelerator technology
New low-beta quadrupoles
More powerful cryogenics
Improved collimation
Improved machine protection
Stronger Radiation to Electronics  relocation in new caverns and galleries
Ph. Lebrun

## Slide 6: HiLumi LHC landmarks

## Slide 7: The Inner Triplet region with in-kinds
SC Links
D1
DFX
CP
Q3
Q2b
Q2a
Q1
Service gallery (UR)
Connection to LHC (UL)
TAXS
DFM

## Slide 8: The MS region with in-kinds
Crab cavities
D2
Collimators
TAXN
Service cavern
UA gallery
Q4
(BBLR)
Staging of crab cavities:
Start with 2/4 units per side
Keep the option of installing 4/4 units per side

## Slide 9: HL-LHC Project structure and WP17

## Slide 10: Technical infrastructure inventory
WP17.1: Civil engineering
WP17.2: Electrical distribution
WP17.3: Cooling and ventilation
WP17.4: Access & alarm system
WP17.5: Technical monitoring system
WP17.6: N/A (Survey  WP15.4)
WP17.7: Transport
WP17.8: Contribution to SM18 upgrade
WP17.9: Logistics and storage
WP17.10: Operational safety
The main
cost drivers of the technical infrastructure!

## Slide 11: Technical infrastructures at Point 5
SU chillers & pumping stations
SU Ventilation units
SD He refrigerator
SF cooling towers
SHM Helium compressor station

## Slide 12: Underground structure (e.g. US/UW cavern)
Cooling & ventilation
Cold box
Transformers
Safe room
Ventilation & smoke-extraction ducts

## Slide 13: Master schedule
Courtesy of Planning team

## Slide 14: WP17 schedule (w/o civil-engineering)
Courtesy of Planning team

## Slide 15: 2016 downtime per system of LHC machine
Technical infrastructure faults have a large impact on overall availability
 Good reliability mandatory

## Slide 16: Introduction to the review
Recommendations of the last C&S Review (Oct’16)

## Slide 17: Thank you!