## Slide 1: Difference in transfer function between Q2a and Q2b
E. Todesco
12 January 2017 - CERN

## Slide 2: THE PROBLEM
  What is the difference in the transfer function between Q2a and Q2b ?
  Spread of the quadrupole transfer function:
    Main quadrupole: 13 units (one sigma)
    MQXA: 5 units (one sigma)
    Guess for MQXF: 10 units (one sigma)
  There will be the possiblity of having sorting
    A Montecarlo gives a 1/3 probability of having a difference between Q2a and Q2b below 5 units
    With sorting this increases to 2/3 – but 1/3 are still larger than 5 units, and 17% larger than 10 units
  To get down to less than 5 units one has to couple the sorting with other methods to control the TF

## Slide 3: THE PROBLEM
Other methods to control the TF:
  Lengths of iron laminations
  One can change up to ±10 units with a change of ±100 mm of length of non magnetic pads
  Problem
    If the length has to be increased, peak field increases – but one could acts always in the same direction (i.e. having two magnets with TF difference, reducing the larger TF
    The action has to be done before final assembly so it requires some additional manpower – to be analysed
  In principle we see showstoppers not allowing to control the TF difference within 10 units