## Slide 1: Wish list for wire MDs
Y.Papaphilippou, G.Arduini, S.Fartoukh, R.Jones, D.Pellegrini, S.Redaelli, A.Rossi, H.Schmickler, G.Sterbini, R.Tomas (CERN),
M.Fitterer, A.Patapenka, A.Valishev (FNAL)
Second workshop for wire experiment for LRBB compensation, 20/03/2017

## Slide 2: Outline
List of MD studies for 2017
  Commissioning (beyond HW tests), preparation (crossing angle scans) and compensation tests
    Goals and procedures
    Beam parameters
      Intensity, emittance, train composition
    Machine configuration
      Energy, optics, crossing angle, orbit control, tune, chromaticity, octupole current
    Wire settings
      Position (alignment) and currents L/R of IP5
    Observables and associated instrumentation
    Further beam-beam wire related studies, including synergies with other MDs
    Prioritization (following 1, 2, 3, 4)
  MD time request and time-line
Key simulation studies for preparing MDs

## Slide 3: Wire impact on single beam - goal
Goal: Test and calibrate the effect of the wires in a single beam
  Need to measure impact of wires on beam orbit, tune, beta-beating, chromaticity, tune-spread, coupling, RDTs
  Calibrate wires and estimate orbit and tune feedback functions during the compensation tests
  Align wires with respect to the beam (vertical orbit, coupling)
  Similar measurements for the external wires can be foreseen, but also for negative polarity and with vertical position at non-zero, e.g. @ 45o degrees
  Estimate impact in lifetime and emittance (tails, halo?) and compensate with other wire
See presentation of G.Sterbini
Priority 1, 2, 3, 4

## Slide 4: Wire impact on single beam – set-up
Energy: All can be done at 450 GeV
  Qualification of tune and orbit feed-forward would be desirable at 6.5 TeV
Beams required: Only beam 2
  Could be compatible with parallel studies using beam 1
Beam composition and intensity: Single nominal bunches of 1.3 x 1011 ppb
  ome tests can function already with probe
Emittances: Nominal BCMS, i.e. ~1.5-2.0 μm.rad
Optics: Nominal @ injection with nominal injection tunes, octupoles and chromaticity settings
  More exotic options if testing compensation or lifetime impact can be foreseen (for example beam2 squeezed with beam1 nominal, equal β aspect ratio at the wire,…)
See presentation of G.Sterbini
Priority 1, 2, 3, 4

## Slide 5: Wire impact on single beam - procedure
Procedure:
  Alignment
    Move the TCT collimators with 1 wire at a time and measure impact on vertical orbit, align the jaw to minimise this.
    Measure coupling.
  Orbit, tune
    For fixed wire distance (jaw at ~6 σcol), measure impact of different currents to the beam orbit and tune
    Do the same for fixed current, moving the collimator jaw.
    Set-up orbit and tune feed-forward
  Chromaticity: With corrected orbit and tunes, measure impact in chromaticity (maybe also non-linear) for different currents
  Beta-beating, tune-spread, RDTs: Usual optics correction set-up
  Repeat above for external wires and negative polarity
  Lifetime and emittance: With corrected orbit and tunes, measure impact in lifetime and emittance evolution. Compensate with other wire (needs special optics)
Time needed: 1.5 x 8 h, 2 x 8 h, 3 x 8 h, 4 x 8 h
See presentation of G.Sterbini
Priority 1, 2, 3, 4

## Slide 6: BBLR Compensation preparation - goal
Goal: Measure the crossing angle reduction impact on lifetime
Ideally, part of the commissioning
  Synergy with crossing angle levelling setting-up
Energy: 6.5 TeV
Beam composition: 2-3 colliding trains in beam1 and 2 (without/with IR8), a few single bunches in beam 2
  With full long-range, PACMAN-L/R, non-colliding
Intensity: Nominal @ 1.25 x 1011 ppb
Emittances: Nominal for trains i.e. 2.5 μm.rad for BCMS, some nominal single bunches and some blown up by ADT to 4-5μm
  Optics measurements can be done with pilot
Optics: Nominal @ collision with nominal tunes, octupoles and chromaticity settings
  β* of 40 cm, but probably 33 cm if commissioned
Priority 1, 2, 3, 4

## Slide 7: BBLR Compensation preparation - procedure
Procedure:
  Reduce crossing angle in steps
  Measure impact on lifetime of different bunches, while keeping constant orbit and tune
  Monitor impact in emittances, luminosity, halo, losses
  Measure optics, e.g. beta-beating, coupling, chromaticity, tune spread, RDTs
Time needed: 1.5 x 8 h, 2 x 8 h, 3 x 8 h
Priority 1, 2, 3, 4

## Slide 8: BBLR Compensation goal
Goal: Prove BBLR compensation with powering wire when crossing angle reduction impacts beam lifetime
  Leading order octupole effect compensation possible with present hardware
Energy: 6.5 TeV
  Partial squeezed optics @ injection could be envisaged
  Simulation work to be done and optics commissioning overhead
Beam composition
  A few single bunches (around 3-4) in beam 2 (weak beam) spaced by > 15x25 ns for machine protection (abort gap kicker rise time)
  With full long-range, 1 non-colliding
  As many trains in beam 1
Intensity: Nominal of 1.25 x 1011 ppb for strong (or highest possible from SPS)
Emittances: Nominal for trains i.e. 2.5 μm.rad for BCMS, some nominal single bunches and some blown up by ADT to 4-5μm
  Small enough to guarantee that long range kick identical to 1/r field corrected by wire for all LRs
Optics: Nominal @ collision Nominal @ collision with nominal tunes, octupoles and chromaticity settings
  β* of 40 cm, but probably 33 cm if commissioned
  Un-squeezed optics in IR1, only if synergy with IR compensation MD
Crossing angle:
  Nominal in both IR1 and 5, no collisions in IR2 and 8
  Moving only one IR crossing angle could be envisaged
Priority 1, 2, 3, 4

## Slide 9: BBLR Compensation procedure
Procedure:
  Inject and ramp up a few bunches in beam 2 to commission orbit and tune feed-forward with wire (ideally during calibration phase) and blow-up effect of ADT
    Compatible with parallel tests in beam 1
  Inject, ramp-up and collide strong (beam 1) and weak beam (beam 2)
  Set internal TCT/L jaw at 5-6σcol (including other collimation adjustments enabling this)
  Reduce crossing angle in steps, while keeping orbit and tune constant
  Observe lifetime reduction and ramp-up the current of each wire in steps, observing lifetime recovery in colliding weak beam
    Note that if collimator distance in mm is equal L/R from the IR, wire current should be the same, whereas if distance is equal in σ, L/R current should be adjusted independently
  Monitor emittance, luminosity, halo, losses
  Repeat the test with different weak beam flavours (Pacman-L, Pacman-R, without HO and non-colliding)
  Measure optics, e.g. beta-beating, coupling, chromaticity, tune spread, RDTs, with wire compensation
  Repeat the test with IR1 crossing angle fixed and/or separated in IR1
  Repeat the test using the wires in external jaw
Time needed: 3 x 8 h, 3.5 x 8 h, 4 x 8 h, 5 x 8 h
Priority 1, 2, 3, 4

## Slide 10: Observables and instrumentation
Observables instrument
  Lifetime FBCT
  Losses (D)BLMs
  Halo coronograph
  Emittance BSRT
  Orbit, crossing angle BPMs, DOROS
  Tune, chromaticity BBQ, Schottky
  Tune-spread BPMs, BBQ, BTF
  RDTs BPMs, BBQ
Priority 1, 2, 3, 4
See presentations of B.Salvachua, G.Trad, T.Levens, R.Tomas, X.Buffat

## Slide 11: Other compensation studies and spin-offs
BBLR Compensation with octupoles (arc, IR)
Flat optics
Wires are powerful enough to be used for linear and non-linear optics studies but also collective effects
Measuring tune-spread, RDT, instability studies, halo cleaning
See presentation of S.Fartoukh
See presentation of M.Fitterer, X.Buffat and R.Tomas

## Slide 12: MD schedule and time-line
Only 15 MD block days
  Possibility for additional days after TS2 if LHC lumi goal reached
Wire MD requests 48 h for strict minimum (96 h for more complete studies)
Ideally wire calibration and crossing angle scanning should profit from recommissioning time in May (~16h)
Would like to profit already from the 1st MD block for most of the studies
See presentation of R.Tomas

## Slide 13: Outlook
Devise a strict minimum commissioning and MD plan that demonstrates BBLR compensation already in 2017
Continue simulations studies for consolidate experiment
Start discussing configuration for 2018 and possible optics options (injection, flat optics, etc.) still using the present H/W solution
Start a reflection for the optimal configuration and hardware to put in operation for (HL-)LHC

## Slide 14: Thanks for your attention