## Slide 1: BLM DIAMOND system
Future Acquisition and Processing Electronics
With the contribution of: Ewald Effinger, Jiri Kral, Stephane Bart Pedersen, and Chen Xu

## Slide 2: Current Installations

## Slide 3: Diamond types
CIVIDEC
  Pt. 2,8 | Pt. 6 | Pt. 7 – total 8 detectors
  Copper cables
BCM1F
  Pt. 4 – total 4 detectors
  Fiber (analogue)

## Slide 4: Electronic types
LeCroy scopes
  Custom BI FESA server
ROSY System
  2 sets of 4-channel picosecond-resolution oscilloscopes, first for waveform digitization, second with FPGA for online time-loss histograms.
  Embedded PC with Linux server for device configuration and data output.

## Slide 5: Some User Cases
Direct waveform output to IQC triggered by beam-injection pre-pulse (Pt2,Pt8)
Sub-minute continuous beam loss waveforms with bunch-resolving compatible sampling rate
Level triggered waveform acquisition as fast UFO-buster in Pt7

## Slide 6: VFC/ADC electronics
Standardisation and long term maintenance

## Slide 7: VFC-HD Carrier module
Beam Synchronous Timing
Ethernet (White Rabbit)
4 SFP for fast connections to the Front-ends
HPC-FMC slot
Rear Transition Module connection
DDR3
ARRIA V FPGA
VME64x interface
P0 User defined connection
BE-BI development as the future carrier board for most of its systems

## Slide 8: FMC-1000 Mezzanine
FMC-HPC module with
  2x1000 MSPS 14-bit ADCs,
  2x1000 MSPS DACs,
  DC coupled A/D & DACs

## Slide 9: Settings/Variables
Acquisition/Binning frequency:
  Fixed acquisition at 650 MHz (limited by carrier)
  Selectable binning 1.54 ns – 50 ns , i.e. multiples of base frequency
  Binning by averaging on the FPGA input stage
  Separate setting for histogram and waveform binning
Histogram refresh and reset:
  Refresh at 10 ms – 1.2 s
  With reset at each refresh or at basic period
  Limitation is only the maximum number of hits/bin (now at 5.8 s)
Histogram threshold level:
  Complete ADC range
  Counting at rising edge of the bin or each bin over threshold
Waveform Capture trigger event:
  External (timing events)
  Internal (edge, continuous)
Capture bunch selection:
  all bunches or a single bunch

## Slide 10: Some examples
Single on-board FPGA:
  Scope and histogram in parallel for all channels (without splitting the analogue signal)
  Continuous histograms
Dual DDR3 memories:
  4000 LHC turns waveform of all bunches
  14 m LHC turns waveform in single bunch
  Note: it will take a few minutes (~ 5 m) to readout the complete waveform
Long term possibilities:
Connect to BIS
… completely BI owned system

## Slide 11: Deployment/Future
Already a prototype installation in the lab
  Major features available in firmware and server
  Expert GUI available for the histogram and waveform
First deployment at LSS1 of SPS
Four more mid-2017
  locations to be decided
Gradually add features in firmware and server
  Add settings and more features
  Add monitoring of the system
  Connect to the Logging and PM servers

## Slide 12: Thank you