## Slide 1: First thoughts about the FCC-ee polarization wigglers Attilio Milanese, Marek Bohdanowicz 23 Mar. 2017

## Slide 2
The reference example – also for the nomenclature –
is the LEP polarization wiggler

## Slide 3
Tentative (realistic) parameters are used so far
gap
could be changed to 80 mm, as last version of dipoles
distance between B+ and B- poles
so far dictated by coil design
excitation range
if B is fixed (or within a small range), trims could be avoided
field quality
∫B overall (central and within ± lateral distance)
B+ and B- uniformity over ± lateral distance, possibly also longitudinally
 |  |  | FCC-ee | LEP
full gap height | h | [mm] | 90 | 100
central field | B+ | [T] | 0.7 | 1.0
central pole length | L+ | [mm] | 700 | 760
asymmetry ratio (L-/L+) | r | [/] | 4 | 2.5
to be discussed

## Slide 4
This is a first magnetic concept, which keeps some of the ideas of the LEP design, in particular the “floating” poles
mass ≈ 4 tons
beam
central main coils
side trim coils
wider (300 mm) central pole
narrower (200 mm) lateral poles

## Slide 5
With these poles and distances, the overall length is ≈ 4 m (it was 3 m for LEP) – a “self cancelling” single unit looks feasible
beam

## Slide 6
The plot of central B vs. a longitudinal axis looks as expected
center
cutout for trim coil
start of L-
end of L+
end of L-
By [T]
z [mm]
350
260
1400

## Slide 7
The self cancellation of the field is promising – the simulation is with trim coils off, realistic nonlinear iron and (very) limited overall optimization
x [mm] | central B+ [mT] | ∫B [mTm]
0 | 652.54 | 3.22
10 | 652.59 | 3.19
20 | 652.80 | 3.05
30 | 653.22 | 2.73
DB/B for central B+
at 1∙10-4 at 10 mm radial
at 10∙10-4 at 30 mm radial
3.2 mTm means
0.02 mrad at 45 GeV
NI = 2×31700 A
P ≈ 50 kW

## Slide 8
requirements
iterate on field, pole (effective?) lengths, lateral / longitudinal field homogeneity, etc. – maybe tracking would be helpful?
magnetic design
among other things, explore in particular other coil geometries, as the saddle shape introduces saturation
Conclusions
shall we propose a prototype
(ex. scale 1:4, overall length ≈ 1 m)
to be ready for the CDR?
at the level of a feasibility investigation such a wiggler looks indeed feasible

## Slide 9
thank you