## Slide 1
WP11: electron and proton beam testing
J. Schwindling / CEA Saclay
ARIES kickoff meeting, CERN 4-5 May 2017

## Slide 2: Goal of WP11
Testing of instrumentation, beam optics, RF equipment, accelerator components with low-medium energy proton and electron beams
Also synchrotron radiation, RF, neutrons
5 installations: ANKA, FLUTE, IPHI, SINBAD, VELA

## Slide 3: Test Facility ANKA at KIT
KIT Synchrotron
Circumference: 110.4 m
Energy range: 0.5 - 2.5 GeV
Beam current up to 200 mA
RMS bunch length: 45 ps (for 2.5 GeV), down to a few ps (for 1.3 GeV)
ANKA has been in operation for more than 15 years
2016-01-01 Foundation of the KIT Institute for Beam Physics and Technology
2016: IBPT operated the storage ring 3200 hours
IBPT has dual mission
  promote cutting-edge accelerator research
  supply synchrotron radiation for users at KIT and collaborating partners

## Slide 4: ANKA in ARIES
Give access to:
  Electrons at the accelerator
  Synchrotron radiation
Fast –gated
intensified
camera
2.7 MHz, sub-ps
Electro-optical
Monitor
BMBF-Verbund Speaker
A.-S. Müller, 2016 - 2019
05K16VKA
Fast ps THz
detectors
Coating studies
8 beam periods
2.5 days + preparation
24 hours / day
Examples of devices / studies
www.ibpt.kit.edu/anka

## Slide 5: Test Facility FLUTE at KIT
FLUTE (Ferninfrarot Linac- Und Test-Experiment)
  Test facility for accelerator physics
  Experiments with THz radiation
Gun
Linac
Bunch compressor
THz
Laser running, e gun and first diagnostic section for 7 MeV assembled
First experiment autumn 2017
www.ibpt.kit.edu/flute

## Slide 6: FLUTE in ARIES
Laser
beam
Gun
Linac
Laser lab
Chicane
15 Meter
Topview FLUTE hall
THz lab
Klystron
Serve as a test bench for new beam diagnostic methods and tools
Develop single shot fs diagnostics
Synchronization on a femtosecond level
Systematic bunch compression studies
Generate intense THz radiation
Compare different coherent THz radiation generation schemes in simulation and experiment
8 beam periods
5 days + preparation
8 hours / day

## Slide 7: IPHI at CEA Saclay
The High Intensity Proton Injector was built and is being commissioned at CEA Saclay through a CEA – CERN – IN2P3 collaboration
Design performances are 3 MeV – 100 mA – CW proton beam (300 kW)
First beam accelerated in Spring 2016 at low duty cycle (~ 1.5 kW)
Power will be increased gradually in S2 2017
The IPHI RFQ
beam
SILHI source
95 keV
100 mA
RFQ
Diagnostic lines

## Slide 8: IPHI in ARIES
IPHI will provide:
  Protons at 3 MeV, 1 mA to 100 mA, duty cycle 1 ms / 1 Hz to CW
  Access to 352 MHz RF platform (CW or pulsed, ~ 2 MW peak power)
  Neutrons (109 – 1010 n/s)
Neutron production and moderation device @ IPHI in June 2016
Beam in IPHI in April 2016
12 beam periods
5 days + preparation
8 hours / day

## Slide 9: SINBAD at DESY, Hamburg
A dedicate accelerator R&D facility currently under construction at DESY
Reusing the old DORIS tunnel to set up multiple independent experiments
E = 100 MeV, charge: 0.5 - 20 pC, bunch length: few fs, transverse norm. emittance < 0.5 mm*mrad, arrival time jitter stability < 10 fs RMS, rep-rate: < 50Hz
Available: spring 2019
Old DORIS accelerator removed
Building refurbished
Beam line design frozen
Infrastructure installations starting
Procurement of RF-stations, beam line elements,...

## Slide 10: SINBAD in ARIES
TNA - access starting in spring 2019
Access will be granted to the normal conducting, S-band 100 MeV electron linac
Available experimental space in default location:
  ca 3m wide
  length preferably < 4m
9 beam periods
5 days + preparation
14 hours / day

## Slide 11: VELA at STFC Daresbury
VELA = Versatile Electron Linear Accelerator
S-Band photo-injector
Up to 250 pC bunch charge
6 MeV beam energy (upgrade to 40 MeV in progress)
10 Hz repetition rate (upgrade to 100 Hz in progress)
Copper photo-cathode driven by UV laser
1 mm profile FWHM at the cathode
10 MW klystron

## Slide 12: VELA in ARIES
VELA has two experimental areas available:
  Beam Area One
  2 metre long experimental vacuum chamber
  Quadrupole pair for capture post experimental region
  Faraday cup, YAG:Ce screens, non-invasive BPMs
  Beam Area Two
  Customer configurable bunker
 | J | F | M | A | M | J | J | A | S | O | N | D
2017 |  |  |  |  |  |  |  |  |  |  |  | 
2018 |  |  |  |  |  |  |  |  |  |  |  | 
2019 |  |  |  |  |  |  |  |  |  |  |  | 
2020 |  |  |  |  |  |  |  |  |  |  |  | 
2021 |  |  |  |  |  |  |  |  |  |  |  | 
 |  | Not available |  |  |  |  |  |  |  |  |  | 
 |  | Low availability |  |  |  |  |  |  |  |  |  | 
 |  | High availability |  |  |  |  |  |  |  |  |  | 
Availability, subject to change
VELA/CLARA Jan 2017
14 beam periods
3 days
8 hours / day

## Slide 13: Final words
All installations:
  provide local support for users
  need time to check experiment feasibility, safety issues… requests should be sent well in advance to the task leader and to jerome.schwindling@cea.fr
A User Selection Panel is being setup
Task | Installation | Location | Task leader | Beam periods | In operation
11.1 | ANKA | KIT | marcel.schuh@kit.edu | 8 periods x 2.5 days x 24 h | Yes
11.2 | FLUTE | KIT | marcel.schuh@kit.edu | 8 periods x 5 days x 8 h | End 2017
11.3 | IPHI | CEA Saclay | jerome.schwindling@cea.fr | 12 periods x 5 days x 8 h | End 2017
11.4 | SINBAD | DESY | ulrich.dorda@desy.de | 9 periods x 5 days x 14 h | Spring 2019
11.5 | VELA | STFC Daresbury | anthony.gleeson@stfc.ac.uk | 14 periods x 3 days x 8 h | Yes