## Slide 1: Status and Summary of the Impedance Results for the LIU Wire Scanners Christine Vollinger with help and support from: T. Kaltenbacher, P. Kramer, A. Lasheen, M. Migliorati, J. Repond, B. Salvant and input from: D. Amorim, T. Rijoff

## Slide 2: LIU WS: Machine Element Impedances
  Status of qualification for installation in the PSB, PS, SPS.
  Status of simulations of mode-induced wire heating.
  Work plan up to LS2.

## Slide 3: 1- Beam Impedance Evaluation

## Slide 4: Evaluation of PSB Wire Scanner
RF- measurements were carried out on the PSB WS.
Probe-to-Wire measurements
via Hybrid to distinguish magnetic and
electric mode coupling to the wire.
Probe-to-Feedthrough measurements
(to see additional modes).
Probe-to-Probe measurements
Feed-through

## Slide 5: Evaluation of all Wire Scanners
EM-simulations were carried out on the PSB WS, PS WS, SPS WS.
EM-model for the PSB WS
“Cover” of the rotating mechanism helped reducing EM-disturbances;
Model is asymmetric w.r.t. beam axis

## Slide 6: PSBooster WS: S-parameter vs. Eigenmode
Rather strong resonances
at 812 MHz and 867 MHz.
Courtesy: T. Kaltenbacher

## Slide 7: Beam Impedance Results PSBooster WS
Courtesy: T. Rijoff

## Slide 8: Transverse Beam Impedance Results PSB, PS & SPS WS
PSB:
  Effective impedance is ~ 1kOhm/m per wirescanner in both transverse planes.
   negligible
  Modes sit 1 to 2 orders of magnitude higher in frequency compared to the beam spectrum (well beyond 100 MHz compared to ~10 MHz).
   would not be considered in the current way of analysing instabilities.
  Furthermore, computed modes are in the kOhm/m to 100 kOhm/m range, which is reasonable for such a device, and not expected to change stability thresholds.
PS:
  Effective impedance is ~ 1kOhm/m per wirescanner in both transverse planes.
   negligible impact on global impedance.
  DELPHI beam dynamics simulations expect no impact from modes on transverse stability.
SPS:
  Effective impedance is ~ 1kOhm/m per Wirescanner in both transverse planes.
   negligible impact on global impedance
  DELPHI beam dynamics simulations expect no impact from modes on transverse stability
 No visible showstopper expected from transverse plane

## Slide 9: Longitudinal Beam Impedance Results PSB, PS & SPS WS
These conclusions are a team effort; beam dynamics evaluations from:
PSB transverse impedance →T. Rijoff, B. Salvant.
PS and SPS transverse impedance → D. Amorim, B. Salvant.
PSB longitudinal impedance → D. Quartullo.
PS longitudinal impedance → A. Lasheen, M. Migliorati.
SPS longitudinal impedance → J. Repond, A. Lasheen.
Note that for PSB and PS, longitudinal impedance models are in development stage and hence these results are preliminary!
  PSB:
  Modes sit 1 to 2 orders of magnitude higher in frequency compared to the beam spectrum (well beyond 100 MHz compared to ~10 MHz).
   to give a more detailed evaluation of MW-instabilities, model is in development.
PS:
  Impedance impact was estimated from analytical formulae.
   Preliminary results show only small contributions that are considered not critical.
SPS:
  Beam dynamics simulations are carried out showing no significant impact on intensity threshold.  negligible impact on global impedance.
 No visible showstopper expected from longitudinal plane

## Slide 10: 2- Evaluation for Wire Heating

## Slide 11: PSBooster WS: RF-meas vs. Simulation for 2 Fork Positions
Measurement
Simulation
Dependence on fork position,
But 812 MHz resonance stays.

## Slide 12: PS, SPS WS: Simulation for Different Fork Positions
Courtesy: T. Kaltenbacher
Simulation
523 MHz
882 MHz
known eigenmode

## Slide 13
EM-Field Configuration – 135 deg for PS/SPS WS
523 MHz
882 MHz
Highest induced power observed at 523 MHz and 882 MHz at 135 deg position.

## Slide 14: Beam Induced Power Estimation
Wire conductivity: s≈ 7.46 x 104 S/m.
Coupling extracted from eigenmode
simulation.
LIU beam specification used.
machine | tot. loss in wire [W/turn] | e.g. [W/turn]
PS | 0.01 | 0.01 @ 874 MHz
SPS | 0.11 | 0.11 @ 523 MHz
Values for 0 deg fork position (parking pos.)
machine | tot. loss in wire [W/turn] | e.g. [W/turn]
PS | 0.03 | 0.02 @ 882 MHz
SPS | 1.98 | 1.36 @ 523 MHz 0.51 @ 882 MHz
Values for 135 deg fork position
PS/SPS WS
SPS beam (blue); WS long. Impedance
for 135 deg (green)

## Slide 15: 3- Work Plan until LS2 (tentative)

## Slide 16
Bench measurements on PS and SPS prototypes
  Measurements with a real wire might give more insight (?).
Measurements with CLEAR beam:
  on simple tank;
  on wire scanner equipment in that tank;
  on the PSB/PS/SPS prototypes (when available).
Potential for measurements with PSB/PS/SPS beam?
  Can we instrument some wirescanners temporarily to measure also the high frequency content of what is coming out of the wires with PSB and SPS beam?
Work Plan (to be discussed!)

## Slide 17: Thank you!

## Slide 18: More details to be found here:
https://indico.cern.ch/event/625631/contributions/2526500/attachments/1434087/2204420/WS_Impedance.pdf
http://paf-spsu.web.cern.ch/paf-spsu/
https://indico.cern.ch/event/616762/