## Slide 1: Online data processing in ALICE
B. von Haller
23.03.2017
CERN

## Slide 2: Overview
Context
  Major upgrade of ALICE for Run 3 and 4 (i.e. post 2020)
  O2 project : a common online/offline computing system
Outline
  Rationales for O2 and online data processing
  Requirements, architecture and design
  Data quality control

## Slide 3: Today’s system
Triggered
  only a small amount of events is actually recorded
Limited online processing
  the High Level Trigger processes the data of the largest detector
  a few calibration are done online without human intervention
Full reconstruction and calibration is done offline, in the days, weeks and months after the data taking
Online
Offline
ALICE
Notes: TODO add drawing

## Slide 4: Rationales for a new computing system
After LS2, LHC min bias PbPb at 50 kHz
  ~100 x higher event rate than during Run 1
  Too much data to be stored
Physics topics addressed by ALICE upgrade
  Rare processes, very small signal over background ratio
  Needs large statistics of reconstructed events, 13nb-1 for PbPb
  Triggering techniques very inefficient or impossible in most cases
TPC inherent rate (drift time ~100 µs) < 50 kHz
  Support for continuous read-out, as well as triggered read-out

## Slide 5: Tomorrow’s system
Read-out the data of all collisions
Compress these data intelligently by reconstructing and calibrating them online
One common online-offline computing system: O2
Paradigm shift compared to today’s approach
But built on our experience with the HLT

## Slide 6: Functional flow
Asynchronous (few hours) event reconstruction with
final calibration
Compressed Sub-Timeframes
Continuous and triggered streams of raw data
Data aggregation Synchronous global
data processing
Data storage (60 PB)
1 year of compressed data
Write 170 GB/s, Read 270 GB/s
Compressed Timeframes
Reconstructed events
Compressed Timeframes
Base Line correction, zero suppr. Readout
Data aggregation Local data processing
Detectors electronics
3.4 TB/s HI:50kHz pp/pA:200kHz
500 GB/s HI:50kHz pp/pA:200kHz
90 GB/s HI:50kHz pp/pA:200kHz
Tier 0, Tiers 1 and Analysis facilities
20 GB/s
Trigger system
First Level Processors (FLP)
Event Processing Nodes (EPN)
Synchronous
Asynchronous
Notes: Consider removing Tiers

## Slide 7: Readout & FPGA Hardware acceleration
RORC 1 | C-RORC | CRU
2 ch @ 2 Gb/s PCIe gen.1 x4 (1 GB/s) | 12 ch @ up to 6 Gb/s PCIe gen.2 x 8 (4 GB/s) | 24 ch @ 5 Gb/s PCIe gen.3 X 16 (16 GB/s)
Custom DDL protocol | Custom DDL protocol (same protocol but faster) | GBT
Protocol handling TPC Cluster Finder | Protocol handling TPC Cluster Finder | Protocol handling TPC Cluster Finder Common-Mode correction Zero suppression
Run 3
LS 2
Run 2
LS1
Run 1

## Slide 8: Hardware acceleration (FPGA)
Performance of the FPGA-based FastClusterFinder algorithm for DDL1 (Run1) and
DDL2 (Run2) compared to the software implementation on a recent server PC.

## Slide 9: Computing requirements for online processing
Computing requirements -> Total : ~ 100000 CPU cores 5000 GPU chips
Goes together, merging and fitting can run on GPUs too
Being ported to GPU, conversion factor unknown
Theoretically could run on GPU
Notes: In case of GPUs, we will refer to the number of GPU cards.}
TPC 1000 -> 6000
Effective CPU (if GPU: 26 CPUs + 3 CPUs) : 235000

## Slide 10: Hardware acceleration (GPU)
For TPC track finding on EPNs (as today’s HLT)
Possibly more use cases depending on R&D
Tracking time of HLT TPC Cellular Automata tracker on Nehalem CPU (6Cores) and NVIDIA Fermi GPU.

## Slide 11: O2 Hardware facility
Detectors
9000 Read-out Links
270 FLPs
First Level Processors
(FLPs)
1500 EPNs Event Processing Nodes
(EPNs)
Input: 270 ports
Output : 1500 ports
3.4 TB/s
Switching
Network
500 GB/s
RD and WR
440 GB/s
68 Storage Arrays
60 PB
34 Storage Servers
Storage
Network
Input: 1500 ports
Output : 34 ports
90 GB/s

## Slide 12: O2 Farm
~100k CPUs, ~5k GPUs, ~500 FPGAs
FLPs at P2 in existing CR1
EPNs and storage need a new dedicated room
  Space and weight limitations
Two scenarios
  CR0
    Container(s)
    Call for tender (common with LHCb and neutrino platform)
  Common Data Center in Prevessin
    An alternative to the CR0 at P2 has been proposed by CERN
    New common data center in Prevessin
    Being studied
CR1
CR0
IT network
9000 optical
fibers
Notes: TODO rework the image

## Slide 13: Software for online processing
Message-based multi-processing
  Ease of development
  Ease to scale horizontally
  Possibility to extend with different hardware
  Multi-threading possible within processes
ALFA : ALICE-FAIR concurrency framework
  Data transport layer
  ZeroMQ
  Multi-process
  First version available, development ongoing
AliceO2
  Prototyping
  Steady started
Design
Libraries and tools
ALFA
Cbm
AliceO2
Panda
FairRoot
. . . . . . .
EPN m
EPN 1
n
2
1
…
…
Notes: TODO add schema for the multi-process vs mutli-threading

## Slide 14: Data Quality Control
Run 3 Data Quality Control (QC) combines
  Data Quality Monitoring (online)
    Make sure to record and reconstruct high quality data
  Quality Assurance (offline)
    Make sure to reconstruct and analyze high quality data
Crucial because we do a lossy compression
  Get feedback on the quality of the data and the processing
  Identify and solve issues early
    With or without human interventions
  Help streamline the processing by identifying ”good” data
Without QC we are blind
Dataflow
Monitoring Object Generation
Automatic
Quality Assessment
Storage
Visualization
Notes: Involves
  [Online gathering of data]
  Analysis by user-defined algorithm
    Production of monitoring objects such as histograms
    Assessment of the quality of the data based on the objects
  Storage of monitoring data
  Visualization (+ human assessment of quality)

## Slide 16: QC requirements
Based on 2 detailed surveys and on our experience
100 tasks (most are parallelized over 100s of machines)
Analysing 1-100% of the data
  Possibly in stage, not everything synchronously with data
10’000 objects (mostly histos) after merging, updated every minute
  We actually expect 25’000 objects and plan for peaks of 50’000
5% of objects to be kept forever, all the rest kept for days or weeks
Short feedback loop (seconds) with initial setup within minutes
Automatic as much as possible, machine learning ideally

## Slide 17: Summary
O2 is a project with ambitious requirements
  > 3.4TB/s detector input, ~100x more than today
  Online synchronous compression factor of >30
  Major paradigm change with combined offline and online system
Hardware
  HW acceleration (FPGAs, GPUs) for online processing
  O2 farm with ~100 k CPU cores and ~5000 GPUs
Software
  Multi-processes + multi-threaded
  Data Quality Control is both crucial and challenging

## Slide 19: O2 Schedule
2020-2021
Design
R&D
Demonstrators
O2 TDR
Products selection
Detailed design
R&D
Prototyping
Development
Products selection
Prototypes
Detailed design
R&D
Prototyping
Development
Products selection
Prototypes
Final components
Deployment
Commissioning
Development
Products selection
Final components
Deployment
Commissioning
Production
2018-2019
2016-2017
2014-2015
2012-2013
High-Level Design
R&D
Trigger TDR
Project organization
Run 3
LS 2
Run 2
LS1
Run 1

## Slide 20: Network performance tests
Comparison of Ethernet, IP over InfiniBand and IP over Omni-Path
40 GbE: 40 Gigabit Ethernet OPA: Intel® Omni-Path IB: InfiniBand O2: ALICE Online-Offline framework
Chart: Block Size (B)
| 1000.0 | 10000.0 | 100000.0 | 1.0E6 | 1.0E7 | 2.5E7 | 5.0E7 | 7.5E7 | 1.0E8
40 GbE (O2) | 1.91 | 11.86 | 30.26 | 37.17 | 36.52 | 34.3 | 28.07 | 26.2 | 28.19
40 GbE (max) | 40 | 40 | 40 | 40 | 40 | 40 | 40 | 40 | 40
OPA (O2) | 2.81 | 9.13 | 23.17 | 35.32 | 34.96 | 21.8 | 16.51 | 12.83 | 13.45
OPA (max) | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100
IB (O2) | 1.98 | 7.26 | 16.63 | 22.24 | 11.58 | 12.11 | 15.01 | 14.38 | 14.03
IB (max) | 56 | 56 | 56 | 56 | 56 | 56 | 56 | 56 | 56
1K 10K 100K 1MB 10M 100M
Notes: If needed, remove the one on the right.
If needed remove the FDT.

## Slide 21: Storage
Client File Systems performance tests
ADM: Administration server
MD: Metadata server
DS: Data server
CLI: Client
GE: Gigabit Ethernet
IB: InfiniBand
GPFS: General Parallel File System
Lustre: open-source parallel file system
Ceph: distributed object store
RADOS: Reliable Autonomic Distributed Object Store
Notes: capacity and throughput on a set budget
The R&D is set up in three layers:
  (basic) storage elements, technology
  SSD storage
    Magnetic rotating disks storage
    All-Flash, NVMe storage
  Storage systems (enclosures, servers, ..)
  Storage Chassis
    Storage Servers
    Storage Racks
    Flash Arrays
  Client access (file systems)

## Slide 22: Physics software design
Online processing workflow
EPN: synchronous asynchronous
All FLPs
Raw data
Local Processing E.g. Clusterization Calibration
Detector Reconstruction
E.g. TPC & ITS
Track finding
CTF
AOD
Step 1
Step 2
Step 3
Step 4
Inter-detector
matching procedures
Final calibration, 2nd matching
Final matching, PID, Event extraction
Step 0
Notes: also muon pre-clustering, calorimeters cell energy and time extraction
TPC and ITS track finding, ITS vertexing, MCH track clusterization, FIT -> multiplicity,
inter-detector matching procedures
  TRD: Matching of TPC tracks to TRD online tracklets
  ITS/TPC: standalone tracks matching (full or partial, depending on ITS noise)
  TPC calib : Drift velocity from limited sample TPC/ITS matching
TPC calib : Gain, space charge an drift velocity; TRD calib: Chamber status and gain. TPC, ITS : final tracking ; MFT MUON track finding and matching
matching to TOF, HMPID, calorimeters, PID calibrations and the event build/extraction

## Slide 23: Computing Model
T0/T1
CTF -> ESD -> AOD
AF
AOD -> HISTO
O2
RAW -> CTF -> ESD
-> AOD
1
T2
MC -> CTF -> ESD
-> AOD
1..n
1..n
1..3
CTF
AOD
AOD
AOD
Glossary
RAW: raw data
CTF: Compressed Time Frame
ESD: Event Summary Data
AOD: Analysis Data Object
O2: Online-Offline facility
T0, T1, T2: Grid Tier 0, 1, 2
AF: Analysis Facility
MC: Monte-Carlo
HISTO: Subset of AOD specific for a given analysis
Notes: The AF must have very good network connectivity and a large, efficient local disk buffer 5PB dedicated to the storage of an entire set of active ALICE AODs with the associated CPU capacity for efficient processing of AODs several times per day.