## Slide 1: (quasi) real-time connectivity requirements ”CERN openlab workshop 23/4/17”
Niko Neufeld
niko.neufeld@cern.ch
https://www.afinite.co.uk/media/85/Connectivity.jpg

## Slide 2: Acknowledgements & disclaimer
Most of this is not original, though some of it I arrived at independently 
Too vast a topic for 15 minutes, you will be subject to heavy presenter’s bias

## Slide 3: The 4 tasks with data
Getting from the sensors
Distributing
Processing
Storing
Specific to Online computing
Not covered in this talk
Both Online & Offline
Repeated cycles

## Slide 4: The ideal experiment: get all data which your instrument provides!
In theory this should allow you to extract anything of interest
In practice this can be a lot of data. Typical LHC experiment has 10^7 sensors with new values every 25 ns – assuming (pessimistically) 8 bit ADC for each sensor – this gives 400 Tbyte / second (!)
What is limiting us?

## Slide 5: The 4 limitations with data
Getting from the sensors
Distributing
Processing
Storing
Specific to Online computing
Not covered in this talk
Not covered in this talk

## Slide 6: The readout chain
Ideally all these functions are integrated in the front-end chip
There will be challenges with power (dissipation), in particular at high rate detectors, and, in some cases, radiation
Amplifier
Filter
Shaper
Range compression
clock
Sampling
Digital filter
Zero suppression
Buffer
Format & Readout
Buffer
Feature extraction
Detector / Sensor
to Data Acquisition System

## Slide 7: The last (first) mile
The last mile is (still) in copper
Optical modules too large / too power hungry / not radiation hard enough
But copper is not what we want in the way of our particles!
This is the ultimate limit to high-rate read-out

## Slide 8: Very high density readout 1): wireless
Wadapt: “Wireless Allowing Data And Power Transmission”
Original idea by R. Brenner (Uppsala)
Radial Datatransfer
  Communication between layers
Signal cannot traverse layers
  Reuse of frequency channels

## Slide 9: The next link for LHC: LpGBTX (draft characteristics)
500 mW (target)
  5.12 Gbit/s low power
10.24 Gbit/s (”high” speed)
Includes possibility for strong Forward Error Correction (FEC)
Bidirectional link including possibility to use for synchronous (trigger) commands, clock and slow-control: one link for everything
https://espace.cern.ch/GBT-Project/default.aspx

## Slide 10: Silicon photonics
Challenging, but very hot topic  industry interest (hint, hint )
  High bandwidth (10, 25 Gbit/s)…
Allows very tight integration, very compact, dense optical transmitters directly from front-end ASICs
Lots of challenges:
  Integration with other electronics and packaging
  Radiation hardness needs to be established (some first encouraging results have been achieved)
Source: S. Seif El Nasr-Storey et al. http://http://cds.cern.ch/record/2025925

## Slide 11: Transiting to COTS
Data
formatting
MUX
DAQ
Zero-
suppression
Data
formatting
Data buffering
during trigger
Derandomizer buffer
On-detector
Off-detector
Custom Electronics
Commercial of the Shelf
Switching network
Optional, if event-building required
Processing Elements
Transition module

## Slide 12: Transitioning to COTS using PCIe and an (intel) FPGA
Today transitioning to COTS means PCIe or Ethernet
Example: PCIe40, developed by CPP Marseille
Will be used by ALICE and LHCb for LHC run-3
48 bi-directional links
  up to 10 gbit/s
  Free choice of protocol (ex. Gbt, ethernet etc…
  Multimode fibre 850 nm
Can bring up to 110 Gbit/ into a PC over PCIe
High-port density, cost-effective solution – more integration possible? CPU/FPGA?

## Slide 13: Event-building
Detector
Switching network
100 m rock
Readout Units
Compute Units
Every Readout Unit has a piece of one data-set (“event”)
If all pieces must be brought together into a single compute unit for filtering then event-building is required
This can be most easily be done by a switching network

## Slide 14: LAN technologies
Ethernet (Ieee 802.3 xx)
  The LAN
  Normally used in conjunction with IP (and tcp)
Infiniband (IB)
  Open standard, single vendor
  Complete stack(no need for IP or TCP) rmance computing and as a back-end for storage
  Low cpu usage on clients by using remote direct memory access (rdma)
  Low latency
Omni-path
  Intel alternative to infiniband
  Lowest cost per unit bandwidth
Anything else is exotic
http://www.digibarn.com/collections/diagrams/ethernet-original/composit-ethernet-sketch.jpg

## Slide 15: DAQ challenges
Transport multiple Terabit/s reliably and cost-effectively
500 port full duplex, full bi-sectional bandwidth network, aiming at 80% sustained link-load @ >= 100 Gbit/s / link
Integrate the network closely and efficiently with compute resources (be they classical CPU, “many-core” or accelerator-assisted)
Multiple network technologies should seamlessly co-exist in the same integrated fabric (“the right link for the right task”)

## Slide 16: Future network needs for LHC DAQ
Chart: Network – Projected Throughput [Tbit/s]
| Alice | Atlas | CMS | LHCb | LHC combined today
Throughput | 10 | 22 | 40 | 40 | 2.5
2020
2020
2026
2026

## Slide 17: The evolution of Network Interconnects
Chart: Gbit/s
| 2008.0 | 2012.0 | 2013.0 | 2014.0 | 2015.0 | 2016.0 | 2017.0 | 2018.0
Ethernet | 10 | 40 | 40 | 40 | 100 | 100 | 100 | 100
Intel OmniPath | 100 | 100 | 200
InfiniBand | 32 | 54 | 54 | 100 | 100 | 100 | 200 | 200
PCIe x8 | 32 | 64 | 64 | 64 | 64 | 128 | 128 | 128
PCIe Gen4
PCIe Gen3
available
HDR (200 Gb/s) HCA
expected
100 GbE NIC
Only general purpose technologies shown
Driven by SERDES speed: 10, 25, 50 GHz

## Slide 18: How much does a Gigabit/s cost?
Chart: LAN cost evolution (list-price)
| 2011.0 | 2013.0 | 2015.0
1 Gigabit/s (adatper) | 18.1 | 12.5 | 9.8
1 Gigabit/s (switch) | 5.7 | 4.6 | 3.6
Source: http://www.kernelsoftware.com/products/catalog/mellanox.html

## Slide 19: Cost example DAQ (Fat Tree)
Based on Ethernet (40G)
Assume 100 data sources and 150 computers, 40G / server!
The radix is here 32
We need 35 switches, 474 cables
Cost (assuming typical discounts) ~ 333000 USD
Assumes perfect scaling!
DIY:
http://www.broadcom.com/application/cloud_scale_network/cloud_configurator.php
(design the network + network costs)
http://www.colfaxdirect.com (adapter cost)
Source: https://computing.llnl.gov/tutorials/lc_resources/

## Slide 20: Scaling in practice
A lot of challenges remain!
Notes: The good: more than 31 Tbit/s in flight!
The bad: between 4 and 512 nodes loose more than 50%

## Slide 21: Long-distance data-transport a.k.a. the Prevessin challenge
The servers can be hosted elsewhere. In that case the 32 Tbit/s raw data need to be transported off-site
Distance: about 4 km (for ALICE and LHCb)
Lay many new fibres or use of DWDM
Using 25 GHz wavelength about 1200 lambdas are needed in the maximum configuration
The solution should be compact, does not need 99.999% availability, it should be scalable (starting smaller to be ramped up to max later)
Traffic is essentially uni-directional  Could this be exploited?
In any case data transport cost / Tbit/s is significant, compression of data is attractive, if cost-efficient

## Slide 22: Conclusions
Significant challenges remain in all areas of data movement
  Not only online but also offline
Getting the data out and distributed is crucial for more and better physics in all future experiments
LAN growth is still strong, but Online requirements are very high and budgets are limited