## Slide 1: FE Optical Link Validation Setup
Rainer Schwemmer – LHCb Upgrade Electronics Meeting 13.4.17

## Slide 2: Future DAQ Architecture
Current Baseline for Optical Readout
O(10k) optical links with > 300m length @ 4.8 GHz
Outside the design goal for the Versatile Link (80m)
In previous tests we verified that this can work
Looking at component specs: this might be a bit on the edge though
Never checked with GBT <-> Transmitter electrical link
Validation needed
2
Detector front-end electronics
Eventbuilder network
TELL40s
Eventfilter Farm
~ 80 subfarms
subfarm switch
500 x
100 Gbit/s
100 Gbit/s
subfarm switch
Online storage
10000 x
Versatile Links

## Slide 3: BER considerations
Test setup at P8
36 links for 8 Months
BER < 1.3 x 10-18 @ 95% CL
Ramifications (example):
  Expected error rates DAQ @ BER 1.0 x 10-18
  10k links  4 Errors per day
  8 bit header (120 bit frames)  4 days between errors in header which can potentially upset DAQ (desynchronization)
  Rest is bit flips in detector channel data (detector noise)
Problem rate increases proportional with error rate
3
AMC40
Patch Panel
SX8
(Gas Building)
Patch Panel
UX8
Bunker
BER tester
~ 350 m

## Slide 4: Proposed setup for validation
In the process of acquiring all the pieces which are the current baseline for the final system
  350m x 144 Trunk cable  already delivered
  Fan-outs  ordered
  Patch panels  ordered
  Attenuators  Supplier found, order after Easter
  Tell40s  already delivered
Enough cables to fully populate 2 Tell40s
Hoping that we can have the hardware setup ready and debugged by mid May
4

## Slide 5: Validation procedure/goals
GBT on FE produces test pattern
  Preferably PRBS
Tell40 measures error rate of transmission
Use set of attenuators to dampen signal to obtain coarse BER curve
Use previous lab measurements to extrapolate error rate at 0 dB attenuation
Suggested target values (assuming similar behavior as previous tests):
  3.5dB safety margin for aging, installation issues, variance
  BER < 1.0 x 10-18
  < 10-8 @ 6 dB O(seconds)
  < 10-12 @ 5 dB O(10 min)
Goals
  Validate optical components (again)
  Validate electrical path on FEs
  Check all FE designs by end of Year
5
Chart: 400m OM3, OM4 - Attenuation
| 16 | 15.5 | 15 | 14.5 | 14 | 13.5 | 13 | 12.5 | 12 | 11.5 | 11
OM3 YOFC CH_0 | 0.022007 | 0.012967 | 0.0059153 | 0.0019295 | 0.00046752 | 7.252e-05 | 7.1836e-06 | 2.0929e-07 | 2.3426e-09 | 3.7975e-11
OM3 YOFC CH_1 | 0.020672 | 0.010587 | 0.0040906 | 0.0013067 | 0.00040793 | 5.8964e-05 | 4.5797e-06 | 1.3439e-07 | 3.3406e-09 | 1.2975e-11
OM3 YOFC CH_4 | 0.017874 | 0.0094964 | 0.0044448 | 0.0014313 | 0.00029219 | 3.9481e-05 | 3.0298e-06 | 1.9475e-07 | 3.1634e-09 | 2.9161e-11
OM4 YOFC CH_0 | 0.024553 | 0.015237 | 0.0074552 | 0.0026052 | 0.00084205 | 0.00012626 | 1.0249e-05 | 5.6667e-07 | 2.1517e-08 | 3.6001e-10
OM4 YOFC CH_1 | 0.020936 | 0.011781 | 0.0059065 | 0.0019793 | 0.0004441 | 7.6343e-05 | 6.382e-06 | 4.6795e-07 | 1.2999e-08 | 8.8557e-11
OM4 YOFC CH_4 | 0.024706 | 0.016336 | 0.0078119 | 0.0031517 | 0.00072148 | 0.00011962 | 1.6487e-05 | 1.1259e-06 | 3.5792e-08 | 1.1369e-09 | 1.0347e-11
OM4 Furukawa CH_0 | 0.020317 | 0.011552 | 0.0048723 | 0.0015051 | 0.00038676 | 6.3598e-05 | 5.8067e-06 | 1.9957e-07 | 5.7585e-09 | 6.6615e-11
OM4 Corning CC CH_0 | 0.015434 | 0.0083352 | 0.0024794 | 0.00083694 | 0.00010879 | 1.8793e-05 | 8.3814e-07 | 2.795e-08 | 1.0285e-09 | 1.7412e-11

## Slide 6: Discussion/Questions