## Slide 1: Remote FPGA configuration
João Vítor Viana Barbosa
Electronics upgrade meeting, 13th april 2017

## Slide 2: How it is done – control system integration
GbtServ
WinCC-OA Control PC
ConfigServ
Bitstream file
Progress report
SOL40
(SOL40_SCA)
Front End

## Slide 3: How to use (command line)
$ configure_kintex7 --gbt 3 --sca 0 --chain-len 6 --dev-index 2 --file pdmdb_top.6LinksOK.bit
$ configure_microsemi --gbt 3 --sca 2 --chain-len 6 --dev-index 2 --file cluster_fpga.dat –action PROGRAM
Additional parameters:
--control <control_reg> (see GBT-SCA manual, default 0x4200 for Kintex and 0x0 for Microsemi)
--frequency <val> (0 to 20000000, default 20Mhz)
--loglevel <val> (0 to 7, 7 is default)
--irlen <val> (default is 6 for kintex7 and 8 for microsemi)

## Slide 4: Initially too much time!!
  Configuring a Kintex7 was taking 180 seconds at 20MHz JTAG frequency
  Configuring an IGLOO2 was taking 17 minutes

## Slide 5: JTAG Composite commands (acceleration)
Basic commands | Composite commands
JTAG_W_TMS0(1, 2, 3) JTAG_W_CTRL JTAG_W_TDO0(1, 2, 3) JTAG_GO | JTAG_W_TMS JTAG_TDO_SCAN_OUT (5x reduction SCA software access)
JTAG_W_TMS0(1, 2, 3) JTAG_W_CTRL JTAG_GO JTAG_R_TDO0(1, 2, 3) | JTAG_W_TMS JTAG_TDO_SCAN_IN (5x reduction SCA software access)
JTAG_W_CTRL JTAG_GO JTAG_R_TDO0(1, 2, 3) | JTAG_TDO_SCAN_OUT (6x reduction SCA software access)
Biggest factor for big configuration times is probing for replies in the SOL40_SCA from the software.
Mitigated by implementing composite commands in firmware.

## Slide 6: How long does it take ?
Roughly 5x improvement for 3MB files on the Kintex 7 (180 s to 35 s)
About 2.5x improvement for 5.6MB files on IGLOO2 (17 to 7 mins, to be improved)
Chart: Configuration with BASIC commands (Kintex 7)
| 1 MHz | 10 MHz | 20 MHz
440 KB | 34.3075 | 28.026 | 28.2727
740 KB | 58.7374 | 47.4045 | 47.9224
2140 KB | 167.5272 | 137.216 | 135.3984
Chart: Configuration with COMPOSITE commands (Kintex 7)
| 20 | 10 | 5 | 1 | 0.5 | 0.1
3 MB | 35 | 36 | 59 | 71 | 115 | 284

## Slide 7: Features now in place
FPGAs supported | Xilinx series 7 family | IGLOO2, SmartFusion2
Protocol used | JTAG | JTAG (check), SPI (debug phase)
Timing | ~35 secs for 3MB file (15s compressed file) | 7 min for 5.6MB file
Daisy chain | YES | YES
Actions | PROGRAM, READ_ID | PROGRAM, ERASE, VERIFY, READ_ID, READ_INFO
Partial Reconfiguration | NO | -
Progress report | YES | YES
ECS integration | Soon | 

## Slide 8: Tests performed
Subdetector | Successfully tested features | To be done
SciFi | JTAG FPGA config (microsemi), all actions | SPI FPGA config (microsemi)
CALO |  | JTAG FPGA config (microsemi)
Muon |  | SPI FPGA config (microsemi)
RICH | FPGA config daisy chain (compressed and uncompressed bitstream) | 

## Slide 9: When can we use it?
  Everything should be available with the next release of fwGbt libraries and the next merge to of TFCv4 branch to master
  GbtServer and tools should be released soon
  Will already be able to use the command line tools if you compile the minidaq firmware from TFCv4

## Slide 10: Other news for the new release
  As requested, will be possible to send simple commands to the terminal in the CCPC through WinCC-OA (ls –a, pwd, etc..)
  Bug fix in SOL40_SCA that got the WinCC-OA managers and the GbtServer stuck when the control system tried to access SCAs that were not connected (pushed to TFCv4)
  Possible to configure the MiniDAQ firmware from the Control System (WinCC Project and ByteBlaster must be in the same machine)
  Closing and opening BAR0 and BAR2 access from WinCC-OA possible
  Loading ecs_driver from WinCC-OA possible