## Slide 1: Beam distribution at the TDE for different scenarios including re-triggering
C. Wiesner, W. Bartmann, C. Bracco, M. Fraser
WP14 Meeting
March 28, 2017

## Slide 2: Outline
C. Wiesner: MKB Failures and TDE Patterns
1) Introduction: LBDS Failure Scenarios
2) Loss of MKBH/MKBV
3) MKB Erratics and Retriggering Strategy
4) Outlook: Upgrade Possibilities
5) Summary
M. Frankl: Energy-Deposition Studies
T. Polzin: Thermo-Mechanical Effects

## Slide 3: LBDS – Failure Scenarios
T. Kramer et al, PAC’09, TU6RFP031
Erratic firing of MKD  Asynch. dump
New failure case (2016): Parasitic coupling of MKBs  Possibility of multi-erratics…
Erratic firing of MKB  Synchronous dump
Loss of 1 or 2 MKB due to flash-over during execution of dump.
Simulated beam pattern at TDE: nominal and with 2 MKBH failing.
4 MKBH and 6 MKBV
MKD
MKBV
MKBH
Time delay between MKBs  Risk of phase opposition

## Slide 4: Dilution Kicker (MKB)
Same maximum kick angle in both planes (~ 0.28 mrad)
4 MKBH operated at 27 kV
6 MKBV operated at 16 kV
 MKBH operated at higher voltage than MKBV  Failure of MKBH is more likely
In addition: for the given TDE pattern, loss of horizontal deflection is more critical

## Slide 5: Missing MKBH
vmin = 7.7 μm/ns
Sweep Velocity at TDE
Proton Density at TDE
Nominal TDE Pattern
3.9e6 macro particles
rpeak(p+) = 100%
Strong dependence on horizontal sweep velocity.
All 4 MKBH
Nominal waveform data taken from <2016-07-22, 17:01h> dump, Beam 2, e = 3.75 μm.
Sweep velocity is averaged over 7 adjacent bunches to reduce effects from waveform noise.
Filling scheme HL-LHC: filling_scheme_bcms_25ns_2604b_2592_2288_2396_288bpi12inj

## Slide 6: Missing MKBH
vmin = 6.0 μm/ns
Nominal waveform data taken from <2016-07-22, 17:01h> dump, Beam 2, e = 3.75 μm.
Sweep velocity is averaged over 7 adjacent bunches to reduce effects from waveform noise.
Filling scheme HL-LHC: filling_scheme_bcms_25ns_2604b_2592_2288_2396_288bpi12inj
Sweep Velocity at TDE
Proton Density at TDE
1 MKBH Missing
3.9e6 macro particles
rpeak(p+) = 130%
1/4 MKBH missing
Strong dependence on horizontal sweep velocity.

## Slide 7: Missing MKBH
vmin = 4.4 μm/ns
Sweep Velocity at TDE
Proton Density at TDE
2 MKBH Missing
3.9e6 macro particles
rpeak(p+) = 157%
Strong dependence on horizontal sweep velocity.
Nominal waveform data taken from <2016-07-22, 17:01h> dump, Beam 2, e = 3.75 μm.
Sweep velocity is averaged over 7 adjacent bunches to reduce effects from waveform noise.
Filling scheme HL-LHC: filling_scheme_bcms_25ns_2604b_2592_2288_2396_288bpi12inj
2/4 MKBH missing

## Slide 8: Missing MKBV
vmin = 7.7 μm/ns
Sweep Velocity at TDE
Proton Density at TDE
Nominal TDE Pattern
3.9e6 macro particles
rpeak(p+) = 100%
All 6 MKBV
Nominal waveform data taken from <2016-07-22, 17:01h> dump, Beam 2, e = 3.75 μm.
Sweep velocity is averaged over 7 adjacent bunches to reduce effects from waveform noise.
Filling scheme HL-LHC: filling_scheme_bcms_25ns_2604b_2592_2288_2396_288bpi12inj

## Slide 9: Missing MKBV
vmin = 7.7 μm/ns
Sweep Velocity at TDE
Proton Density at TDE
1 MKBV missing
3.9e6 macro particles
rpeak(p+) = 104%
Nominal waveform data taken from <2016-07-22, 17:01h> dump, Beam 2, e = 3.75 μm.
Sweep velocity is averaged over 7 adjacent bunches to reduce effects from waveform noise.
Filling scheme HL-LHC: filling_scheme_bcms_25ns_2604b_2592_2288_2396_288bpi12inj
1/6 MKBV missing

## Slide 10: Missing MKBV
vmin = 7.3 μm/ns
Sweep Velocity at TDE
Proton Density at TDE
2 MKBV missing
3.9e6 macro particles
rpeak(p+) = 106%
Nominal waveform data taken from <2016-07-22, 17:01h> dump, Beam 2, e = 3.75 μm.
Sweep velocity is averaged over 7 adjacent bunches to reduce effects from waveform noise.
Filling scheme HL-LHC: filling_scheme_bcms_25ns_2604b_2592_2288_2396_288bpi12inj
2/6 MKBV missing

## Slide 11: Missing MKBV
vmin = 6.0 μm/ns
Sweep Velocity at TDE
Proton Density at TDE
3 MKBV missing
3.9e6 macro particles
rpeak(p+) = 120%
Nominal waveform data taken from <2016-07-22, 17:01h> dump, Beam 2, e = 3.75 μm.
Sweep velocity is averaged over 7 adjacent bunches to reduce effects from waveform noise.
Filling scheme HL-LHC: filling_scheme_bcms_25ns_2604b_2592_2288_2396_288bpi12inj
3/6 MKBV missing
Compared to rpeak(p+) = 160% for 2/4 MKBH missing.

## Slide 12: Missing MKBV
vmin = 4.0 μm/ns
Sweep Velocity at TDE
Proton Density at TDE
4 MKBV missing
3.9e6 macro particles
rpeak(p+) = 159%
Nominal waveform data taken from <2016-07-22, 17:01h> dump, Beam 2, e = 3.75 μm.
Sweep velocity is averaged over 7 adjacent bunches to reduce effects from waveform noise.
Filling scheme HL-LHC: filling_scheme_bcms_25ns_2604b_2592_2288_2396_288bpi12inj
4/6 MKBV missing

## Slide 13
Missing MKB
 |  | Number of active MKBV |  |  |  |  |  | 
 |  | 6 | 5 | 4 | 3 | 2 | 1 | 0
Number of active MKBH | 4 |  |  |  |  |  |  | 
 | 3 |  |  |  |  |  |  | 
 | 2 |  |  |  |  |  |  | 
 | 1 |  |  |  |  |  |  | 
 | 0 |  |  |  |  |  |  | 
HL-LHC BCMS Filling Pattern
Nominal
Single
Failure
Single Failure

## Slide 14
Missing MKB
 |  | Number of active MKBV |  |  |  |  |  | 
 |  | 6 | 5 | 4 | 3 | 2 | 1 | 0
Number of active MKBH | 4 | 100% | 100% | 105% | 120% | 165% | 263% | 636%
 | 3 | 115% | 123% | 121% | 126% | 166% | 270% | 740%
 | 2 | 164% | 164% | 164% | 167% | 172% | 284% | 917%
 | 1 | 251% | 246% | 252% | 255% | 262% | 299% | 1328%
 | 0 | 604% | 660% | 736% | 790% | 959% | 1387% | 4559%
HL-LHC Standard Filling Pattern
Nominal
Next steps: Energy-deposition and thermo-mechanical studies (BCMS/standard) for HL-LHC parameters
Peak r(p+)

## Slide 15: Erratic 2016-10-01: Waveforms
Measured waveforms
Beam 1
MKBH.B in antiphase
For a single erratic, the worst case is loss of (less than) 2 MKB

## Slide 16: Problem: MKB Coupling
For t∞
αmax  75%
(loss of 1 MKBH)
For t∞
αmax  50%
(loss of 2 MKBH)
For t∞
αmax  25%
(loss of 3 MKBH)
For t∞
αmax  0%
(loss of 4 MKBH)
For delay < 150us:
double erratic is worst case
For shift 200us..600us: triple erratic is worst case
Spontaneous trigger  time delay between MKBHs  Risk of Antiphase
Minimum BETS delay (?)
Delay for MKBH erratic 2016-10-01
Hardware mitigation (common mode filtering and insulation of retrigger boxes) successfully implemented. However, immunity margin with respect to HL-LHC parameters to be further validated.

## Slide 17: Options MKB Retrigger Strategy
 | Max. horizontal deflection, single erratic | Max. horizontal deflection, double erratic | Required Changes
Current situation: BETS reacts with delay time < 1ms | 63%...87% (for BETS delay > 220 us) | 27%...77% (for BETS delay > 220 us) | None
Directly request synch. dump (do no retrigger MKBs) | 53%...95% | 5%...90% | Reduce delay time? …
Directly request synch. dump and retrigger all MKBs (within <1us) | 80% (Change of phase relation between MKD&MKB  significant change of TDE pattern). | 80% (Change of phase relation between MKD&MKB  significant change of TDE pattern). | Install dedicated MKB retrigger line Fast detection of erratic required
Directly request asynch. dump | Close to nominal for TDE. But losses in IP6. | Close to nominal for TDE. But losses in IP6. | Trigger signal MKB to MKD (?)
Increase delay time, e.g. >1.5ms | ~75% | ~50% (Remark: will get worse for erratic of 3, 4) | Introduce additional time delay (~1ms ?)…
Increase damping factor |  75% ? (small change of TDE pattern) |  50% ? (small change of TDE pattern) | Hardware changes, resistor? ...
Remove “fast path” (to reduce risk of multiple triggering) | No change for synch. dump; TDE pattern (slightly?) changed for asynch. dump. | No change for synch. dump; TDE pattern (slightly?) changed for asynch. dump. | Remove “fast path”
Idea: Eliminate the risk of antiphase by direct retriggering of all MKB

## Slide 18: Possible Solution: MKB Retriggering?
vmin = 7.9 μm/ns
Nominal waveform data taken from <2016-07-22, 17:01h> dump, Beam 2.
Sweep velocity is averaged over 7 adjacent bunches to reduce effects from waveform noise.
Filling scheme HL-LHC: standard_25ns_2748b_2736_2452_2524_288bpi12inj
Sweep Velocity at TDE
Proton Density at TDE
Nominal TDE Pattern
Time delay between MKBs and MKDs changes the TDE pattern.
3.9e6 macro particles

## Slide 19: MKB Retriggering
Nominal waveform data taken from <2016-07-22, 17:01h> dump, Beam 2.
Sweep velocity is averaged over 7 adjacent bunches to reduce effects from waveform noise.
Filling scheme HL-LHC: standard_25ns_2748b_2736_2452_2524_288bpi12inj
Sweep Velocity at TDE
Proton Density at TDE

## Slide 20: MKB Retriggering
Nominal waveform data taken from <2016-07-22, 17:01h> dump, Beam 2.
Sweep velocity is averaged over 7 adjacent bunches to reduce effects from waveform noise.
Filling scheme HL-LHC: standard_25ns_2748b_2736_2452_2524_288bpi12inj
Sweep Velocity at TDE
Proton Density at TDE

## Slide 21: MKB Retriggering
Nominal waveform data taken from <2016-07-22, 17:01h> dump, Beam 2.
Sweep velocity is averaged over 7 adjacent bunches to reduce effects from waveform noise.
Filling scheme HL-LHC: standard_25ns_2748b_2736_2452_2524_288bpi12inj
Sweep Velocity at TDE
Proton Density at TDE

## Slide 22: MKB Retriggering
Nominal waveform data taken from <2016-07-22, 17:01h> dump, Beam 2.
Sweep velocity is averaged over 7 adjacent bunches to reduce effects from waveform noise.
Filling scheme HL-LHC: standard_25ns_2748b_2736_2452_2524_288bpi12inj
Sweep Velocity at TDE
Proton Density at TDE
Highest p+ density, but very localized.

## Slide 23: MKB Retriggering
Nominal waveform data taken from <2016-07-22, 17:01h> dump, Beam 2.
Sweep velocity is averaged over 7 adjacent bunches to reduce effects from waveform noise.
Filling scheme HL-LHC: standard_25ns_2748b_2736_2452_2524_288bpi12inj
Sweep Velocity at TDE
Proton Density at TDE

## Slide 24: MKB Retriggering
Nominal waveform data taken from <2016-07-22, 17:01h> dump, Beam 2.
Sweep velocity is averaged over 7 adjacent bunches to reduce effects from waveform noise.
Filling scheme HL-LHC: standard_25ns_2748b_2736_2452_2524_288bpi12inj
Sweep Velocity at TDE
Proton Density at TDE

## Slide 25: MKB Retriggering
Nominal waveform data taken from <2016-07-22, 17:01h> dump, Beam 2.
Sweep velocity is averaged over 7 adjacent bunches to reduce effects from waveform noise.
Filling scheme HL-LHC: standard_25ns_2748b_2736_2452_2524_288bpi12inj
Sweep Velocity at TDE
Proton Density at TDE

## Slide 26: MKB Retriggering
Nominal waveform data taken from <2016-07-22, 17:01h> dump, Beam 2.
Sweep velocity is averaged over 7 adjacent bunches to reduce effects from waveform noise.
Filling scheme HL-LHC: standard_25ns_2748b_2736_2452_2524_288bpi12inj
Sweep Velocity at TDE
Proton Density at TDE

## Slide 27: MKB Retriggering
Nominal waveform data taken from <2016-07-22, 17:01h> dump, Beam 2.
Sweep velocity is averaged over 7 adjacent bunches to reduce effects from waveform noise.
Filling scheme HL-LHC: standard_25ns_2748b_2736_2452_2524_288bpi12inj
Sweep Velocity at TDE
Proton Density at TDE

## Slide 28: MKB Retriggering
Nominal waveform data taken from <2016-07-22, 17:01h> dump, Beam 2.
Sweep velocity is averaged over 7 adjacent bunches to reduce effects from waveform noise.
Filling scheme HL-LHC: standard_25ns_2748b_2736_2452_2524_288bpi12inj
Sweep Velocity at TDE
Proton Density at TDE

## Slide 29: MKB Retriggering
Nominal waveform data taken from <2016-07-22, 17:01h> dump, Beam 2.
Sweep velocity is averaged over 7 adjacent bunches to reduce effects from waveform noise.
Filling scheme HL-LHC: standard_25ns_2748b_2736_2452_2524_288bpi12inj
Sweep Velocity at TDE
Proton Density at TDE

## Slide 30: MKB Retriggering
Nominal waveform data taken from <2016-07-22, 17:01h> dump, Beam 2.
Sweep velocity is averaged over 7 adjacent bunches to reduce effects from waveform noise.
Filling scheme HL-LHC: standard_25ns_2748b_2736_2452_2524_288bpi12inj
Sweep Velocity at TDE
Proton Density at TDE

## Slide 31: MKB Retriggering
Nominal waveform data taken from <2016-07-22, 17:01h> dump, Beam 2.
Sweep velocity is averaged over 7 adjacent bunches to reduce effects from waveform noise.
Filling scheme HL-LHC: standard_25ns_2748b_2736_2452_2524_288bpi12inj
Sweep Velocity at TDE
Proton Density at TDE

## Slide 32: MKB Retriggering
Nominal waveform data taken from <2016-07-22, 17:01h> dump, Beam 2.
Sweep velocity is averaged over 7 adjacent bunches to reduce effects from waveform noise.
Filling scheme HL-LHC: standard_25ns_2748b_2736_2452_2524_288bpi12inj
Sweep Velocity at TDE
Proton Density at TDE

## Slide 33: MKB Retriggering
Nominal waveform data taken from <2016-07-22, 17:01h> dump, Beam 2.
Sweep velocity is averaged over 7 adjacent bunches to reduce effects from waveform noise.
Filling scheme HL-LHC: standard_25ns_2748b_2736_2452_2524_288bpi12inj
Sweep Velocity at TDE
Proton Density at TDE

## Slide 34: MKB Retriggering
Nominal waveform data taken from <2016-07-22, 17:01h> dump, Beam 2.
Sweep velocity is averaged over 7 adjacent bunches to reduce effects from waveform noise.
Filling scheme HL-LHC: standard_25ns_2748b_2736_2452_2524_288bpi12inj
Sweep Velocity at TDE
Proton Density at TDE

## Slide 35: MKB Retriggering
Nominal waveform data taken from <2016-07-22, 17:01h> dump, Beam 2.
Sweep velocity is averaged over 7 adjacent bunches to reduce effects from waveform noise.
Filling scheme HL-LHC: standard_25ns_2748b_2736_2452_2524_288bpi12inj
Sweep Velocity at TDE
Proton Density at TDE

## Slide 36: MKB Retriggering
Nominal waveform data taken from <2016-07-22, 17:01h> dump, Beam 2.
Sweep velocity is averaged over 7 adjacent bunches to reduce effects from waveform noise.
Filling scheme HL-LHC: standard_25ns_2748b_2736_2452_2524_288bpi12inj
Sweep Velocity at TDE
Proton Density at TDE

## Slide 37: MKB Retriggering
Nominal waveform data taken from <2016-07-22, 17:01h> dump, Beam 2.
Sweep velocity is averaged over 7 adjacent bunches to reduce effects from waveform noise.
Filling scheme HL-LHC: standard_25ns_2748b_2736_2452_2524_288bpi12inj
Sweep Velocity at TDE
Proton Density at TDE

## Slide 38: MKB Retriggering
Nominal waveform data taken from <2016-07-22, 17:01h> dump, Beam 2.
Sweep velocity is averaged over 7 adjacent bunches to reduce effects from waveform noise.
Filling scheme HL-LHC: standard_25ns_2748b_2736_2452_2524_288bpi12inj
Sweep Velocity at TDE
Proton Density at TDE

## Slide 39: MKB Retriggering
Nominal waveform data taken from <2016-07-22, 17:01h> dump, Beam 2.
Sweep velocity is averaged over 7 adjacent bunches to reduce effects from waveform noise.
Filling scheme HL-LHC: standard_25ns_2748b_2736_2452_2524_288bpi12inj
Sweep Velocity at TDE
Proton Density at TDE

## Slide 40: Retriggering: Density Comparison
Overlap
bin size: 200 um x 200 um
Localized hotspot due to low vsweep.
1 LHC turn
reduced vsweep
1 MKBH period
Sweep velocity is averaged over 11 adjacent bunches to reduce effects from waveform noise.

## Slide 41: Retriggering: Summary
Findings:
Retriggering of all MKBs eliminates risk of antiphase.
It can lead to increased p+ density at TDE:
  overlap at (30 us… 45 us) and (~6us, ~110 us), but at relatively high vsweep. Therefore, not prohibitive.
  localized hotspots due to reduced vsweep
  damping effect for tshift > 100us
Certain time delays lead to reduced p+ density.
Strategy:
Concentrate on immediate retriggering: tshift < 110 us to avoid damping effect
Tailor MKD/MKB waveforms? (Overshoot? Larger damping factor?)
Continue studies of energy deposition and thermo-mechanical stresses.
Evaluate implication for hardware, controls and machine protection (!)

## Slide 42: Possible Upgrades
Approach 1: Reduce MKB(H) voltage to reduce failure probability
Approach 2: Reduce sensitivity to failures

## Slide 43: Reduce MKBH Operational Voltage
Idea: Reduce MKBH operational voltage (and thus kick strength) to e.g. 90%.
Advantage: Straightforward to implement
Disadvantage: Reduced TDE pattern  Increased TDE density
See talk by M. Frankl for FLUKA results.
Simulated TDE patterns with MKBH voltage at 90%
4/4 MKBH
3/4 MKBH
2/4 MKBH

## Slide 44: Adding 2 MKBH
MKBH.A/B
MKBV.E/F
MKBH.C/D
MKBV.A/B
MKBV.C/D
4.762 m
4.256 m
Thanks to L. Ducimetiere
Approach: Keeping total deflection angle  reduced voltage for each MKBH generator to ≈ 67%·V0 ≈ 18 kV  (significantly) reduced risk of erratic firing
More modules  reduced failure sensitivity
To be studied: apertures, integration of magnets and generators, costs…
In addition, nominal MKBH voltage could be reduced.
58 mm
MKBH
32 mm
66 mm
MKBV
36 mm
Apertures
Downstream shift of 4.8 m increases Δx by ± 1.3 mm

## Slide 45: Adding 2 MKBH
LHC 4R6
MKBV -- BPMD.683451.B1 -- BTVD.683458.B1 -- TCDQ

## Slide 46: Increasing Generator Capacitance
To be studied: change in TDE pattern (due to change in waveform, larger damping)
MKBH
Thanks to V. Senaj
Increase C0 by 30%  Decrease voltage by 14%
Results in larger damping
Adjust (decrease) L0

## Slide 47: Add Optics Elements in Dump Line
  Add quadrupole in dump line to increase kick strength?
    To be studied: integration, apertures, costs, sensitivity for orbit excursions.
  Increase Q4 gradient?
    To be studied: Implications for optics, failure cases.
D. Barna/T. Kramer, FCC-hh Dump Pattern Studies
Example: possible FCC dump line

## Slide 48: Approach 2: Reduce sensitivity to failures
  Retrigger all MKBs in case of erratic firing?
    To be studied: change of TDE pattern, implications for hardware, controls and machine protection
  Change MKD/MKB waveforms (overshoot, damping) to avoid overlap for retrigger case?
    To be studied: change of TDE pattern
    Combine with increased generator capacitance
  Change nominal timing between MKBs and/or between MKBs and MKDs to be less sensitive to horizontal failure?
    To be studied: change of TDE pattern, implications for hardware, controls and machine protection
  …

## Slide 49: Summary
Loss of MKB
  Failure of MKBH is more likely and more critical
  p+ density increase <170% for 2/4 MKBH and 4/6 MKBV missing
MKB coupling issue might be solved by fast retriggering of all MKBs
  However, this leads to a significant change in the TDE pattern (in case of erratic firing) and significant implications for controls and machine protection
  TDE patterns studied and main effects identified (overlap, local density hotspots) so that possible mitigation measures can be evaluated
Upgrade strategy to reduce MKB failure probability and failure sensitivity to be defined

## Slide 50
Thank you for your attention!

## Slide 51: Modified Timing
vmin = 9.8 μm/ns
Sweep Velocity at TDE
Proton Density at TDE
All 4 MKBH
3.9e6 macro particles
rpeak(p+) = 83%
All 4 MKBH
Less dependence on horizontal sweep velocity.
Nominal waveform data taken from <2016-07-22, 17:01h> dump, Beam 2, e = 3.75 μm.
Sweep velocity is averaged over 7 adjacent bunches to reduce effects from waveform noise.
Filling scheme HL-LHC: filling_scheme_bcms_25ns_2604b_2592_2288_2396_288bpi12inj
MKD delayed by 22 μs w.r.t MKB.

## Slide 52: Modified Timing
vmin = 8.3 μm/ns
Sweep Velocity at TDE
Proton Density at TDE
1 MKBH missing
3.9e6 macro particles
rpeak(p+) = 104%
1 MKBH missing
Less dependence on horizontal sweep velocity.
Nominal waveform data taken from <2016-07-22, 17:01h> dump, Beam 2, e = 3.75 μm.
Sweep velocity is averaged over 7 adjacent bunches to reduce effects from waveform noise.
Filling scheme HL-LHC: filling_scheme_bcms_25ns_2604b_2592_2288_2396_288bpi12inj
MKD delayed by 22 μs w.r.t MKB.

## Slide 53: Modified Timing
vmin = 5.4 μm/ns
Sweep Velocity at TDE
Proton Density at TDE
2 MKBH missing
3.9e6 macro particles
rpeak(p+) = 141%
2 MKBH missing
Less dependence on horizontal sweep velocity.
Nominal waveform data taken from <2016-07-22, 17:01h> dump, Beam 2, e = 3.75 μm.
Sweep velocity is averaged over 7 adjacent bunches to reduce effects from waveform noise.
Filling scheme HL-LHC: filling_scheme_bcms_25ns_2604b_2592_2288_2396_288bpi12inj
MKD delayed by 22 μs w.r.t MKB.

## Slide 54: Modified Timing: Comparison

## Slide 55
Missing MKB
 |  | Number of active MKBV |  |  |  |  |  | 
 |  | 6 | 5 | 4 | 3 | 2 | 1 | 0
Number of active MKBH | 4 | 100% | 104% | 106% | 120% | 159% | 269% | 621%
 | 3 | 130% | 129% | 131% | 130% | 164% | 273% | 746%
 | 2 | 157% | 160% | 162% | 162% | 170% | 272% | 906%
 | 1 | 247% | 251% | 246% | 253% | 265% | 294% | 1279%
 | 0 | 594% | 684% | 757% | 805% | 987% | 1383% | 4315%
HL-LHC BCMS Filling Pattern
Nominal
Next steps: Energy-deposition and thermo-mechanical studies (BCMS/standard) for HL-LHC parameters
Peak r(p+)

## Slide 56: Retriggering: Density Comparison
bin size: 200 um x 200 um
Energy density on upstream windows seems to follow the p+ density.
For discussion of absolute values and thermo-mechanical stresses see talks by M. Frankl and T. Polzin.
FLUKA values courtesy of M. Frankl.
reduced vsweep
Sweep velocity is averaged over 11 adjacent bunches to reduce effects from waveform noise.

## Slide 57: Retriggering: Density Comparison
bin size: 200 um x 200 um
Energy density in dump core and downstream window might be less sensitive to localized hotspots in the p+ density.
For discussion of absolute values and thermo-mechanical stresses see talks by M. Frankl and T. Polzin.
reduced vsweep
FLUKA values courtesy of M. Frankl.
Sweep velocity is averaged over 11 adjacent bunches to reduce effects from waveform noise.