## Slide 1
Update on Linac4 Status, Reliability Run and Modelling
J. Uythoven, O. Rey Orozco, A. Apollonio and R. Schmidt
CERN
Acknowledgements: colleagues from Empresarios Agrupados
and the LINAC4 team @ CERN
MYRTE 4th WP2 Meeting, 27-28/03/2017, Madrid

## Slide 2: Outline
Introduction and Linac4 Status
Plans for Linac4 Reliability Run
Linac4 Fault Tracking
Linac4 Failure Catalogue
Availability Modelling
  Common Input Format
  Linac4 Model
Milestones

## Slide 3: LINAC4 made it to the final energy !

## Slide 4: A word on the Source
Many improvement since march 2015
Intensity
Stability
Auto-Pilot (automatic regulation of critical source parameters for increased stability)
Ceasiation with autopilot , time needed went from half day w/o beam to few hours in degraded beam conditions
Still needs attention
Control of the emittance
Optimised electrode shape
Matching into the LEBT
Mastering neutralisation?
Current at 3 MeV before chopping
Studies show that the reduced current can be compensated by more injection from the LINAC into the PSB.

## Slide 5: LINAC4 Status
Operational without major problems for over 10 weeks since November 2016
  About 10 days of total down time due to 3 water leaks (DTL)
  Re-alignment not fully successful, impacting the chopping efficiency
Half Sector Test first phase successful = test stand of injection system with stripping foil into the next accelerator (PSB)
  Beam delivered over the last four weeks
The Linac4 can be run from the CERN Control Centre CCC in preparation of the Reliability Run

## Slide 6: The LINAC4 Half Sector Test
HST
Stripping Foil
Test Stand
Stripping foil
system
Chicane
magnets +
H0/H- dump
Temporary
dump
Linac4
+ diagnostics, vacuum eq. …
Installed in Linac4
during summer 2016

## Slide 7: LINAC4 Reliability Run
RR Foreseen to start summer 2017, most likely continue in 2018
  Smooth transition from commissioning to operation: train operators, software development, finish tweaking the machine
  Find the weak points and improve on them in time
  Achieve beam availability above 90 % (spec. is 95 %)
  Verify the LINAC4 availability modelling
  Short runs followed by repairs & optimisation  longer runs towards the end
  Regular measurement of Beam Quality (Current, emittance, T-o-F)
Routine operation from the CCC by operators
Registration of the faults with standard tool which left its marks at the LHC: Accelerator Fault Tracking

## Slide 8: Accelerator Fault Tracker
LHC Accelerator Fault Tracker (AFT) in operation from beginning of 2015 – excellent experience
“Cardiogram of LHC Operation”

## Slide 9: AFT implementation
Web interface allowing to browse, edit and analyse fault data. Collaboration between operators, system experts and availability experts.

## Slide 10: Fault editing in AFT
Recording potential fault overheads (access, RP, transport)
Link faults to their root cause (‘parent’), …
Fault Duration
Detailed Description
Fault Relations
Fault State
Additional Information

## Slide 11: Failure Analysis
Fault vs. Fault Duration

## Slide 12: Fault Classification
Predefined Fault Tree used to classify faults
Several Layers, with increasing level of detail
Possibility to make visible to OP only some layers of the Fault Tree to facilitate data-capture
System experts can then refine fault classification
LINAC4:
Fault Classification = Faults in the LINAC4 availability study

## Slide 13: Goal of the Linac4 Availability Study
Predict the expected availability / future operation
Refine and validate models with the Reliability Run data
Provide guidelines for Linac4 performance improvement
Contribute to better understanding of MYRRHA availability

## Slide 14: Gathering data for the Availability Model
Hardware description
Failure modes
Failure data
Repair / Maintenance assumptions
Simulation parameters
  Linac4 availability model
Assumptions and simulation parameters
Failure mode analysis

## Slide 15: Gathering Data for Availability Models
FAILURE MODE ANALYSIS
Failure catalogue based on
  Outcome of meetings with
  system experts
  Failure data from Linac2
Identification of system failure modes
Quantification of failure effects (mainly in terms of downtime)
Continuously updated (Started in 2012 and followed-up in the commissioning)
Link information with SNS Failure Catalogue (Empresarios Agrupados)
Development of a common database for MYRRHA (CERN + EA)

## Slide 16
Gathering data for the Availability Model
  ASSUMPTIONS AND SIMULATION PARAMETERS
  Simulation period: 1 year (operation 24/7)
  Components failure behaviour follow an exponential distribution
  Maintenance/repairs:
    Only repairs when the system is down due to components failures
    Repairs of different systems can be done simultaneously
    All repairs must finished before restarting the Linac
  The system is down after failure -> No components failure during repair

## Slide 17: Availability Model Implementation in Isograph®
Linac4 failure behaviour modelled by Reliability Block diagrams in Isograph®
Each block can be assigned a failure mode…
  Failure distribution
  MTTF
  Consequences
…and a maintenance strategy

## Slide 18
Linac4 Availability model results
Chart: ELMAS
Availability | Mean down time | Failures | Mean time to repair (MTTR) | Mean Time to Fail (MTTF)
96% | 14 d 18.5 h / 1 year | 97 | 3.64h | 3 d 18 h
Chart: 
Up
Down
Operation
Failure / Downtime

## Slide 19
Focus: Top Contributors to Downtime/Failures
Failure Root Causes
t
Failure Downtime
Which system failure contributed more to Linac4 downtime?
Which system failure caused the Linac4 to fail?

## Slide 20
Simulation results: Contributors to Linac Downtime
Which component contributed more to repair time (DT) after system failure?
  H- Source 44%
  RF System 37%
  Dump 6%
  MEBT 5%
Chart: 
| Source | RF System | Dump | MEBT | Electro Magnets | Vacuum System | Accelerator Controls | LEBT | Technical Network | Machine Interlocks | Beam Instrumentation
 | 157.7196 | 130.5502 | 21.8134 | 17.288 | 10.0885 | 9.9917 | 2.2865 | 2.0126 | 1.8133 | 0.77402 | 0.13667
TOTAL DOWNTIME: 14 days 18.5 h / 1 year
Notes: Important: stress that this is from the simulations … hopefully in one year we have a graph with data
Mention DUMP , why contributes to downtime?

## Slide 21
Chart: 
| Source | RF System | Dump | MEBT | Electro Magnets | Vacuum System | Accelerator Controls | LEBT | Technical services | Machine Interlocks | Beam Instrumentation
 | 17.841 | 46.042 | 0.138 | 6.679 | 9.563 | 2.297 | 6.498 | 0.711 | 6.522 | 0.691 | 0.261
Simulation results: Contributors to Linac Failures
Which component caused the system to go down?
  RF System 47%
  Source 18%
  Electro Magnets 10%
  MEBT 7%
  Technical Services 7%
  Accelerator Controls 7%
NO. OF FAILURES: 97

## Slide 22
Linac4 Availability model results
Chart: ELMAS
Linac4 availability estimations | 
Availability | 96 %
No. of failures | 97
Mean Down time | 14 d 18.5 h / 1 year
MTTR | 3.64h
Mean Available time | 3 d 18 h
Downtime | Failures
H- Source ( 44%) | RF System ( 21%)
RF System ( 37%) | H-Source ( 20%)
Dump ( 6%) | Electro Magnets ( 13%)
MEBT ( 5%) | MEBT ( 7%)
Electro Magnets ( 3%) | Technical Services ( 7%)
Vacuum System ( 3%) | Accelerator Controls ( 7%)
Accelerator Controls( 1%) | Vacuum System ( 2%)
LEBT ( 1%) | Machine Interlocks ( 1%)
Important for Linac4
Important for MYRRHA

## Slide 23: Gathering data for Availability Models
Hardware description
Failure modes
Failure data
Repair / Maintenance assumptions
Simulation parameters
Common
input format
Common
input format
Common
input format
Common
input format
  Set of tables that fully define the availability model
  Linac4 availability model

## Slide 24: Gathering data for Availability Models
Merge all the relevant information to define the MYRRHA Availability Model (CERN + EA)
CONCEPT OF THE COMMON INPUT FORMAT

## Slide 25: Gathering data for Availability Models
  FEEDBACK FROM EA ON THE COMMON INPUT FORMAT
  Well elaborated, provides complete information about the Linac4 system reliability/maintainability.
  Some misleading terminology: Some concepts need to be reviewed.
  Some of the attributes will not be relevant for MYRRHA
  Overall, good format to define the MYRRHA model and inputs

## Slide 26: Next steps CERN + EA
Under study…
Application and extension of Linac4 data in the common failures database (Failure Catalogue) and the common input format to MYRRHA
For 2017…
Refine and validate the Linac4 availability model with the Reliability Run data
Provide guidelines for Linac4 performance improvement
For 2018…
Evaluate applicability of Linac4 enhancement conclusion to MYRRHA in consideration of the previous recommendation of D4.4 (MAX) reliability report.

## Slide 27: Summary
LINAC4 reached nominal energy, tests of PSB injection system
Reliability Run to start summer 2017
Fault Tracking ready to be deployed
Detailed availability modelling LINAC4 done
  Simulations seem to show a realistic prediction, to be proven with the RR
  Synchronisation of failure catalogue and Fault Tracking
Collaboration between CERN and EA on modelling
  Development of common input format to compare tools
  LINAC4 Reliability Run results to be folded into Myrrha model

## Slide 28: THANKS A LOT FOR YOUR ATTENTION!