## Slide 2: FCT and CERN Portuguese Trainee Programme Report
Claudia Dias
CERN, Technology Department
Vacuum, Surfaces and Coatings Group
Interlocks Controls Monitoring
| 31st March, 2017
FCT and CERN Portuguese Trainee Programme Report

## Slide 3: Resume
Vacuum at CERN – Overview
Vacuum Control SCADA System – Developments
Vacuum Equipment Labelling – Campaign
Vacuum Monitoring Application – Development
Training Competences
| 31st March, 2017

## Slide 4: Vacuum at CERN – Overview
| 31st March, 2017
Beam and Insulation vacuum systems
> 128km of vacuum chambers across all accelerators
Pressure range from 10-4 to 10-11 mbar achieved by:
  ~3000 vacuum pumps
  ~3000 vacuum gauges
  ~500 sector valves
How to supervise and control such a large system?
  7 SCADA servers
  ~300 PLCs
  Backboned by vacuum-specific software frameworks
Field
Control
Supervision

## Slide 5: Vacuum Control SCADA System – Developments
| 31st March, 2017
Valve Monitoring panel
  Real-time and continued valve fatigue follow-up
  Archiving of valve behaviour main parameters
  User notification features (system warnings, errors)

## Slide 6: Vacuum Control SCADA System – Developments
| 31st March, 2017
Valve Monitoring panel
  Real-time and continued valve fatigue follow-up
  Archiving of valve behaviour main parameters
  User notification features (system warnings, errors)
Vacuum devices Help panels
  Real-time device state description
  Emulation of any device state, and description
LHC Sector Valves
Penning Gauges
Ion Pumps
Pirani Gauges

## Slide 7: Vacuum Control SCADA System – Developments
| 31st March, 2017
Valve Monitoring panel
  Real-time and continued valve fatigue follow-up
  Archiving of valve behaviour main parameters
  User notification features (system warnings, errors)
Vacuum devices Help panels
  Real-time device state description
  Emulation of any device state, and description
Beam Line name tags
  Automatic and user-defined beam line identification on synoptic

## Slide 8: Vacuum Control SCADA System – Developments
| 31st March, 2017
Valve Monitoring panel
  Real-time and continued valve fatigue follow-up
  Archiving of valve behaviour main parameters
  User notification features (system warnings, errors)
Vacuum devices Help panels
  Real-time device state description
  Emulation of any device state, and description
Beam Line name tags
  Automatic and user-defined beam line identification on synoptic
Vacuum Sector selectable by user (on work)
  Sector lines can be right-clicked
  Sector status can be set, affecting its synoptic representation
  Integration with assets management

## Slide 9: Vacuum Equipment Labelling – Campaign
| 31st March, 2017
Quality developments on assets management
  Vacuum equipment name standardization
  Integration with global asset management tools
Applying to all the vacuum devices and monitoring hardware
The complete VSC-ICM team involved
>2000 labels printed and scanned

## Slide 10: Vacuum Monitoring Application – Development
| 31st March, 2017
Monitoring webpage
  SCADA synoptic for the main accelerators
  Beam status
  Vacuum devices status
  External operational panels
  Main user: Vacuum Monitoring Operator
  Displayed in the CERN Control Center (CCC) and around the Vacuum building
  http://vacmon.web.cern.ch
Improvements:
  Interactivity with user
  New web development technologies
  Enhance maintenance
  Boost the development of new features
  Integration with SCADA system to provide more detailed information to the user
  Integration CERN groups databases

## Slide 11: Training Competences
Competences being acquired:
  SCADA (WinCC-OA, PVSS) development
  General programming (Java, C++, QT, VBS)
  Web Development (Java Spring)
  Databases (SQL, architecture)
  Quality assurance and management
Overall purpose:
  Vacuum Controls features extension
  Vacuum control system user-support
| 31st March, 2017

## Slide 12: Questions?
FCT and CERN Portuguese Trainee Programme Report
| 31st March, 2017